## Slide 1: A BIRD 75 Multi-lingual Example Lynne Green
IBIS Summit
January 2003

## Slide 2: Multi-Lingual Example
Simple receiver
SPICE
VHDL-AMS
Calling in IBIS 4.x File

## Slide 3: Simple Receiver
Pair of clamp diodes
Input capacitance
No package parasitics
Pin/Pad
Core

## Slide 4: Simple Receiver in SPICE
.subckt Rcvr 1 2 4 5
D1 1 2 DD
D2 5 1 DD
M1 1 3 2 2 P
M2 1 3 5 5 N
M3 3 4 2 2 P
M4 3 4 5 5 N
.model DD d Cj0 2p
.model N nmos
.model P pmos
.ends
Analog input and output
KCL and KVL at all nodes
Core
Pin/Pad
1
2
3
4
5

## Slide 5: Simple Receiver in VHDL-AMS
Library IEEE;
use IEEE.math_real.all;
use IEEE.std_logic_1164.all;
library IEEE_proposed;
use IEEE_proposed.electrical_systems.all;
use IEEE_proposed.energy_systems.all;
entity Rcvr is
generic(
TempC : real := 25.0;
cap : capacitance :=2.0e-12;
Vinh :voltage :=2.0;
Vinl : voltage :=0.8);
port (terminal v_pad, v_pwr, v_gnd : electrical;
signal core : out std_logic);
end entity Rcvr;
KCL and KVL only
at analog nodes

## Slide 6: Simple Receiver in VHDL-AMS
architecture linear of Rcvr is
constant vt : real := K*(TempC + 273.0)/Q;
constant isat : current := 1.0e-15;
constant delay1 :time :=3.5 ps;
quantity v_cap across i_cap through v_pad to v_gnd;
quantity v_gc across i_gc through v_gnd to v_pad;
quantity v_pc across i_pc through v_pad to v_pwr;
begin

## Slide 7: Simple Receiver in VHDL-AMS
process (v_cap'above(Vinh), V_cap'above(Vinl)) is
begin
if v_cap'above(Vinh) then
core <= '1' after delay1;
elsif not v_cap'above(Vinl) then
core <= '0' after delay1;
else
core <= 'X' after delay1;
end if;
end process;
i_cap==cap*v_cap'dot;
i_gc == isat*(exp(v_gc/vt) - 1.0);
i_pc == isat*(exp(v_pc/vt) - 1.0);
end architecture linear;

## Slide 8: Calling the External Model
| +----------+
| D_enable--- | |---A_puref
| ||\ |---A_pcref
| D_drive---- || >----+--|--A_signal
| ||/ /| | |---A_gcref
| D_receive-- | < |--+ |---A_pdref
| | \| |---A_gnd
| | |---A_extref
| +---------+

## Slide 9: Calling the SPICE Model
[Model] ExBufferSPICE
Model_type Input
Vinh = 2.0
Vinl = 0.8
[Voltage Range] 3.3 3.0 3.6
|
[External Model]
Language SPICE
Corner Typ rcvr_typ.spi Rcvr
Corner Min rcvr_min.spi Rcvr
Corner Max rcvr_max.spi Rcvr

## Slide 10: Calling the SPICE Model
| List of pin/port names
| in same order as in SPICE
Ports A_signal A_puref core A_pdref
|
| Convert analog core signal to digital core signal
| A_to_D d_port port1 port2 vlow vhigh corner_name
A_to_D D_receive core A_pdref 0.8 2.0 Typ
|
[End External Model]

## Slide 11: Calling the VHDL-AMS Model
[Model] ExBufferAMS
Model_type Input
Vinh = 2.0
Vinl = 0.8
[Voltage Range] 3.3 3.0 3.6
|
[External Model]
Language VHDL-AMS
Corner Typ rcvr_typ.vhd Rcvr
Corner Min rcvr_min.vhd Rcvr
Corner Max rcvr_max.vhd Rcvr

## Slide 12: Calling the VHDL-AMS Model
| Parameters are allowed
Parameters TempC cap
|
| List of pin/port names
| in same order as in VHDL-AMS
Ports A_signal A_puref core A_pdref
|
[End External Model]