## Slide 1: Lossy Line Simulation and Analysis
Dima Smolyansky
TDA Systems, Inc.
www.tdasystems.com
Based on a paper at Printed Circuit Design Magazine, March 2003
Rev. 7/30/26

## Slide 2: Effect of Losses
Amplitude degradation
Rise time degradation
Notes: The effect of frequency dependent losses on the interconnect link performance is primarily in degradation of rise time, amplitude, and eye diagram. The rise time for the signal transmitted through a link slows down as a result of losses, and the signal amplitude decreases. The amplitude, however, does not stay at a permanently lowered level, as it would in a case of purely DC loss. In fact, it gradually creeps up towards the incident signal amplitude. However, the losses can delay the signal to the point that it effectively looks as if it never reaches that incident signal level.
The eye diagram degradation due to losses in the interconnects may result in a significantly more closed eye, with decreased eye diagram width due to rise time degradation, and decreased height due to amplitude degradation.

## Slide 3: Lossy Line Simulation Approaches
S-parameters
Parametric models
RLGC tables
Behavioral model

## Slide 4: Using S-parameters in Simulation
Tried and true approach in microwave design
  Used in linear or small-signal regime
  Skip the modeling, save the time!
SPICE just begins to support it
  Need to use in non-linear regime
  Accuracy yet unknown
Notes: Taking a clue from microwave design, the natural way to characterize and simulate losses is by using measured network parameters of the interconnect link. These network parameters can be Time Domain Reflection and Transmission (TDR/T) data or S-parameters (TDT or S21, the insertion loss and TDR or S11, the return loss) of the interconnect link. These S-parameters can be measured directly using a vector network analyzer (VNA), a time domain reflectometry oscilloscope (TDR) with IConnect® TDR software, or computed using one of the numerous electromagnetic field solver tools. In the latter case, when the S-parameters are computed numerically, their accuracy must be verified using either TDR or VNA. If the driver and receiver can be assumed to be linear, then it is a fairly straightforward task to evaluate the performance of the interconnect link using the IConnect linear interconnect link simulator. A designer can also include in the IConnect simulations the effect of the equalization and pre-emphasis, connectors and vias, IC packages and sockets that reside in the signal path.
In addition, in narrowband microwave design there are no causality issues to address, which makes it more simple than in broadband design.

## Slide 5: TDA’s Interconnect Link Simulator
Use TDR/T or S-parameter data in simulations
  Quickly predict eye diagram, jitter, losses, crosstalk, reflections, ringing
  Efficiently validate analytical and field solver models
Notes: IConnect interconnect link simulator allows exactly that – inclusion of S-parameters into the simulation directly. Even though Link Simulator is a linear simulator, and as such is not a full SPICE or IBIS simulator, and does not support active device model inclusion, Link Simulator is an efficient way to evaluate performance of the interconnect link itself, including the effects of equalization and emphasis.

## Slide 6: Parametric Models
Parametric model make specific assumptions
Example: the hailed and hollered W-element…
  Accuracy – depends on who you talk to
  Clearly, dielectric loss simulation is not perfect
Speed and efficiency – very good
Pre-defined assumptions make it easy to extract the accurate model from measurement
Notes: Parametric models utilize certain assumptions about the nature of the losses. For example, the W-element in HSpice, which has been thoroughly discussed in the industry, and has equivalents in other major SPICE simulators, assumes square root dependence of the skin effect with frequency and linear dependence of the dielectric loss with frequency.
In these equations, Rdc and Rac are the DC and high-frequency resistances of the conductor, Gd is the dielectric loss parameter related to material losses, and f is frequency.
As long as these assumptions hold, the model will be simulated accurately. One advantage of this model is that making the parametric assumptions allows the designer to extract the skin effect and dielectric loss from a single measurement, requiring no exact knowledge about the geometry or material properties that a typical electromagnetic field solver might require. For example, these losses can be extracted from TDR/T or S-parameter measurements using the lossy line extraction routine in IConnect TDR software. The extracted model is listed below, and the correlation between the measurement and the simulated data in time and frequency domains are also shown.

## Slide 7: TDA Modeling Experience with W-element
Not bad with proper treatment!
Notes: Despite the multiple (and valid) complaints about accuracy of W-element, we found that we can achieve good quality W-element models, which correlate to measurements quite well.

## Slide 8: Frequency Tables
Better accuracy than parametric
Slower simulation time
More difficult to extract accurately
Example: TDA extraction
Notes: Frequency dependent RLGC tables do not make the assumptions that a parametric model might make, but instead provide a table with RLGC values for a number of frequency points. The advantage of this approach is the increased accuracy, but the disadvantages are many. First, it typically takes longer to simulate. Second, unless the same assumptions as for parametric model are made, it is impossible to separate the frequency dependent R from G directly from measurement, making it necessary to first run a field solver analysis, and then validate it using measurements. Finally, because the simulator is sometimes forced to interpolate the frequency dependent values, which lie between the table data points, it can produce data that make the simulation unstable, violating causality, passivity and stability constraints which must be imposed on the normally causal (does not respond before the time 0), passive (does not amplify signal or generate energy), and stable (does not oscillate) interconnect link.
IConnect TDR software offers a frequency dependent RLGC table output for its lossy line model extractor. To be able to separate the series R and L components from shunt C and G components, however, IConnect is forced to make the same assumption as for its parametric model extraction method. A typical output is shown below. Note that the fact that the dielectric loss parameter G varies with frequency forces the capacitance to vary with frequency as well.

## Slide 9: Behavioral Modeling
Different algorithms are available
Can achieve exact correlation between model and measured data
Simulation tends to be slower for large interconnect structures
  Lumped element approach is the only approach where passivity can be ensured
Notes: Typical examples of behavioral modeling are Laplace element and the lumped element approximation. The Laplace element is subject to the same issues as sampled RLGC data: accuracy, stability, causality. This includes interpolation and extrapolation issues. A lumped element representation is the only one that can guarantee passivity.

## Slide 10: TDA Experience: Parametric Behavioral
Convert mathematically exact skin effect and dielectric loss into behavioral model
Notes: This example shows correlation between simulation and measurement for a Gigabit Ethernet example from Mysticom backplane. As we can see, excellent correlation can be achieved with parametric model, which then is converted into a behavioral model.

## Slide 11: TDA Experience: MeasureXtractor™
Notes: IConnect MeasureXtractor™ is an automated model extraction tool, allowing the designer to obtain an accurate measurement based model of the interconnect with no effort at all. MeasureXtractor™ will guide you through the data acquisition process, help you acquire your TDR/T or S-parameter data, and will automatically produce an accurate model that will match both the time and frequency response of your interconnect. Losses, dispersion, jitter, crosstalk, reflections and ringing are predicted accurately, up to the highest frequency of operation of your instrument. Passivity of such models is assured though TDA Systems proprietary algorithm.
MeasureXtractor™ produces what is known as a behavioral model. Such a model does not take into account the actual topology of the interconnect, but instead simply aims to accurately represent the time and frequency behavior of the interconnect in the most simulation efficient manner; in the case of IConnect MeasureXtractor™, that means with the minimum number of components, and guaranteed passivity. Nonetheless, behavioral models can result in longer simulation time, in particularly for large interconnect structures.

## Slide 12: Summary