## Slide 1: An Initial Case Study for BIRD95: Enhancing IBIS for SSO Power Integrity Simulation
SIGRITY, INC.
Sam Chitwood
Raymond Y. Chen
Jiayuan Fang

## Slide 2: Contents
Present-day IBIS vs SPICE correlation
  Limitations of IBIS based SSO simulations
Currents that IBIS can calculate
  Comparison of IBIS currents with transistor currents
BIRD95: Add parasitic currents to the IBIS model
  Parasitic current extraction methodology
  Preliminary results and observations
Suggestions for improvement
Summary

## Slide 3: Correlation of IBIS and SPICE output voltages
I/O voltage at the die; 10 pF load; no package information; ideal PDS
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue

## Slide 4: Comparison of IBIS and SPICE total VDDQ current
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue
Total VDDQ driver current; 10 pF loading; ideal PDS
The total VDDQ current for the transistor-level model is significantly different from its pullup component. There is a large amount of pre-driver current due to crowbar effects and gate capacitance charging.
Pre-driver current occurs significantly earlier than the pullup current. The pre-driver current is rapidly decreasing as the pullup is turning on.
The pre-driver current peaks almost as high as the pullup current. Note that the dI/dt of the pre-driver is much larger than that of the pullup current.
Pre-driver
Current
Low-to-high transition
Pullup
Current
High-to-low transition
Pre-driver
Current
Crowbar
Current

## Slide 5: Currents that IBIS can calculate
IBIS components
Analog Model of an IBIS output
The pullup and pulldown components are modeled as voltage controlled current sources
The instantaneous value for each voltage controlled current source is derived from the I/V tables and is scaled based on the information in the V(t) tables
The voltage controlled current sources are simultaneously active to model crowbar
Crowbar current can be approximated fairly well if all four V(t) tables are present in the IBIS file

## Slide 6: Comparison of final drive stage crowbar current
Current through the driver’s upper device; open circuit loading; ideal PDS
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue
The IBIS algorithms in HSPICE and Speed2000 include the crowbar current. The overlap of the pullup and pulldown current sources is inherent in the model and cannot be excluded.
HSPICE currents show the best correlation for the low-high transition at 1ns.
Speed2000 currents show the best correlation for the high-low transition at 5ns.

## Slide 7: Comparison of driver pullup current
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue
Driver pullup current; 10 pF loading; ideal PDS
The magnitude of the rising-edge pullup current is dominated by the I/O current that charges the load capacitor. Both IBIS algorithms show good correlation to the SPICE model for the rising edge pullup current.
The crowbar current is easily identified for the high-low transition at 5ns. Speed2000 catches the trailing edge of the crowbar current.
Crowbar
+ I/O
current
No crowbar
at this point
Crowbar
Current
Low-to-high transition
High-to-low transition

## Slide 8: Objective of BIRD95: Improve IBIS models to facilitate accurate SSO and other Power Integrity Simulations

## Slide 9: Overview of BIRD95 methodology
I_VDDQ(t)
Total VDDQ current will be measured for the transistor level model
Current versus time tables will be added to the IBIS file
The IBIS simulator will use the I_VDDQ(t) tables to include the parasitic currents from the pre-driver, I/O termination, crowbar, etc.
Note that if an ideal VDDQ supply is used, I_bypass(t) = 0 for all t.

## Slide 10: Overview of BIRD95 methodology
This IBIS simulator will include the parasitic currents by calculating the difference between the IBIS VDDQ current and I_VDDQ(t)
A current source is added in parallel with the IBIS device such that
  I(t) = I_VDDQ(t) – IBIS VDDQ current(t)
I(t)
GND
VDDQ
I_VDDQ(t)

## Slide 11: BIRD95 recommends three parasitic current extractions
BIRD95’s I_VDDQ consists of all pre-driver, final stage I/O, termination, crowbar, and other parasitic currents.
As expected, these waveforms vary significantly due to the final stage I/O currents.
The two spikes that precede each transition are due to the pre-driver current.
Unfortunately, there is no clear separation between the final stage crowbar and I/O current contributions. Is this a problem? If so, why?
50 Ω to GND
50 Ω to VDDQ
1 MΩ to GND (open circuit)

## Slide 12: Comparison of crowbar currents
Upper device current for the transistor level model; ideal PDS
10 pF load – Blue 1 MΩ (open circuit) – Green
This slide compares the final stage’s crowbar current at the high-to-low transition at 5ns. All loads are fully charged to VDDQ before the transition begins, thus the upper device current is the crowbar current.
The crowbar current of the final drive stage is dependent on the I/O loading condition. Therefore, the problem remains that IBIS simulators will have to extrapolate the crowbar current for arbitrary loading conditions that are not provided in the IBIS file.
At this point, it is unclear how this will be implemented from an algorithmic point of view, as the present-day scheme must be improved to incorporate the new data.
Crowbar
Current only
Crowbar
+ I/O
current
No crowbar
at this point
Crowbar
Current

## Slide 13: Pre-driver Current Extraction
Total VDDQ current – Blue Pullup current – Red Pre-driver current – Green
Extraction with 50 Ohms to GND loading; ideal PDS
This paper will examine the results for a 10 pF I/O loading condition, as it is different from the BIRD95 extractions.
To eliminate any double counting of crowbar current, only the pre-driver current was added to the IBIS current.
Pre-driver current =
Total VDDQ current –
final drive stage current
These currents were obtained through HSPICE transistor level simulations.
Again, note that any crowbar current in the final drive stage will be calculated by the IBIS simulator.

## Slide 14: Pre-driver Current Comparison
50 Ω to GND – Green 50 Ω to VDDQ – Blue 1 MΩ to GND – Red
All BIRD95 recommended loading conditions; ideal PDS
For this buffer model, the pre-driver currents were extremely similar for all loading conditions. This is reasonable for pre-driver circuitry that only drives the gates of the final drive stage – their loading is independent of the I/O load.
As the currents were very similar, it appears that scaling is rather unnecessary for this case. Therefore, the 50 Ω to GND pre-driver current was used in the rest of this paper’s analysis.
The BIRD95 recommendations align with the V(t) extraction methodology, which minimizes the difficulty in parasitic current extraction.

## Slide 15: Improved IBIS model with Pre-driver Current
The pre-driver current is added in parallel with the pullup/pulldown
A PWL current source was used to implement the extracted pre-driver current. It was aligned in time with the stimulus pulse.
A realistic PDS was modeled by a 2-port S parameter element
PWL
I(t)
2 port
S model
VDDQ

## Slide 16: Voltage waveforms for the new methodology
SSO waveforms with realistic PDS, 10 pF driver load, PWL I(t) in parallel with the IBIS device
The new IBIS methodology is now able to model the pre-driver and final drive stage currents. Correlation with the SPICE results is significantly improved over the IBIS-only results.
Waveforms from both IBIS simulations were very similar. No artifacts were observed.
Note that the IBIS waveforms overestimate the peak-peak SSO magnitude and occur slightly before the SPICE peaks. The cause can be found by examination of the current waveforms.
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue

## Slide 17: Current waveforms for the new methodology
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue
Total VDDQ current; 10 pF loading; realistic PDS
The PWL pre-driver current has a higher dI/dt than the realistic pre-driver current. The difference is because the PWL pre-driver current was extracted with an ideal PDS that facilitated the optimistic dI/dt.
The situation can be improved: certain parasitics of the circuit have been overlooked at this point…
Total current for the two IBIS simulations are very similar. The primary difference is in the crowbar current algorithm.

## Slide 18: What is the model missing?
Parasitic capacitance exists between all MOSFET terminals
For the I/O pin, this is modeled in IBIS by C_comp
A new compensation capacitor is needed for the power and ground parasitics to maximize SSO correlation with realistic PDS models

## Slide 19: Suggested schematic to maximize correlation
A frequency domain analysis was performed to determine the impedance between power and ground for the transistor level model
The impedance was curve fit to a series RC circuit for time domain analysis
This circuit was added in parallel to the PWL current and IBIS driver
PWL
I(t)
2 port
S model
VDDQ
Cpwr_gnd
Rpwr_gnd

## Slide 20: Voltage waveforms for the suggested improvement
SSO waveforms with realistic PDS, 10 pF driver load, PWL I(t) and RC circuit in parallel with IBIS device
The IBIS simulations now show excellent correlation with the SPICE results over the full simulation. With the addition of the RC circuit, the oscillations occur at the proper frequencies and the SSO magnitude is correct.
As before, waveforms from both IBIS simulations were similar and no artifacts
were observed.
HSPICE transistor – Red HSPICE IBIS – Green Speed2000 IBIS – Blue

## Slide 21: Summary and Observations
IBIS algorithms attempt to model the crowbar current of the final drive stage
  Correlation is dependant on load conditions; a new modeling method is definitely needed for highly accurate SSO analysis with arbitrary loading
BIRD95 shows great promise
  The parasitic current extractions are relatively easy to generate
  Pre-driver currents can be accurately modeled with this technique
  Algorithm research is needed to accurately extrapolate crowbar currents for arbitrary loads that are not explicitly included as parasitic I(t) tables
A power / ground impedance model is necessary for optimal correlation
This study only examined an HSTL buffer – additional investigations should be performed on other buffer types for verification (SSTL, PECL, etc.)
The IBIS-based SSO simulations were significantly faster than SPICE

## Slide 22: References and Acknowledgements
[1] Perivand F. Tchrani, Yuzhe Chen, Jiayuan Fang, “Extraction of Transient Behavioral Model of Digital I/O Buffers from IBIS”, 46th IEEE Electronic Components & Technology Conference, Orlando, May 28-31, 1996, pp 1009-1015.
[2] Ying Wang and Han Ngee Tan,“The Development of Analog SPICE Behavioral Model Based on IBIS Model”, Proceedings of the Ninth Great Lakes Symposium on VLSI, March 1999.
[3] Raymond Y. Chen, “Adding On-Chip Capacitance in IBIS Format for SSO Simulation”, IBIS Summit, February 2004.
[4] “HSPICE MOSFET Models” User Manual, Synopsys, September 2004.
Many thanks to Cisco Systems, Inc. for providing the SPICE and IBIS models used in this analysis and especially to Dr. Zhiping Yang for his invaluable ideas and discussions.

## Slide 23: Appendix
System-level SSO schematic
Procedure used to obtain Cpwr_gnd and Rpwr_gnd

## Slide 24: System-level SSO schematic
Cpwr_gnd
PWL
I(t)
Rpwr_gnd
2N port PDS and I/O
S parameter model
(package & board)
VDDQ
Cdie
Rdie
Cpwr_gnd
PWL
I(t)
Rpwr_gnd
Data 1
Data N-1
1
.
.
.
N
N+1
.
.
.
2N
.
.
.
Cdie and Rdie model the total
on-die capacitance.
These elements are different from the “unit cell” R and C parasitics.

## Slide 25: Procedure used to obtain Cpwr_gnd and Rpwr_gnd
Perform an AC sweep on the SPICE circuit
  Connect a voltage source across the power & ground SPICE terminals
  Sweep the voltage source over an appropriate frequency range
  Measure the current through the voltage source
  Calculate Z(f) based on this current: V(f) = I(f) x Z(f)
Fit Z(f) to an appropriate
time domain model by
inspecting Re[Z] and Im[Z]
(series R and C for this circuit)
Note that this impedance curve is for reference only. It is not the impedance that was measured in this study.