## Slide 1: Stacked Package Modeling with IBIS Version 4.1
Tom Dagostino and Bob Ross
DesignCon IBIS Summit Meeting
Santa Clara, California
January 31, 2005

## Slide 2: 58 Pin IBIS Component Problem
58 pin 2 Gbit 128M X 16 SRAM memory consisting of eight stacked 54 pin TSOP 256 Mbit X 8 SRAM ICs addressed by layer-based chip selects
3-D metal interconnect strips (vertical, on 4 sides and horizontal layer routing) produce significant degradation

## Slide 3: Photograph of Package

## Slide 4: 8 Stacked ICs, NC Pin Strips Bring Out 8 Chip-selected I/Os on 2 Pins
DQ4
DQ14
DQ4 DQ14
8
7
6
5
4
3
2
1
4 3 2 1
8 7 6 5
Q NC

## Slide 5: I/Os for Layer 8 (Red) Component and Layer 1 (Green) Component
DQ4
DQ14
DQ4 DQ14
8
7
6
5
4
3
2
1
4 3 2 1
8 7 6 5
Q NC

## Slide 6: Ver. 4.1 Multi-lingual IBIS Model
8 – 58 pin [Component]s, one per active layer
  I/Os and Inputs for that layer plus I/Os from layer +/- 4
  Other inactive layer Inputs and I/Os hard coded as Terminators (so, one signal active per pin)
  Choose [Component] for best and worst paths
240 node super-die interconnect structure to Inputs and I/O’s plus nodes to pins
  Extracted lossy, coupled interconnect structure linked by [External Circuit] to SPICE & a [Circuit Call]
Models set up as [External Circuit]s
  But with vendor SPICE-based IBIS model links

## Slide 7: Interconnect Extraction
Vendor supplied bare package for T-lines
  TDR for delays, impedances of strips
  And measured dimensions
Layout all buffers and layers in HyperLynx with T-lines and dimensions
Export lossy, coupled interconnect into HSpice formatted subcircuit

## Slide 8: IBIS Buffer Models
Single IC supplied separately and fully modeled as an independent IBIS file with [Component] and [Model]s
  I/O buffers
  Input buffers
  Package – (default package added to code for models)
Construct huge multi-lingual IBIS model file
  Passed Beta ibischk4 Version 4.1
  Eight internal layer [Component]s

## Slide 9: Results
No tool can simulate multi-lingual model
  Vendor-specific SPICE used (could have used Berkeley SPICE for interconnect)
  [External Circuit] buffers with SPICE-based IBIS calls do not work (and direct table links not legal)
  No Model_type information for automatic processing
  Cannot bring in total simulation net
HyperLynx simulation by hard coded buffer selection – cannot be used as component on larger board
  But did simulate with expected interconnect degradation in about 20 seconds per buffer

## Slide 10: Alternative Approaches
EBD
  No coupling (50% too fast), but Terminator stubs not needed
Vendor-specific psuedo board from electrical information
  Not tried because not acceptable to chip vendor
ICM
  No links to IBIS, no support and more complicated
No other vendor-specific solution worked
  [Circuit Call] to IBIS [Model] links – configuration issues
  Spice-based net with IBIS calls – syntax issues

## Slide 11: Multi-lingual Issues
Multi-lingual for interconnect and *-AMS models
  Solution for encoding IBIS models directly
  Forces *-AMS code, but limited *-AMS tool support, plus vendor-specific configuration issues
  Requires Bi-directional models with driving and receiving modes

## Slide 12: Cannot be Solved by IBIS Unless …
Direct IBIS table links to [Model] and [External Model]
  Expanded [Circuit Call] or new [Model Call]?
Some power-rail issues
  Can Input or Terminator model have inactive A_puref and A_pdref nodes? (OK in standard IBIS)
How to selectively bring in partial or full interconnect structure
  EDA tool issue
On-die chip select
  Limitation overcome by using several [Component]s