## Slide 1: Using Python to Debug IBIS-AMI Models
David Banas
IBIS Summit at DesignCon 2013
January 31, 2013
Santa Clara Convention Center

## Slide 2: Our Current Options for Debugging IBIS-AMI Models
Run a full blown, GUI based simulation in our favorite IBIS-AMI capable simulator.
  Pros
    Can use GUI to set parameters. (Don’t have to create a *.CSV file.)
    Can debug model in the same environment that your customer will use to run it.
  Cons
    A lot of overhead for debugging something simple in an iterative fashion.
    You tie up a license, which might be needed elsewhere.
Use one of the command line tools provided.
  Pros
    Quick & dirty; can run many iterations.
    No license required.
  Cons
    Need to create a *.CSV file.
    Single run mode only. (Model loads, runs, and falls out of scope.)
    No access to source code (that I’m aware of).
    And, if there is, it’s probably in C; yuk!

## Slide 3: A 3rd Alternative – PyIBIS-AMI (Python AMI testing package)
Pros
  Forget about *.CSV files.
  Use Python data structures for holding parameter values, and tweak/reinitialize in an iterative fashion.
  Keep the model in scope. (Tweak parameters and re-initialize.)
  Bring the power of Python and its libraries to bear on your debugging effort.
  Plot results, as part of your iterative debugging loop.
Cons
  Have to learn Python.
  Have to install a Python environment.
  Performance hit, relative to C.

## Slide 4: Live Demo
Importing the PyIBIS-AMI package.
Instantiating the AMIModel class.
Instantiating the AMIModelInitializer class.
Initializing the model.
Viewing the resultant impulse response.
Debugging the faulty impulse response.
  Plotting the frequency response.
  Querying the model, in response to a hypothesis.
  Tweaking the initialization data and reinitializing.
  Viewing the results and validating the hypothesis.

## Slide 5: Going Further
Applying the power of the NumPy/SciPy libraries.
  Both the model and its initialization data are first class Python objects, which means you can do anything with them that you could do with any other Python objects.
  The NumPy/SciPy library pair form a nearly complete replacement of MATLAB, including most of its numerical processing libraries! Imagine the possibilities.
Batch mode execution for automated flows.
  Test construction grammar makes use of Python embedding, via EmPy.
  Output is XML, for flexible stylizing.
GUI tool (coming soon).
  Plots will be present by default and updated automatically, when a change is made to the initialization data.

## Slide 6: FAQ
Does this have any momentum in the community?
  Yes!:
Which Python distribution do you recommend?
  http://www.enthought.com/products/epd_free.php

## Slide 7: FAQ (cont’d.)
I’m not a bit head; I know just enough C to get my model built. How can I learn just enough Python to use this tool? Check out these resources:
  Learning Python by Lutz (Published by O’Reilly).
  Python in a Nutshell by Martelli (Published by O’Reilly).
  The Wiki page for this project: https://github.com/capn-freako/PyAMI/wiki
  Udacity Python programming course: http://www.udacity.com/overview/Course/cs101/CourseRev/apr2012
  Send e-mail to ibis-atm@freelists.org. Other users of this package, including myself, might be able to offer some helpful guidance.

## Slide 8: Q&A
Questions of clarification on this presentation?
Questions on the structure of the PyIBIS-AMI package and/or how it fits into the rest of your Python installation?
Questions on getting Python installed?
Stump the Chump!
  A completely unprepared, uncanned, very dangerous, potentially embarrassing demonstration of the PyIBIS-AMI package in action… …(Wait for it)… DIRECTED BY YOU (i.e. – NOT me).
    The intent here is to offer a true demonstration of the usefulness of this package to someone, whom is just beginning to explore and debug a new model.
    Hopefully, in doing this we will flush out some of the handier features of Python and its run time command line environment.