## Slide 1: Using X-Parameters* to Generate IBIS Models
Tom Comberiate
and José Schutt-Ainé
University of Illinois
at Urbana-Champaign
tcomber2@illinois.edu
*X-Parameters is a registered trademark of Agilent Technologies.
IBIS Summit at DesignCon
January 31, 2013
Santa Clara, CA

## Slide 2: Outline
Motivation
Background
IBIS Model Construction
  X-parameter File Generation
  Simulations to Produce IBIS Model
Conclusions/Comments
Future Work

## Slide 3: Motivation
IBIS models can be difficult to generate, especially without revealing IP to the model generator.
  NC State’s s2ibis3 [1] is still the open-source standard for simulated IBIS generation [2].
X-parameters [3]:
  Are behavioral, protect IP.
  Are the mathematical superset of S parameters.
  Can describe nonlinear effects.
  Can be measured with NVNAs [4].
Would like for designers to be able to exchange .xnp files and generate IBIS models from them.

## Slide 4: Polyharmonic Distortion (PHD) Model [5]
“Black-box” behavioral model of a nonlinear component defined in the frequency domain.
Large-signal tone A11 is applied to the input.
Additional “small” harmonic frequency components respond linearly but can also contribute to each other.

## Slide 5: X-Parameters Formalism [5]
Harmonic components of scattered waves are determined by the incident waves and their conjugates.
S and T parameters are functions of frequency, fundamental magnitude, and DC bias.

## Slide 6: IBIS Model Construction
Starting point: SPICE netlist for basic inverter, Vcc = 2.5 V.
Goal: IBIS file of output model with no parasitics, clamps, or AMI [6].

## Slide 7: Rules/Guidelines
Only generating X-parameter data that could be measured with a real NVNA.
Using the IBIS Cookbook v4.0 as a guide to generate I-V and V-t curves [7].
Comparing results to those generated with s2ibis3.

## Slide 8: x2ibis Flowchart

## Slide 9: Generating X-Parameters
X-parameters generated with Harmonic Balance simulation. Need to set proper values for:
  Frequency range
  Fundamental power
  DC bias
X-parameter measurements are unidirectional because of large-signal fundamental |A11|.
Different types of X-parameter ports [8]:
Source
Load
Bias

## Slide 10: x2ibis Flowchart

## Slide 11: I-V Curve X-Parameter Generation
Bias input port to activate pull-up or pull-down network.
Sweep the output from –Vcc to 2Vcc to cover full range needed and extract current and voltage.
Approximate steady-state response with low frequency sinusoidal stimulus.

## Slide 12: x2ibis Flowchart

## Slide 13: V-t Curve X-Parameter Generation
Cookbook calls for ideal step stimuli with prescribed rise and fall times.
Approximating the ideal step with a sinusoid.
Load has Vcc V and 0 V DC biases.

## Slide 14: What We Have
2 .xnp files
1-port measurement
1 fundamental frequency (low)
11 harmonics
1 power level, 2 input bias levels
26 kB
2-port measurement
1 fundamental frequency (high)
7 harmonics
1 power level, 2 input bias levels
39 kB

## Slide 15: Simulating with X-Parameters
Can only use X-parameter data in Harmonic Balance (HB) simulations, which are steady-state (periodic).
Use scattered and incident waves to calculate voltage and current needed for IBIS tables.

## Slide 16: x2ibis Flowchart

## Slide 17: I-V Curve Calculation from X-Parameter Measurement
Apply 1-tone voltage stimulus same as for generation.
Measure input current and plot against input voltage.
Normalize voltage so curve goes through (0 V, 0 mA).

## Slide 18: I-V Curve Generation Results
x2ibis and s2ibis have excellent match

## Slide 19: x2ibis Flowchart

## Slide 20: V-t Curve Calculation from X-Parameter Measurement
Approximate a step function with a sinusoid.
Generate V-t rising and falling curves from the corresponding portions of the response to the stimulus.
Normalize beginning and end points to match I-V data.

## Slide 21: V-t Curve Generation Results
x2ibis and s2ibis have reasonable match

## Slide 22: Putting It All Together
Comparison of x2ibis and s2ibis models with PRBS stimulus:
x2ibis and s2ibis match well

## Slide 23: Conclusions/Comments
Only 2 small X-parameter files needed, <100kB.
IBIS data is generated in a seamless manner.
Ability to include second-order effects to improve accuracy.
Could include multiple frequencies in the V-t curve .xnp file to vary rise times.
Ideally, these .xnp files could be sent to model developer instead of SPICE netlist.

## Slide 24: Future Work
Improve approximation of ideal step for V-t curve generation.
Perform x2ibis on more complicated buffer circuits.
  Include parasitics, clamps, etc.
  Include equalizer blocks
Develop transient simulation techniques for use with .xnp files.
Implement BIRD releases (95 & 98)

## Slide 25: Acknowledgments
Signal Integrity Research Group at the University of Illinois at Urbana-Champaign.
  Xu Chen
Agilent Technologies, Inc. for providing the X-parameter platform.
  Loren Betts
  Steve Fulwider
  David Root
  Eric Iverson
This research was made possible with United States Government support under and awarded by DoD, Air Force Office of Scientific Research, National Defense Science and Engineering Graduate (NDSEG) Fellowship, 32 CFR 168a and through the support of the National Science Foundation.

## Slide 26: References
[1] s2ibis3 v1.1. Copyright © North Carolina State University. Last modified: March 27, 2006.
[2] C. Warwick, “What About the *.ibs File?” blog, 15 December, 2011; http://signal-integrity.tm.agilent.com/2011/what-about-the-ibs-file/.
[3] “X-Parameters Trademark Usage, Open Documentation and Partnerships,” http://www.home.agilent.com/agilent/editorial.jspx?cc=US&lc=eng&ckey=1822138&id=1822138&cmpid=zzfindeesof-x-parameters-info.
[4] Agilent Technologies, “PNA-X Nonlinear Vector Network Analyzer (NVNA),” January 2013. http://www.home.agilent.com/en/pd-1381958/pna-x-nonlinear-vector-network-analyzer-nvna-options-510-514-518-and-520.
[5] J. Verspecht and D. E. Root, “Polyharmonic Distortion Modeling,” IEEE Magazine, June 2006, pp. 44-57.
[6] The IBIS Open Forum, “I/O Buffer Information Specification Version 5.1.” Ratified August 24, 2012. IBIS homepage: http://www.eigroup.org/ibis/.
[7] The IBIS Open Forum, “IBIS Modeling Cookbook for IBIS Version 4.0,” Copyright © 2005 Government Electronics and Information Technology Association and The IBIS Open Forum.
[8] Agilent Advanced Design System, Version 2011.10 Help Notes, “X-Parameter Generator Basics ADS help notes on X-parameter ports.” Copyright © 1983-2011, Agilent Technologies.