## Slide 1: IBIS Quality Status Report
Mike LaBonte, SiSoft
Bob Ross, Teraspeed Consulting Group
IBIS Summit Meeting
January 31, 2012
DesignCon, Santa Clara, CA

## Slide 2: IBIS Quality Task Group Meetings
19 meetings in 2012
Regular Participants:
  Ericsson
  Intel
  IO Methodology
  Nokia-Siemens Networks
  SiSoft
  Teraspeed
Primary Topics:
  IQ Specification
  AMI quality
  Waveform validation
  IBIS Parser

## Slide 3: IBIS Quality Specification
Current IBIS Quality Specification version is 2.0
  http://www.eda.org/ibis/quality_ver2.0/quality_ver2_0.pdf
QUAILs (QUAlity Issue List):
  Check for Pullup/Pulldown I-V Zero-crossing for IQ2.0
  Correct usage of Open-sink
No update currently planned

## Slide 4: AMI Quality Checklist
  1.1 Parameter names in DLL same as names in AMI file
  1.6 Fully IBIS compliant analog model present
  2.4 Multiple instances of one model can run in one simulation/analysis
  2.6 Model can run multiple simultaneous simulations
  2.7 Unrecognized parameters do not cause failure
  2.8 Useful parameter Descriptions
  4.5 Information about maximum data rate delivered
  Work suspended while major IBIS AMI specification changes were in progress

## Slide 5: IBIS Correlation Test Waveform Set

## Slide 6: IBIS Accuracy Figure of Merit
FOM 94.320%
FOM 38.073%
FOM 98.307%
FOM 99.429%

## Slide 7: IBIS FOM Test Waveform Results
Waveform | IBIS FOM
Perfect | 100.000%
TimeOffset | 90.244%
DutyCycle | 95.122%
VoltageOffset | 97.500%
Amplitude | 97.988%
Dead | 59.756%
Slope | 95.122%
Inverted | 19.512%
Overshoot | 99.512%
NonMono | 99.543%
Random | 98.873%
LongFlat | 99.851%
Real_1 | 94.320%
Even a broken clock is right twice a day
… Seeking a better way to measure correlation

## Slide 8: IBIS Quality Parser BUG
IBISCHK BUG 140: Unexpected Non-Monotonic Warning Messages for Combined I-V Tables

## Slide 9: IBIS Golden Parser Document
IBISCHK user guide
  Command line usage
  1,204 Messages explained
    Error number index
    Explanation of variables
  Algorithms explained

## Slide 10: Parser source code reference
How to call the parser
Reference organized by code module
Code examples

## Slide 11: Participation Encouraged!
Meetings every other Tuesday, 8:00am PT
Web: http://eda.org/ibis/quality_wip/
  Email list:
    Web subscribe: http://www.freelists.org/list/ibis-quality/
    Or send email:
      To: ibis-quality-request@freelists.org
      Subject: subscribe