## Slide 1: Combined I-V Table Checks (BUG140)
 2013 Teraspeed Consulting Group LLC
DesignCon IBIS Summit
Santa Clara, CA, January 31, 2013
Bob Ross Yingxin Sun, Joy Li
Teraspeed Consulting Group Cadence Design Systems
bob@teraspeed.com sunyx@cadence.com
joyli@cadence.com

## Slide 2: BUG140 Issue
 2013 Teraspeed Consulting Group LLC
Unexpected Non-Monotonic Warnings for Combined I-V Tables (derived from monotonic data)
Combined I-V table checks:
  [Pulldown] + [Gnd Clamp] + [Power Clamp]
  [Pullup] + [Gnd Clamp] + [Power Clamp]
Ibischk5 parser is de facto standard for IBIS model correctness (and ibischk5 is embedded in tools)
Some companies require 0 Errors, 0 Warnings
IBIS Quality Spec, recommends 0 Errors and 0 Warnings
Warning messages create support issue for model authors or automatic modeling utility

## Slide 3: Facts
 2013 Teraspeed Consulting Group LLC
No specification REQUIREMENT that individual or combined I-V tables be monotonic
No stated method to sum mismatched voltage points (piecewise linear interpolation is allowed and used)
Specification recommends individual I-V table parser checking
Combined checks added with BUG94 (BUG92 dealt with submodels): http://www.eda.org/ibis/bugs/ibischk/
Non-monotonicity often occurs outside of normal simulation region – in clamping region and not a problem
Ibischk5 parser is operating correctly

## Slide 4: Observations
Non-monotonic behavior can occur
  Combined I-V table slope is small
  I-V table points are misaligned due to
    Offset V intervals due to Gnd, Vdd and delta V
    Different reference voltages (min/max)
    Extraction with piecewise linear interpolation calculations (if not done right)
    I-V tables have different V resolution
  Combination of above cases
 2013 Teraspeed Consulting Group LLC

## Slide 5: Example: x Step 2, Offset by 1 (Red: Interpolated Value)
x y1 y2 y1-y2 = 0?
= x^2 = x^2
0 0
1 2 1 1
2 4 5 -1
3 10 9 1
4 16 17 -1
5 26 25 1
6 36
 2013 Teraspeed Consulting Group LLC
Non-monotonic due to piecewise linear interpolation on both columns

## Slide 6: x Step 0.02, Offset by 0.01 (Red: Interpolated Value)
x y1 y2 y1-y2
= x^2 = x^2
0.00 0.0000
0.01 0.0002 0.0001 0.0001
0.02 0.0004 0.0005 -0.0001
0.03 0.0010 0.0009 0.0001
0.04 0.0016 0.0017 -0.0001
0.05 0.0026 0.0025 0.0001
0.06 0.0036
 2013 Teraspeed Consulting Group LLC
Still non-monotonic with higher resolution data

## Slide 7: x Steps 0.02 and 0.01, 0.00 Offset (Red: Interpolated Value)
x y1 y2 y1-y2
= x^2 = x^2
0.00 0.0000 0.0000 0.0000
0.01 0.0002 0.0001 0.0001
0.02 0.0004 0.0004 0.0000
0.03 0.0010 0.0009 0.0001
0.04 0.0016 0.0016 0.0000
0.05 0.0026 0.0025 0.0001
0.06 0.0036 0.0036 0.0000
 2013 Teraspeed Consulting Group LLC
Different resolution data causes non-monotonic combination

## Slide 8: Real Data from BUG140 and Cadence Presentation
“Golden Parser Non-monotonic Warning’s Investigation” by Yingxin Sun and Joy Li, Cadence Design Systems, November 9, 2012: http://tinyurl.com/byqu7yn
Presented at IBIS Quality Committee November 27, 2012
BUG140: http://www.eda.org/ibis/bugs/ibischk/
(In all test cases, the [Gnd Clamp] data is 0.0 in the region of interest)
 2013 Teraspeed Consulting Group LLC

## Slide 9: Checking bug140a.ibs
 2013 Teraspeed Consulting Group LLC
IBISCHK5 V5.1.2
Checking bug140a.ibs for IBIS 3.2 Compatibility...
NOTE (line 39) - Pulldown Typical data is non-monotonic
NOTE (line 42) - Pulldown Minimum data is non-monotonic
NOTE (line 42) - Pulldown Maximum data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 137) - Pullup Maximum data is non-monotonic
NOTE (line 138) - Pullup Minimum data is non-monotonic
WARNING - Combined Pulldown for Model: iobuf Maximum data is non-monotonic
Errors : 0
Warnings: 1
File Passed

## Slide 10: bug140a.ibs Maximum Data (Vdd = 1.3 V)
 2013 Teraspeed Consulting Group LLC
1.8 V
1.8 V
Power Clamp
Pulldown

## Slide 11
 2012 Teraspeed Consulting Group LLC

## Slide 12
 2011 Teraspeed Consulting Group LLC

## Slide 13: Checking bug140b.ibs
 2013 Teraspeed Consulting Group LLC
IBISCHK5 V5.1.2
Checking bug140b.ibs for IBIS 4.2 Compatibility...
NOTE (line 40) - Pulldown Minimum data is non-monotonic
NOTE (line 51) - Pulldown Maximum data is non-monotonic
NOTE (line 52) - Pulldown Typical data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 146) - Pullup Maximum data is non-monotonic
NOTE (line 202) - Pullup Minimum data is non-monotonic
WARNING - Combined Pulldown for Model: model_with_warning Typical data is non-monotonic
WARNING - Combined Pulldown for Model: model_with_warning Maximum data is non-monotonic
Errors : 0
Warnings: 2
File Passed

## Slide 14: bug140b.ibs Typical Data (Vdd = 1.5V)
 2013 Teraspeed Consulting Group LLC
1.95 V
1.95 V
Power Clamp
Pulldown
Different delta V density

## Slide 15: Combined Pulldown Data with Aligned Vdd (Different Delta V’s)
 2013 Teraspeed Consulting Group LLC
1.850 2.395370e-002
1.880 2.397163e-002
1.900 2.401136e-002
1.920 2.401229e-002
1.950 2.411007e-002 <--
1.960 2.411006e-002 <--
2.000 2.432631e-002
2.040 2.472520e-002
2.050 2.489275e-002
2.080 2.539300e-002
10 nA (0.000041%) non-monotonicity

## Slide 16: Checking bug140b.ibs
 2013 Teraspeed Consulting Group LLC
IBISCHK5 V5.1.2
Checking bug140b.ibs for IBIS 4.2 Compatibility...
NOTE (line 40) - Pulldown Minimum data is non-monotonic
NOTE (line 51) - Pulldown Maximum data is non-monotonic
NOTE (line 52) - Pulldown Typical data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 146) - Pullup Maximum data is non-monotonic
NOTE (line 202) - Pullup Minimum data is non-monotonic
WARNING - Combined Pulldown for Model: model_with_warning Typical data is non-monotonic
WARNING - Combined Pulldown for Model: model_with_warning Maximum data is non-monotonic
Errors : 0
Warnings: 2
File Passed

## Slide 17: bug140b.ibs Maximum Data (Vdd = 1.58 V)
 2013 Teraspeed Consulting Group LLC
1.95 V
1.95 V
Power Clamp
Pulldown

## Slide 18
 2012 Teraspeed Consulting Group LLC

## Slide 19
 2012 Teraspeed Consulting Group LLC

## Slide 20: BUG140 Resolution
Change WARNING to NOTE
  Valid solution for user
  Avoids tool and model developer support issues
Add “based on piecewise linear interpolation” to message
No practical fix
  Still issues with higher resolution or choosing percentage threshold
  Piecewise linear interpolation is legal, and spline fitting would just hide information
 2013 Teraspeed Consulting Group LLC