## Slide 1: Corner Considerations Bob Ross, Teraspeed Labs bob@teraspeedlabs.com DesignCon IBIS Summit Santa Clara, CA January 30, 2015
(Given previously November 14, 17, 20, 2014)

## Slide 2: Outline
Overview
Corner Review
Parameter Passing Corners in IBIS Version 6.0
Upcoming Interconnect Modeling Corners
Td, Zo to/from L, C Conversions
Concluding Comments

## Slide 3: Overview
Corners in this presentation mean the assignment of Typ, Min, Max (or Typ, Slow, Fast) entries
Different areas of IBIS have different corner definitions
IBIS supports passing parameter values into IBIS-ISS (an HSPICE subset) sub-circuits
The parameter descriptions can also contain corners
Purpose of this presentation is to show different methods and provide some advice

## Slide 4: Corner Review
[Model] Corners
[External Model] Corners
[External Circuit] Corners
[Package] Corners
IBIS-AMI Corners

## Slide 5: [Model] Corners
Typ: Typical process and conditions
Min: Slow, Weak process and conditions (low voltage and high temperature for CMOS)
Max: Fast, Strong process and conditions (high voltage and low temperature for CMOS)
[Model Spec] corners are aligned with [Model]
C_comp corners are by magnitude and represent the range of values
[External Model] Corner lines track [Model] corners (shown next)

## Slide 6: [External Model] Corners
[External Model] Buffer
Language IBIS-ISS
|
| Corner corner_name file_name .subckt_name
Corner Typ buffer.iss typ_typ
Corner Min buffer.iss slow_min
Corner Max buffer.iss fast_max
[External Model] is under [Model]
[Model] corner selection determines which Corner line to use

## Slide 7: [External Circuit] Corners
[External Circuit] Circuit
Language IBIS-ISS
|
| Corner corner_name file_name .subckt_name
Corner Typ circuit.iss typ_typ
Corner Min circuit.iss slow_min
Corner Max circuit.iss fast_max
User or EDA tool selects Corner line:
  For buffer, set same as [Model] setting
  For on-die interconnect, Corner can be used for range of values or aligned with connected [External Circuit] buffer

## Slide 8: [Package] Corners
Default corners show range of values:
[Package] | Corners by magnitude value give range
L_pkg <Typ_val> <Min_val> <Max_val>
C_pkg <Typ_val> <Min_val> <Max_val>
R_pkg <Typ_val> <Min_val> <Max_val>
Most IBIS models have pin-specific detail that overrides [Package] setting:
  L_pin, C_pin, R_pin
  [Package Model] with [Define Package Model]

## Slide 9: IBIS-AMI Corners
AMI File, For example:
(<parameter_name> (Usage Info) (Type Float)
(Corner <Typ_val> <Slow_val> <Fast_val>))
Typ, Slow, Fast entries
Slow, Fast entries not clear for some parameters such as Zo for reference impedance
(Beyond Corners, IBIS-AMI allows these choices: List, Range, Steps, Increment, Value)
User or EDA tool makes Corner selection
Corners used for speed entry or range of values

## Slide 10: Parameter Passing Corners in IBIS Version 6.0 Note
Note, “parameter” used in several ways
  “parameter” name variable in IBIS-AMI
  “Parameter definition file” (an AMI file)
  “Parameters” line assignment for [External Model] or [External Circuit]
  “parameter” value passed into IBIS-ISS sub-circuit
  “Parameter file (a non-AMI file for storing parameter names and assignments)

## Slide 11: Parameter Passing Corners in IBIS Version 6.0
Used with [External Model] or [External Circuit]
Actual corner selections stored in an IBIS-AMI file or a separate parameter file with any extension
Parameter values passed into IBIS-ISS sub-circuits
User selects which Parameter line corner to use
Example shown next with transmission line Td (delay), Zo (reference impedance) parameters

## Slide 12: [External Circuit] with Parameters Corner
Parameters Td=<name>.ami(<root>(Model_Specific(Td)))
Parameters Zo=<name>.ami(<root>(Model_Specific(Zo)))
….
[External Circuit] Interconnect-ISS
Language IBIS-ISS
|
| Corner corner_name file_name .subckt_name
Corner Typ t-line.iss typ_typ
Corner Min t-line.iss slow_min
Corner Max t-line.iss fast_max
Assume Parameters corners used in ALL Corner lines
Td, Zo parameter values passed into the typ_typ, slow_min, fast_max sub-circuits

## Slide 13: [External Circuit] Parameters Using IBIS-AMI Example
Parameters to pass into IBIS-ISS:
Parameters Td=<name>.ami(<root>(Model_Specific(Td)))
Parameters Zo=<name>.ami(<root>(Model_Specific(Zo)))
AMI File, (Model_Specific section):
(Td (Usage Info) (Type Float)
(Corner 60e-12 66e-12 54e-12))
(Zo (Usage Info) (Type Float) (Corner 50 55 45))
(Zo corner is ambiguous – larger value is selected as slow, (weaker) corner

## Slide 14: [External Circuit] Parameter Example Comments
Not clear whether the Parameters Lines should be aligned with the Typ, Min, Max corners or used as a range of values for each of the Corner lines
Helpful solutions: use specific assignment:
  Assign parameters directly in each IBIS-ISS sub-circuit
  Or use separate parameter names; for example, Td_typ, Td_min, Td_max for individual range of values
  Or use direct parameter Value assignment
Minimize complication by minimizing user selections, where possible

## Slide 15: Upcoming Interconnect Modeling Corners
Attaches IBIS-ISS or Touchstone descriptions to buffers, die interfaces or pin interfaces
Focus here is on IBIS-ISS applications
Syntax is similar to [External Circuit] connection syntax (“File_ISS” replaces both “Corner” and “Language IBIS-ISS”)
| file_type corner_name file_name .subckt name
File_ISS Typ net.iss netlist_typ
File_ISS Min net.iss netlist_min
File_ISS Max net.iss netlist_max

## Slide 16: Param Line in Upcoming Interconnect Modeling Proposal
Supports parameter passing to IBIS-ISS (“Param” name is chosen to be distinct from the multiple meanings of the word “parameter”)
  Param <Name> <Typ> <Min> <Max>
Min: Slow, Weak (where possible)
Max: Fast, Strong (where possible)
Mixing Min, Max possible for uncorrelated ranges
All Min, All Max should be one option

## Slide 17: Adding Param Line Example:
| Param Name Typ Min Max
Param Td 60ps 66ps 54ps
Param Zo 50 55 45
|
| file_type corner_name file_name .subckt name
File_ISS Typ net.iss netlist_typ
File_ISS Min net.iss netlist_min
File_ISS Max net.iss netlist_max

## Slide 18: Interconnect Proposal Advice
Similar to [External Circuit] advice
Minimize or avoid parameter passing, where possible
Be specific with parameter corner names
Embed parameter values in sub-circuits
Otherwise, parameters might be treated as a range of values

## Slide 19: Td, Zo to/from L, C Conversions
Interconnect or package values may be extracted from TDR measurement in terms of ideal transmission line Td (delay) and Zo (reference impedance) values
These values can be used directly, or might be converted to L, C representations for package models or for parameters in Interconnect Models
L, C representation of corners give different “effective” ranges than the original Td, Zo corners

## Slide 20: Equations to Plot L versus C as a Function of Td, Zo
Transmission line to/from package transformations:
  Td = Time delay
  Zo = Reference impedance
  L = Inductance
  C = Capacitance
  Td = Sqrt(LC), Zo = Sqrt(L/C) or
  L = TdZo, C = Td/Zo  L = Td2/C, L = Zo2C

## Slide 21: L, C Min/Max Values from Example Td, Zo Corners
Chart: C (pF)
Zo = 55 W
Zo = 50 W
Zo = 45 W
Td = 66 ps
Td = 60 ps
Td = 54 ps
Td = 66 ps
Zo = 55 W
L = 3.63 nH
Td = 54 ps
Zo = 55 W
C = 0.98 pF
Td = 66 ps
Zo = 45 W
C = 1.47 pF
Td = 54 ps
Zo = 45 W
L = 2.43 nH

## Slide 22: Wider “Effective” Td, Zo Based on L, C Corners
Chart: C (pF)
Zo = 60.8 W
Zo = 55 W
Zo = 50 W
Td = 73.0 ps
Zo = 45 W
Td = 66 ps
Zo = 40.7 W
Td = 60 ps
Td = 54 ps
Td = 48.8 ps
Td = ~60 ps
Zo = 60.8 W
L = 3.63 nH
C = 0.98 pF
Td = 48.8 ps
Zo = ~50 W
L = 2.43 nH
C = 0.98 pF
Td = ~60 ps
Zo = 40.7 W
L = 2.43 nH
C = 1.47 pF
Td = 73.0 ps
Zo = ~50 W
L = 3.63 W
C = 1.47 pF

## Slide 23: Wider “Effective” Td, Zo Based on L, C Corner Analysis
|Param Name Typ Min Max | Original
Param Zo 50 55 45
Param Td 60ps 66ps 54ps
|Param Name Typ Min Max | L, C
Param L 3.00nH 3.63nH 2.43nH | parameter
Param C 1.20pF 1.47pF 0.98pF | corners
Combinations of L, C parameter do NOT give the original ranges, as shown in previous slide:
  Td range = 48.8 ps to 73.0 ps
  Zo range = 40.7 W to 60.8 W

## Slide 24: Concluding Comments
IBIS contains several methods to describe corners and to assign and pass parameters
Minimize parameter passing with corners because of different possible interpretations
EDA tool should be capable of mixing or matching Typ, Min, Max conditions
L, C corner values derived from Td, Zo corners can give different “effective” ranges