## Slide 1
Connectors, Sockets, Cables
Bob Ross
Interconnectix, Inc.
IBIS Open Forum 1/29/96

## Slide 2
Outline
Spice Models (what to look for)
Connector Model - BIRD31
Concluding Remarks

## Slide 3
Spice Connector - Single Pin
Characteristics
  Lumped - Several Sections
  Transmission Line
  Sections and Edge Rates
  Symmetry
  Pad Capacitance
  Ground Reference - Assumed Signal/Reference
Spice Subcircuit or Data Sheet Source
Must do Pin Mapping to Connector Pins

## Slide 4
Spice Models - Coupled Pins
Characteristics
  Group or Groupings
  Sections (divide by n) and Edge Rates
  Symmetry (E.g., 3 Inductor, 2 or 4 Capacitor Sections)
  Ground Reference or Implicit
  Pad Capacitance (0.5pF - 2pF)
  Section breaks, Consistency of Groupings (6 columns may just be generalization of 3 columns)
  Fins and Structure
Spice Subcircuits from Field Solvers Source Information
Caps to Maxwell Cap. Matrix, Coupling Coef to Induct. Matrix
Mapping Issue More Complicated - Physical Block Structure

## Slide 5
Spice Problems
Subcircuit May not Describe Actual Device - E.g. Fin Connections and G=0 NOT MODELED
Understand Model - Inconsistent Sections
  Inconsistent Coupling
  Coupling Across Planes
  Incomplete Mapping
  Incorrect Number of Pins
  Defined Reference vs assumed signal/ref. vs. no Ref.
Understand Actual Mapping to Physical Mapping of Groups
Set of Lumped Sections STILL an Approximation
CONCLUSION - Must Consider SPICE sections as Approximations

## Slide 6
BIRD31
General
  Field Solver Source Data
  Manufacturers Provide the Mapping and Deal with Blocks
  Manufacturers Provide the Pin Numbering
Original BIRD31
  Split the Model Into Two Sections - Explicit Symmetry
  Fill out Each Connector Instance - PCB Pins Numbers Same
  No Technical Change of IBIS - Consistent with Package
  Simulator Handles Connections
  Supports Internal Clamps and Pullups with [Model]
  Default Disconnect Structure with Split Structure

## Slide 7
Revised BIRD31
One or Two Pin Columns - Handles numbering, cross connection, and symmetry variations
Embed Cable Within Connector Model groupings
Pad Capacitance Options
Treated as Subcircuit - Simulator can do actual Pin Number to Connector Mapping - E.g. 2 Connectors to 1 Socket
Convenient, but does not support Internal Diodes and Pullups
Implied SYMMETRY of Structure based on L-C-L

## Slide 8
Concluding Comments
Spice Model As Source of Data
  Pin Centric
  MUST understand Model Details & Errors
  MUST do complete mapping
  MUST do conversion if no “Spice Processor”
BIRD31
  Connector Centric - Instance Centric
  Source Data Based
  Potential for More Detail
  Mapping to Multiboard by Simulator
  Potential for Occupied/Unoccupied Connectors/Sockets