## Slide 1: New Needs for Measurements and Parameter Passing in IBIS IBIS Open Forum, July 2006
Ian C Dodd
Architect, High Speed Tools
SDD Division

## Slide 2: Measurement Support in IBIS
Historically IBIS has supported measurement by adding new keywords
  E.g. Vinh, Vinh_ac, Vinh_dc
We are all aware of the difficulties keeping IBIS up to date to meet new measurement requirements
Alternatives to new measurement keywords include:
  Creating or adopting an IBIS measurement language
  Intelligent AMS* models that make their own measurements
    *Analog VHDL, Analog Verilog, VHDL-AMS, Verilog AMS or possibly ‘C’ language models

## Slide 3: New IBIS measurements and SI tools
Historically SI tools have supported IBIS measurements through specialized code
  Requires the SI tool to be enhanced before support for the new keyword becomes available
The alternatives to adding new IBIS measurement keywords can be complemented by enhancing SI tools to dynamically add new measurements
If each new measurement were accompanied by the following information it would allow the SI tools to deploy a user friendly interface:
  For results: keyword, description, usage, data type and valid range
  For AMS parameters: keyword, description, usage, data type and valid data entry range

## Slide 4: Hypothetical Example of a Result
Monotonicity, specified by Vt integral
  Keyword: “monotonic_vti”
  Description: “Maximum non-monotonicity”
  Usage: Constrained simulation result
  Data type: floating point number
  Valid Range: less than 0.021
  Value (from simulation): 0.17 - Violation!

## Slide 5: Hypothetical Example of an AMS Parameter
Monotonicity, specified by Vt integral
  Keyword: “monotonic_vti_max”
  Description: “Maximum non-monotonicity”
  Usage: Maximum value constraint
  Data type: floating point number
  Data Entry Valid Range: 0 to 2.0
  Default Value: 0.0
  Entered Value (from Constraint Spreadsheet): 0.021

## Slide 6: The Big Questions
Does the IBIS Open Forum wish to investigate alternatives to continuing to add measurement keywords?
Does the IBIS Open Forum wish to add to the multi-lingual extensions to support better integration with SI tools?

## Slide 7: Backup Slides

## Slide 8: IBIS Parameter Passing
Model Selector
  Supports selection of one model from a list of available models
  Popular for changing termination
  Inefficient if there are lots of values as each alternative requires a full instantiation of a model
VHDL-AMS and Verilog AMS Multi-lingual parameters
  IBIS supplies parameter names
  AMS source provides parameter name, data type and default value