## Slide 1: IBIS in the Frequency Domain
Michael Mirmak
Intel Corporation
DAC IBIS Summit 2006
July 25, 2006

## Slide 2: Agenda
Frequency Domain and Related Aspects
Area 1: Maximum Switching Frequency
Area 2: C_comp Stability
Area 3: Buffer Impedance and Passive Modeling
Area 4: Edge Rate vs. Switching Frequency
Summary

## Slide 3: Frequency Domain Analysis
SI frequency domain (FD) analysis, modeling options are increasingly popular
  Interface speeds approaching microwave region
    Microwave methods migrating into SI world
  FD analysis, popular for resonance/reflection detection, tends to be faster than time domain
  Tools, industry specifications now defining “channel-based” methods and requirements
    Serial ATA, PCI Express* loss requirements
  S-parameters for interconnects (e.g., ICM)
How well does IBIS perform in these kinds
of applications?

## Slide 4: Key Areas for IBIS and FD
Several key areas should be considered when using IBIS in FD applications
  Maximum switching frequency of the buffer
  Variability of C_comp
  Passive modeling of buffer impedance
  Edge rate vs. switching frequency distinction
All these areas must be understood and checked
to ensure IBIS is applicable.
These should be familiar to long-time users.

## Slide 5: Area 1: Maximum Switching Frequency
The maximum switching frequency for an IBIS model is:
V-t data must start and end with settled DC voltages
    Enables matching to I-V load-line intercepts
Switching buffer more slowly than V-t duration avoids “switching into an unfinished edge”
Some tools may be intelligent enough to cut V-t table data to include only transition information
Trying to “overclock” an IBIS model can lead
to unpredictable results

## Slide 6: Switching into an unfinished edge (review)
Courtesy
Arpad Muranyi,
June 2003
Ad Hoc presentation
Jump occurs with IBIS
but not with transistor model
Accuracy
compromised
at inappropriate
frequencies

## Slide 7: Issues with Switching Frequency
Not technically “in frequency domain”
    Not analyzing buffer with periodic sinusoids but…
For some interfaces, buffers may have limited ramp rates to reduce radiation
    Nearest-neighbor coupling and EMI
    e.g. memory buses with high parallelism
The maximum switching frequency is
determined by the IBIS model data.
In the long term, IBIS overclocking is a tool
equation and/or specification problem.

## Slide 8: Area 2: C_comp
Buffer capacitance is, in part, frequency-dependent
A single value for C_comp may not be universally appropriate for all applications
Can we define a limited region where a single value of C_comp is appropriate?
V
Hz
F
USB Buffer in the Frequency Domain
Slice across the
C_comp profile…

## Slide 9: Area 2: C_comp at 0.3 V
Ignoring voltage, C_comp is stable
Below 100 kHz, C_comp
is flat at 14.7 pF
A single value
is appropriate
in this range

## Slide 10: Issues with C_comp
C_comp is dependent on more than frequency
      Voltage
      Buffer state (high, low, high-impedance)
      See presentations from Giacotto, Mirmak, Muranyi
“Flat” C_comp may be effectively useless
      Based on edge rate and switching frequency (Area 4)
      e.g., USB switches at 1.5 MHz and above
This is a specification-level problem.
C_comp tables? Equations? AMS?

## Slide 11: Area 3: Buffer Impedance & Passive Modeling
Related to C_comp
C_comp is a limited expression of buffer reactance or imaginary portion of total impedance
I-V tables are the real portion of total impedance, taken at DC
Perform a FD sweep and
create a passive model to
match behavior
IBIS Equivalent Circuit
(clamps omitted)

## Slide 12: Problems with FD Passive Modeling
Recall C_comp issues
    Values of R, C change with state, voltage, frequency
    Multiple circuit model may be needed; how to transition?
Passive modeling even of RX buffers questionable
    See transistor theory: AC model and dependent sources
    Also, for TX, see A. Muranyi on gate modulation
Need new fundamental buffer circuit model for IBIS
Drain
Cdrain-body
Cgate-body
Cgate-drain
Body (Substrate)
Gate
Cgate-source
Rds
Csource-body
gmVgs
gmbVbs
Source
Common HF
circuit model
for transistors
(some resistances
omitted)

## Slide 13: Area 4: Edge Rate vs. Switching Frequency
“Maximum frequency” is a vague term
Must distinguish between switching and harmonic content
Energy spectral density (Fknee) from edge rate is a useful metric
An extreme example (alteration of USB scenario)
A 100 kHz interface with ~650 ps edge rate
V-t tables should be 5 μs or shorter in duration
BUT knee frequency ~530-770 MHz!
Switching
Spectral
Density
Rolloff
Which frequency
range is “right” for C_comp or impedance-based
model?

## Slide 14: Edge Rate and Switching
Classic example: System Management Bus (SMBus)*
    Operating frequency: 10-100 kHz
    Rise, fall time maxima between 300 - 1000 ns; no minima
    Bus capacitive load maximum per segment: 400 pF
    Slow edge rate means lumped load design rules can be used for lines up to 250” in length
      No simulations required so long as bus load limited
    What happens with a “fast” buffer (5 ns edge)?
      Interconnects over 5” in length become distributed
      Must use sim tool, plus spec becomes inappropriate
A problem for IBIS & modeling
    What load should be used for Ramp, V-t, Vmeas?
    Loads for lumped assumption good for distributed system?
Buffer design, buffer model AND specification
must be consistent with interface needs

## Slide 15: Summary
IBIS usage changes with FD analysis, increasing frequencies
  Consumers must use models appropriately
    Observe maximum edge rate, switching frequency limits
    Recognize bounds on fundamental IBIS circuit model
Model & tool makers must keep frequency in mind
  What behaviors need to be expressed?
  Are today’s keywords expressive enough? (e.g. C_comp)
  AMS: What specific equations, data sets need inclusion in model examples and templates?
Proposal: Change to complex impedance
model for buffers using AMS. Use native
IBIS for interface pass/fail criteria and
measurements.