## Slide 1: 2001(+5): A Space/Time Odyssey
Gary L. Pratt, P.E.
Product Manager
gary_pratt@mentor.com
Timing and Electrical Measurement of DDR2 Memory with IBIS 4.1 and AMS
Notes: Abstract
IBIS 4.1 and its support for IEEE 1076.1 Analog/Mixed-Signal modeling opens up limitless possibilities for improving the accuracy and efficiency of PCB Signal Integrity analysis. This paper will describe one such application of IBIS4.1/IEEE1076.1 to greatly simply the extremely complex task of electrical and timing analysis of a DDR2 interface.
Authors Biography
Gary Pratt is the manager of high speed partnerships for Mentor Graphics Corp.'s System Design division. He is a graduate of the University of Wisconsin at Madison, a member of IEEE, and a licensed professional engineer with 23 years experience in power electronics; control systems; digital image and signal processing; analog, digital and software design; and engineering management. Pratt has been an evangelist for emerging EDA technologies throughout his career.

## Slide 2: In the beginning …
There was SPICE … and it was sssslllooowww
  but nobody cared, because hey … time didn’t exist yet
Then, there was time …
  But, never quite enough
Then, there was IBIS
  and, it was good, and simple to use, and saved much precious time
Then, came new technology
  which brought a plague of new keywords across the land
Then, IBIS grew large and unwieldy
  and slow to respond to new technologies
Then, the IBIS wise-men … errrr …wise-people said
  let there be AMS
And, then there was AMS
  and it was very good
Then, the masses rejoiced & created multitudes of innovation
  some of which not even the wise-people had foretold …
Notes: The IBIS template model standard was originally created as an alternative to using slow, convergence-error-prone, non-standard SPICE models for PCB Signal Integrity analysis. While IBIS was a significant improvement over transistor-level SPICE models, the need to add to the template for each new technology caused it to often lag behind the latest technologies. For this reason, designers using the latest I/O technology have often been forced back to using SPICE transistor-level models during the years the IBIS specification was being updated and EDA vendors were enhancing their tools.
In the early part of this decade, the IBIS committee recognized the fundamental problem with the existing template approach, and shifted away from a fixed template in favor of flexible analog/mixed-signal modeling languages. This new standard is known as IBIS 4.1. The freedom and flexibility provided by of the new languages has opened the door to a number of new productivity enhancing applications, many of a which were not even anticipated by the original creators of the new standard.

## Slide 3
AMS
for
DDR2 Electrical
and
Timing Measurement
Behold …
Notes: This presentation will outline one such application of IBIS4.1-AMS. This application is used to simplify the extremely complex task of verifying the electrical and timing constraints of a CPU to DDR2 interface.

## Slide 4: DDR2 Electrical and Timing Measurement Requirements
overshoot area
absolute overshoot
slew rate
monotonicity
crossing zone
runt pulse
undershoot area
min pulse width
absolute undershoot
overshoot area
absolute overshoot
pos set runt pulse
undershoot area
pos setup tangent
absolute undershoot
pos hold tangent
neg setup tangent
neg hold tangent
neg hld runt pulse
pos derated setup
pos derated hold
neg derated setup
neg derated hold
Delta TF
pos hld runt pulse
neg set runt pulse
Notes: While certainly not meant to summarize the entire JEDEC DDR2 specification, this diagram does quickly convey the complexity and difficulty of thoroughly testing a typical CPU to DDR2 memory interface. Add to this the fact that these tests must be made on each data line individually and the task quickly becomes overwhelming. Required tests include absolute over/undershoot which tests for the never-to-exceed voltage limits, and the over/undershoot area which limits the power dissipated by clamp diodes. Slew rate is measured on both DQS and DQ which is then applied to the derating table to determine the required setup and hold time based on the rise and fall characteristics. Measuring the DQ slew rate is complicated by the requirement that the slew be based on the line with the maximum slope that originates at the AC crossing and is tangent to the measured signal. Additional tests include the crossing of the differential DQS signal within a certain voltage zone, and the requirement that DQS be monotonic within another voltage zone. Both DQS and DQ must be monitored for runt pulses, where the signal crosses the threshold but fails to reach a certain voltage before crossing back through the threshold. Finally, DQS must be checked for minimum pulse width, and the DQ must be checked for setup and hold requirements based on the slew-rate derated calculations.

## Slide 5: IBIS 4.1 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
DQS
DQ0
Msgs
*
*But, where do violation messages go?
Notes: The measurement model can be used stand-alone as a distinct device in the pre-layout editor …
The model monitors the clock and data pins, and performs the measurements as outlined on the previous slide. If a violation occurs, an appropriate message is generated. Unfortunately, the IBIS standard does not deal with standard message formats, or how to transfer the message out of the model and into the underlying tool for a consistent display to the user. This is an issue the IBIS committee may want to address.

## Slide 6: IBIS 4.1 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
DQS
DQ0
Msgs
*
*But, where do violation messages go?
IBIS 4.1 Memory Model
Notes: Or, the model could be incorporated into an IBIS 4.1 model for pre-layout analysis. This eliminates the need to add a separate instance to the pre-layout diagram.
The model monitors the clock and data pins, and performs the measurements as outlined on the previous slide. If a violation occurs, an appropriate message is generated. Unfortunately, the IBIS standard does not deal with standard message formats, or how to transfer the message out of the model and into the underlying tool for a consistent display to the user. This is an issue the IBIS committee may want to address.

## Slide 7: Measurement Model in IBIS 4.1 Functional SI
IBIS 3.2 Model
DDR2 Memory Digital HLD Model
IBIS 3.2 Model
CPU Digital HLD Model
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
IBIS 4.1 CPU Model
IBIS 4.1 Memory Model
DQS
DQ0
…
…
…
Msgs
*
*But, where do violation messages go?
Analog Simulation
Digital Simulation
Notes: Or, it can be incorporated into the post-layout IBIS 4.1 device model to allow a complete post-layout analysis. This diagram shows the model being incorporated into the DDR2 Functional SI analysis (See DesignCon 2006 IBIS Summit for more details).
Once a measurement model such as this is written and integrated into an IBIS 4.1 wrapper, it is as easy to use as any other IBIS model. In this case, the DDR2 measurement model is integrated into the IBIS 4.1 model for the DDR2 memory.
Once in IBIS 4.1 format, all that is left to the model user is to import the IBIS 4.1 model into their IBIS 4.1 compatible tool, assign the model to the memory part, and invoke the simulator. The IBIS 4.1 models take care of providing stimulus to the PCB, and measuring the resulting signals at the memory pins. All the user need do is review the resulting messages to see if there has been a violation … infinitely simpler than previous alternatives of manual inspection and interpretation.

## Slide 8: IBIS 4.1 Memory Model
*How to deal with single-clock, multiple data?
*
Notes: This is what the IBIS 4.1 file looks like for the pre-layout DDR2 application (with the External Model section split into two columns). The first section is standard IBIS syntax. There is no difference between this and any other IBIS model. The center section is new to IBIS 4.1. In this section, the intermediate node names are declared, the DQS and DQ I/O models and the measurement tool in instantiated, and the measurement tool is declared. The instantiations define the connectivity within the circuit, and the declaration defines the connectivity to and the location of the measurement model source code. The last section is again standard IBIS showing the beginning of the declaration of the I/O model. Note that this example uses standard (pre-4.1) IBIS template models for the I/O.
This simple pre-layout model is easily extended to a larger model of a complete DDR2 memory device for post-layout analysis. To avoid duplicating the checking on the DQS pins, the DQS checking code could be separated into its own model using node declarations for the data interconnections between it and the DQ measurement models. In this way, the entire CPU to DDR2 interface could be checked in one simulation.
In a more traditional one-pin-at-a-time post-layout simulation, the use of this model is complicated by the fact that traditional IBIS is only designed to work with one pin at a time. It has difficulty dealing with models that require two pins (clock and data). The problem is that all the data pins are logically joined into the same circuit by way of their common clock signals. So, if a user selects one data pin to simulate, the simulator will tie in all the other data pins into the same simulation. This is an area where the IBIS specification could be enhanced.

## Slide 9: Memory Data Sheet
*How to deal with multiple speed grades?
*
Notes: This shows the first section of the measurement model AMS code containing the data for the DDR2-400 memory device. The top section contains the electrical and timing specifications and constraints. The center section describes the values for the axes of the derating table for the DQ and DQS slew rates. The derating table itself is at the bottom of the listing. The table look-up code first cycles through the axes values to determine which axis values bracket the input value. The look-up code then performs linear interpolation between the four values of the lookup table which bracket the DQ and DQS slew values. To avoid confusion with units, the units are explicitly identified in the data section, and used in the code.
Currently, the only way to tie data to the code is to either include it in the same model, or to pass it in via generic parameters. Tying it together in the same model, makes it necessary to have a separate model for each speed grade (and causes significant duplication of code). Passing the data in as generics is cumbersome and makes the code difficult to read. This is a potential area of opportunity for the enhancement of the IBIS specification.

## Slide 10
TANGENT MEASUREMENT
Wait for vref crossing
Store data points
Wait for vix_ac cross
Calculate the slope from each point to the vix_ac crossing point
Return the maximum slope
Wait for vix_dc crossing
Calculate the slope from each subsequent point back to the vix_dc crossing
Wait for vref crossing
Return the max slope
(error and exception handling removed for clarity)
*But, “ASP” isn’t an IEEE-1076.1 standard.
*
Notes: This code demonstrates how the maximum tangent line is determined. The calculation of the setup tangent line is complicated by the fact that we do not know the tangent line pivot point (the AC crossing point) until after the datapoints for the free-end of the tangent line have passed. For this reason, the free-end data points must be stored until the AC crossing occurs.
The process begins by waiting for a reference crossing. At that point, the module then stores all the analog solution points (ASPs, also known as “time-points”), until the signal crosses the AC threshold. Instantaneously after the AC crossing, the slopes of the lines from each stored point to the AC crossing point is calculated, and the maximum of these is stored. The “nominal” slope line is the line drawn directly between the reference and AC crossing. If the slope of the signal curves left of the nominal line, the nominal line will end up having the greatest slope and thus its slope will be used as the entry to the derating table. If the signal curves to the right of the nominal line, the resulting tangent line with the greatest slope will be used as the entry to the derating table.
The “Hold” tangent measurement is slightly easier, as we know the pivot point of the tangent line first, so we do not need to store any data points. This section of the process waits until the DC crossing, then calculates the slope from that crossing point to each analog solution point until the reference crossing is detected. The line with the largest slope is used as the tangent line, and used as the index into the hold derating lookup table.
Unfortunately, IEEE 1076.1 does not define a signal for analog solution points. This is left up to the simulator vendors to provide, and might not be a universally supported extension. A work-around to this is to use some fixed period sampling instead of ASPs, but this requires some knowledge of the expected time-step so that an appropriate sampling period can be chosen. Unnecessary sampling could also slightly increase the simulation time for this model. The addition of an ASP signal would be a valuable enhancement for the IEEE 1076.1 committee to provide in their next revision of the standard.

## Slide 11: Absolute and Area Over/Undershoot
Create events on crossings
Wait for a crossing into the overshoot or undershoot area
While in the over/undershoot area, integrate the area under the curve
At any time, if the maximum area is exceeded, generate an violation message
Notice: “REF” is included in each message
Error if absolute limit is exceeded
*But, how to get “REF” into the model?
*
Notes: This code excerpt shows how the DQS and DQ signals are checked for the limits of absolute and area over/undershoot. The first four lines of code generate digital signals when the DQS and DQ voltage signals pass VDD, VSS, or the absolute over/undershoot levels.
The first process waits for the digital signal indicating the DQS or DQ signal has passed into the overshoot area, and then integrates the area until either the area specification is exceeded, or the signal passes out of the over/undershoot area. If the signal exceeds the allowable over/undershoot volt-seconds, then the model outputs an error message identifying the violation, along with the reference-designator/pin-number of the offending signal.
The second process outputs an error message immediately if either the absolute overshoot or undershoot is exceeded.
Unfortunately, the IBIS 4.1 specification does not provide any way for a model to know the reference designator, or the individual pin number of the device to which it is associated. This is not a problem for a pre-layout analysis with a single DDR2 data trace, but can make it difficult to determine where a problem occurred in an interface utilizing multiple devices each with multiple pins. Fortunately, the SI simulator has this information and can easily pass it to the model. Standardizing how this is done would be a valuable enhancement to the IBIS specification.

## Slide 12: Setup Violation Check
Trigger the process after each DQS slope is determined (VIXACMAX-0.50*VDDQ)
Read and interpolate the derating chart according to DQ and DQS slew rate
If DQ is in transition (setup_time=0), report a violation
If derating is valid, check the setup time
If actual setup time is less than derated setup specification, report violation
(error and exception handling removed for clarity)
Notes: This section of the code uses the information from the tangent measurement module to perform the actual setup check. In a digital simulator, the setup time would be checked immediately upon the zero crossing of the DQS signal. But, keep in mind that when considering both electrical and timing characteristics, the timing can not be checked until after the slope of the DQS is determined. And, the slope of the DQS can not be determined until after the DQS passes the vixacmax-Vddq/2 point (which is well after the actual zero crossing).
So, this process is triggered when there is a transaction on dqs_slope (which occurs at the vixacmax-Vddq/2 crossing). The process then passes the current DQS and DQ slope information to the derating interpolation table function which returns the derating value. SETUP is passed to the function to indicate we want the setup derating value returned, and REF is passed so that the lookup table can output meaningful error messages if the slopes are outside of valid axes values, or the table entry is a dash.
The DQ tangent line measurement code sets the DQ setup_time signal to 0.0 when the DQ is between ref and AC. If a DQS crossing occurs when the DQ is undefined such as this, a setup violation is reported. If not, and the derating value is valid, the process then applies the derating value to the base value and compares that to the absolute time between the DQS zero crossing and the DQ AC crossing times. If the derated requirement is not met, an appropriate violation is reported.

## Slide 13: Timing Analysis with IBIS 3.2 Models (adjusting pin-to-pin specs to die-to-die timing)
tQSQ – Δt4
DDR2 Memory Digital HLD Model
PCB
DQS
DQ0
Analog Simulation
Digital Simulation
tQSQ + (Δt1–Δt4)
IBIS 3.2 Model Δt1
IBIS 3.2 Model Δt4
IBIS 3.2 Model Δt2
IBIS 3.2 Model Δt3
Adjustments to Digital Output Timing:
tDS(actual) = tDS(spec) + (Δt2-Δt3)
tDH(actual) = tDH(spec) + (Δt3-Δt2)
tQSQ(actual) = tQSQ(spec) + (Δt1-Δt4)
Adjustments to Digital Input Timing:
Rising and falling Δt Measured with databook load for each process corner.
*Can Δt be made standard between models and tool vendors?
Notes: Certain precautions must be taken when using HDL code to analyze timing in an IBIS environment. The problem stems from the fact that timing values are specified from the pins of the device, where the HDL code actually represents the die of the device. So, any delays or timing measurements in the HDL code must be modified by the delay through the IBIS I/O table models. In the case of a data write, if the delay through the IBIS table-models are all the same, no modification to the HDL timing is required. But, if they are different, the propagation and timing specs need to be adjusted accordingly. If the delays could be made standard between models and EDA vendors, this would greatly simplify the adjustment effort.
If the source has a maximum and minimum propagation delay, the deviation must be subtracted from the setup and added to the hold requirements at the destination.

## Slide 14: Timing Analysis with IBIS 3.2 Models (compensating for delay in IBIS 3.2-models)
Clock
Printed Circuit Board
tPCQ (actual) = tPCQ(spec) - (Δt1+Δt4)
tSU(actual) = tSU(spec) + (Δt3-Δt2)
tH(actual) = tH(spec) + (Δt2-Δt3)
Adjustments to Setup and Hold:
Adjustments to Propagation Delay:
D
Q
D
Q
IBIS 3.2 Model Δt1
IBIS 3.2 Model Δt2
IBIS 3.2 Model Δt3
IBIS 3.2 Model Δt4
IBIS 3.2 Model
*Can Δt be made standard between models and tool vendors?
Notes: However, in the more general case adjustments must be made to the propagation delays and timing limits of both the source and destination devices. If the time delays between the IBIS models could be made standard, the timing adjustments could also be standard. This appears to be another opportunity for the IBIS committee to enhance interoperability through its standard-setting function.

## Slide 15: Timing Analysis with IBIS 3.2 Models
IBIS 3.2 Model
IBIS 3.2 Model
Printed Circuit Board
IBIS 3.2 Model
IBIS 3.2 Model
DQS
DQ0
DDR2 Measurement Model
No adjustment needed when measuring at pins
Notes: Fortunately, in this example, the delay through the IBIS table-models is not a factor, because the measurement tool is not inside the HDL code. In this example the measurement model is a separate module that is connected directly to the pins of the device. So, in this case the measurement model is already measuring the timing from pin to pin, so no adjustments are required (assuming the Clock and Data timing is correct at the pins of the originating device).

## Slide 16: Trace Routing Budget
IBIS 3.2 Model
IBIS 3.2 Model
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
IBIS 4.1 Memory Model
DQS
DQ0
Timing Slack Data
*But, how to get slack data into layout tool?
*
*What slew value to use?
Notes: The timing measurement model can also be used to generate routing constraints by modifying the model to output slack time instead of violation messages, and to run a simulation with the CPU connected directly to the memory (with no intervening PCB). These slack numbers, along with signal speed information derived from the PCB stackup, can be used to provide trace length limits to a PCB layout tool.
The one complicating factor here is there is no standard for providing the slack timing data to the layout tool. Likewise, there is no standard for how the tool consolidates data from multiple measurement models to provide a clear and consistent interface to the user or downstream EDA tools. This is another opportunity for the IBIS committee to set the standard.
Another complication is the fact that the actual slew value will not be known until the trace is placed. But, the trace can not be placed until its length constraint is known. And, the length can not be known until the timing requirements are known, and the timing requirement can not be known until the slew-rate is known. A great exercise in circular logic. The only solution I see is to assume worst-case slew.

## Slide 17: IBIS 4.1 and IEEE 1076.1
Global -- Open Industry Standard
  Portable between IBIS4.1-1076.1 simulators
Complete Automation
  No user intervention required
  violation messages pinpoint problems
Tests all connections in one simulation
  All 180 cpu→mem and 128 mem→cpu nets in one step
Modeling Engineer is in complete control
  No need to involve the IBIS committee or EDA vendors to add new functions or features
Notes: In summary, not only is IBIS-4.1/AMS great for modeling of advanced I/O devices, its also great for making complex timing and electrical measurements. This is the only measurement technique that complies with an open global industry standard. These models will be portable from any EDA tool that supports this open standard. This technique also has the benefit that it removes the measurement burden from the user. These measurements are made completely by the EDA tool, thus making the SI engineer’s efforts significantly more efficient, while also significantly reducing the chance for error. In addition, this application can be extended to perform electrical and timing testing on all the CPU/RAM interconnections in a single simulation.
Perhaps the greatest advantage of IBIS4.1-AMS is the flexibility it provides to the SI engineer. The SI engineer is no longer constrained to the features and functions provide them by the IBIS committee and the SI tool vendor. They are now free to implement any functionality that is required for their task at hand. With the freedom and flexibility provided by IBIS4.1-AMS, the potential applications are limited only by the imagination.

## Slide 18: Future Applications
Automated PCI Express Test Suite?
????

## Slide 19: Next Steps
EDA Vendors
  Support IBIS 4.1 AMS
Silicon Vendors
  Develop and Release IBIS 4.1 AMS models
PCB Engineers
  Demand the benefits of IBIS 4.1 AMS
    Accept no substitutes
IBIS Committee
  Stay tuned for Ian’s presentation

## Slide 20: Thanks to
Randy Wolfe and his associates at Micron for advice on interpreting the JEDEC DDR2 specification and moral support in developing this measurement model.
Todd Westerhoff for help using IBIS 3.2 models in timing analysis.