## Slide 1: Buffers for Advanced SPICE to IBIS Testing
Bob Ross
IBIS Summit Meeting
Design Automation Conference 2006
San Francisco, California
July 25, 2006

## Slide 2: Configurable CMOS & ECL Buffers
Two buffers for all Model_types, voltages, clamps and on-die terminators (ODTs)
Berkeley SPICE to support all SPICEs
  Level 2 CMOS, standard bipolar ECL & simple diodes
  Numerical nodes
  Syntax-neutral multiplier switched conductance
    GPDSW 30 31 POLY(2) (30,31) (21,0) 0 0 0 0 1000
    RPDSW 30 31 1G
      Open: R = 1 G
      Closed: G = 1000 S (0.001 )
  Externally set 0 and 1 voltage assignments
    Could be parameterized
Multiple cases through s2ibis and scripts

## Slide 3: CMOS Buffer
* EN 3 14 PC_REF
* V ^
* PU_REF 12 | |
* ^ | +---+---+
* | | | |
* +-----+-----+ | DPC RPC
* | | | | |
* |--+ |--+ | 34 + + 36
* +--o| M2 +--o| M4 | | |
* | |--+ | |--+--PUSW | PCSW PCRSW
* | | | 32 | | | |
* IN 2 >--+ 10 +----+ 30 +---ENSW---+-------+------<> 1 I/O
* | | | 31 | | |
* | |--+ | |--+--PDSW GCSW GCRSW
* +---| M1 +---| M3 | |
* |--+ |--+ 33 + + 35
* | | | |
* +-----+-----+ DGC RGC
* | | |
* V +---+---+
* PD_REF 11 |
* V
* 13 GC_REF
Diode Clamps, 50 ODTs and confiturations switches
Enable and Model_type configuration switches

## Slide 4: CMOS Configuration Controls .SUBCKT CMOSTEST
*****************************************************************************
* ON-OFF CONFIGURATION SWITCHES
* (1 OR ABOVE = ON, 0 = OFF)
*
* VPD 1 PULLDOWN
* VPU 1 PULLUP
* VGC 1 GND CLAMP
* VPC 1 POWER CLAMP
* VGCR 0 INTERNAL GND CLAMP RESISTOR (50 ohm)
* VPCR 0 INTERNAL POWER CLAMP RESISTOR (50 ohm)
*
* VPD VPU VEN = 1 VEN = 1,0 VEN = 0
* 1 1 Output 3-state, I/O Input, Terminator
* 1 0 Open_drain I/O_open_drain Input, Terminator
* 0 1 Open_source I/O_open_source Input, Terminator
* X X Input, Terminator
*
*****************************************************************************
*
* Control Voltage Configuration
* I/O Inputs References Switches (1 = ON)
* --- -------- ----------- -------------------
.SUBCKT CMOSTEST 1 2 3 11 12 13 14 21 22 23 24 25 26
* I/O IN EN PD PU GC PC PD PU GC PC GCR PCR
*
*****************************************************************************
Diode Clamps and 50  ODTs
Model_type plus Enable Control
Enable with Model_type
I/O, Input and Enable
Voltage Refs
Model_type, Clamps and ODT Config.

## Slide 5: Switches (Berkeley SPICE)
* CONFIGURATION CONTROL SWITCHES---|
* |
* Pulldown and Pullup V
GPDSW 30 31 POLY(2) (30,31) (21,0) 0 0 0 0 1000
RPDSW 30 31 1G
GPUSW 32 30 POLY(2) (32,30) (22,0) 0 0 0 0 1000
RPUSW 32 30 1G
* Gnd Clamp and Power Clamp
GGCSW 1 33 POLY(2) (1,33) (23,0) 0 0 0 0 1000
RGCSW 1 33 1G
GPCSW 34 1 POLY(2) (34,1) (24,0) 0 0 0 0 1000
RPCSW 34 1 1G
* Gnd Clamp Resistor and Power Clamp Resistor
GGCRSW 1 35 POLY(2) (1,35) (25,0) 0 0 0 0 1000
RGCRSW 1 35 1G
GPCRSW 36 1 POLY(2) (36,1) (26,0) 0 0 0 0 1000
RPCRSW 36 1 1G
* Enable
GENSW 30 1 POLY(2) (30,1) (3,0) 0 0 0 0 1000
RENSW 30 1 1G
*****************************************************************************
*
* Control Voltage Configuration
* I/O Inputs References Switches (1 = ON)
* --- -------- ----------- -------------------
.SUBCKT CMOSTEST 1 2 3 11 12 13 14 21 22 23 24 25 26
* I/O IN EN PD PU GC PC PD PU GC PC GCR PCR
*
*****************************************************************************

## Slide 6: [Pulldown]s for Several Model_types
Power and Gnd Clamps
OD
I/O
Output
Output
I/O and OD
Extra substrate diode in PMOS for I/O and Output versus Open_drain (OD)

## Slide 7: Diode and ODT – Test I-V Processing and SPICE to IBIS Methods
[Power Clamp] chopped at Vdd
[Gnd Clamp] chopped at Vdd
Vdd
Total I-V
[Power Clamp]
[Gnd Clamp]
Better tables based on “DEC” (Deviate, Extrapolate, Calculate)
One method based on chopping the I-V tables

## Slide 8: Diode and ODT – Corresponding IBIS Model Plots
Chopped – can cause double counting of ODT currents in some EDA tools
“DEC” IBIS plots show extended range

## Slide 9: DEC and Some Other Choices from Ross, 9/2005 ODT Presentation
Clip and Extend 52.8 
Default DEC 94.2  and 120 
[Gnd Clamp] Shape
[Power Clamp] Shape

## Slide 10: ECL (PECL) Buffer
* PU_REF 12 EN 3 14 PC_REF
* ^ V ^ PC_REF - 2
* | | | |
* +---------+------+ | +---+---+ + 38
* | | | | | | |
* / / | | DPC RPC RTERM=50
* 550 \ 550 \ | | | | |
* / / | | + 34 + 36 + 37
* \ \ |/ | | | |
* | +----| Q3 | PCSW PCRSW RTERMSW
* | | |\ | | | |
* | | +---ENSW---+-------+-------+------<> 1 I/O
* + 8 9 + 30 | |
* |/ \| GCSW GCRSW
* IN 2 >--+---| Q1 Q2 |---+ 10 | |
* |\ 7 /| | + 33 + 35
* +----+----+ | | |
* | PU_REF DGC RGC
* (2 MA) - 1.32 | |
* | | |
* +---------------+------+-------+
* |
* V
* 13 GC_REF

## Slide 11: ECL (PECL) Configuration Control .SUBCKT ECLTEST
*****************************************************************************
* ON-OFF CONFIGURATION SWITCHES
* (1 OR ABOVE = ON, 0 = OFF)
*
* VGC 1 GND CLAMP
* VPC 1 POWER CLAMP
* VGCR 0 INTERNAL GND CLAMP RESISTOR (3K ohm)
* VPCR 0 INTERNAL POWER CLAMP RESISTOR (2K ohm)
* VTERM 0 INTERNAL 50 OHM TERMINATOR TO VCC - 2
*
* VEN = 1 VEN = 1,0 VEN = 0
* Output_ECL I/O_ECL, Input_ECL
* 3-state_ECL
*
*****************************************************************************
*
* Control Voltage Configuration
* I/O Inputs References Switches (1 = ON)
* --- -------- ---------- ---------------------
.SUBCKT ECLTEST 1 2 3 12 13 14 23 24 25 26 27
* I/O IN EN PU GC PC GC PC GCR PCR R50
* 3K 2K 50_2V
*
*****************************************************************************
Enable (ECL/PECL voltage levels require EN voltage shifts so that “0” is off)
Diode Clamps, 2 k and 3 k ODTs, and 50  Internal Terminator
I/O, Input and Enable
Voltage Refs
Clamps and ODT Configuration

## Slide 12: Extraction Tests
CMOSTEST and ECLTEST for advanced extraction testing
  All Model_type configurations
  Voltage reference settings
  Clamps and internal ODT
    Double counting
    Truncation of tables
  Differential models though subcircuit calls
  Typ-Min-Max alignment
Does any s2ibis tool consider all these cases??
  Otherwise need several passes and hand calculations
Not covered
  Submodel modes (for example: DDR2 ODT)
  Pre-emphasis - [Driver Schedule] partitioning