## Slide 1: IBIS Summary and Evolution
Bob Ross
IBIS Summit Meeting
Design Automation Conference 2006
San Francisco, California
July 25, 2006

## Slide 2: Expanded Tree (from Specification) (ross_4_2_tree.txt)
.ibs, .pkg, .ebd files
Keyword hierarchy, grouping, scoping, and subparameters
Repeated keywords and subparameters
Plus major version history for IBIS additions
Plus predefined selections
Provides a partial syntactical summary
Reduced version in IBIS Version 4.2 specificaton

## Slide 3: IBIS Evolution (ross_4_2_evol.pdf)
Overlaps, reformats tree
“Layering” columns of IBIS from Version 1.1 through 4.2 shows functional evolution
Top-level groupings for keywords
Highlights significant [* Spec] subparameters and *_type selections – a key aspect of IBIS
Evolution of all other subparameters
Most predefined selections in tree not shown
Other notable changes given

## Slide 4: IBIS Organization and Consistencies
Same header for .ibs, .pkg, .ebd
Groupings
  Information and Specification (header and throughout)
  Pinout (under Component)
  Package (under Component and Package)
  Model (and submodel)
  Electrical Board Description
Local section or grouping consistencies and rules for functionality groupings (e.g., multi-lingual section, series elements, test loads)
Functionality sometimes touches several areas

## Slide 5: Name, Functional Consistencies
Pin keywords (with [* Pin *] – lower case subparameters as (sometimes optional) column headings (except R_pin, L_pin, C_pin), and usually list pin numbers
Package keywords [* Package *] or under R_pin, L_pin, C_pin columns
All other subparameter names start with upper-case (except dV/dt_r and dV/dt_f)
R*, L*, C* for passive elements, usually V* for voltage
Common names or strings re-used (e.g., POWER, GND, Pullup, Pulldown, ext_ref, ref, etc.)
But always a few exceptions

## Slide 6: Many Consistencies Not Shown
Typ-min-max rules (by magnitude or P/V/T)
Several keyword and subparameter formats
Subparameters positioned before scoped keywords or tables
Very few keyword ordering rules at top-level or within keyword scoping
Single numerical subparameter “=“ rule, otherwise white space
Number system, base units, multipliers
Typ always required
Many more consistencies and also specific exceptions

## Slide 7: Expansion Syntax Options
Remain consistent (at least locally)
  Keyword or Subparameter choice?
  Format style?
  Name options?
Consistency simplifies rules and understanding and promotes adoption

## Slide 8: Closing
Documents summarize IBIS and its evolution leading to 150 pages
Shows name and structural consistency and interactions
(ICM separate document – syntax departures block IBIS merger)
Version 5.x (column) layer and tree expansion
  Link IBIS and ICM, EMC rules, power delivery, more multi-lingual refinements, more specs., etc.
  More layering and blending