## Slide 1: A Standards-based Approach to IP Protection for HDLs
  John Shields
  Staff Engineer, Modelsim

## Slide 2: Overview
Introduction
A Brief Status
First Look at The Flow
Encryption Technology Concepts
Key Management
Second Look at the Flow
Examples of the Protect Directives
A Few Missing Details
Recommendations for EDA Tool and IP Providers

## Slide 3: IP Protection Goals
Deliver HDL-based IP to potential customers you do not completely trust
Fast turnaround from design to delivery
Low cost to protect
Make money while protecting your investment

## Slide 4: Some Approaches to IP Protection
Brick and Mortar Isolation - the Design Center
Trusting the Customer - Contractual Protection
Equivalent Models - an abstraction
They all involve compromise in cost, quality, lead time, or effectiveness!
Encryption – a lossless transformation rendering IP unreadable
Caution: poor implementation could give false hope

## Slide 5: Verilog And VHDL Have Developed A Standard For IP Protection
Based on well-known standardized methods for strong encryption, encoding, and authentication
Markup of unprotected HDL source at the token level
Flexibility to meet issues outside the standards, e.g., international legal considerations
IEEE Verilog 1364 - 2005
Accellera VHDL 2006 - pending approval 7/2006
Minor differences reflect normal syntax considerations and learning curve

## Slide 6: Steady-State Flow At IP Vendor
HDL
…protect me…
HDL
Markup with
protect
directives
Encrypt
Deliver
Repeat if business/legal need

## Slide 7: The Steady-State Flow At IP Vendor
Develop your HDL model
Markup sections of the model with encryption directives
  optionally sanitize source, obsfucate it, etc.
Encrypt the model once
  with any standards-compliant encryption tool
Deliver the IP to your customers
  directly, in a design kit, via a 3rd party, …
Repeat last 3 steps if legal/business considerations dictate different encryption methodology

## Slide 8: The Customer Experience
Customer works in his shop
IP is only decrypted within the tool and just for its intended purpose
The tool is obligated not to reveal information that would compromise protected IP
The encrypted IP is otherwise virtually impossible to crack (OK, we don’t know what the NSA can do :)
Compliant
Design Tool
Runtime Data
Design

## Slide 9: Symmetric Cipher
A secret key is used to convert plaintext to ciphertext
The ciphertext can be sent over an insecure channel without concern of compromise
The same secret key must used to decrypt ciphertext back into plaintext
The secret key is delivered in some out of band communication
Secure bi-directional exchange of messages
Symmetric ciphers may be implemented in hardware or software and are generally quite fast

## Slide 10: Asymmetric Cipher
A pair of keys - one to encrypt, the other to decrypt
One key is designated the public key, the other the private key
Solves key delivery over an insecure channel
Secure way of delivering messages in one direction
Very versatile mechanism applied many different ways
Much slower decryption performance
…commonly 1000x slower!

## Slide 11: Asymmetric Cipher
To send information only you can read, I'll need your public key
Guarantee is anything I send to you can only be read by you (…if that's really your public key)
Anyone else can send you private communication using your public key, too
You may need to authenticate that this came from me
Eavesdropping doesn’t hurt much, but “man in the middle” could

## Slide 12: Digital Envelopes
A hybrid approach employing enhanced key security of asymmetric ciphers with the performance of symmetric ciphers
The data (your IP) is encrypted with a session key using a symmetric cipher
  One use key, generated in a cryptographically random way
The session key is placed in a secure digital envelope
  i.e., encrypted with the public key of an asymmetric cipher
The ciphertext and the secure envelope are delivered to the user
The EDA tool decrypts the envelope, gets the session key, and then decrypts the data
You can send many envelopes holding the same session key at the same time with your data
Notes: Asymmetric ciphers have many applications – direct use, digital envelopes, digital signatures, public key certificates, message authentication

## Slide 13: Digital Signatures
A signature identifies you
  Legal significance, weakly resistant to forgery
In a digital signature, I take a little bit of information about me and/or my message
To sign, I encrypt it with my private key (asymmetric cipher is not about which key is revealed)
With my public key, anyone can authoritatively determine that I signed it
Two important applications to discuss
  Managing keys
  Authenticating delivered IP
Notes: I encrypt with one key and decrypt with the other, it is an application issue which one I choose to reveal

## Slide 14: Public Key Certificates Build Trust
A public key and information about its owner that a trusted party digitally signs is called a public key certificate
The trusted party, the certification authority (CA), guarantees that this is really that owner’s public key
The certificate is like a passport and the CA is like your government state department (or notary public)
The CA can be an external service provider, an industry or government agency
  ITU X.509 public key infrastructure standard
The signer is trusted by you and supports you in trusting someone else
Trust may be built organically using the “web of trust” model
  (open pgp, key signing parties, key servers..)
Notes: The need to build trust for secure transactions is regarded as a foundation for e-commerce
The most widely used standard for secure communication worldwide is openPGP. Its web of trust model works and is extremely scalable

## Slide 15: Using Signatures for Authentication
Compute a fixed length binary string from an arbitrarily long message, its message digest
Cryptographic hash function insures that no 2 messages will have the same digest
Decrypt a message, compute its digest, decrypt the signed digest, and compare
This process validates the authenticity of the message
Using message digests is an option in the standard

## Slide 16: Sanity Check
Strong encryption is possible with both symmetric and asymmetric ciphers
  Brute force attacks are computationally infeasible
Information is secure unless you have the keys
Key attacks could eavesdrop on key transmission, intercept the key and deliver a fake key, or steal the keys
Seems it’s all about managing the keys
Which I claim is about establishing a web of trust and using good quality tools

## Slide 17: The Key Management Problem
The HDL standards do not say how users and tools manage keys
You, as the IP provider, may have numerous keys
  1 per tool vendor, tool, tool rev, user…
  1 per model, per model revision, etc.
You manage these keys inhouse and delivers some of them
Tool Vendor has the same problems and one more
  potentially many keys from many IP providers
  tools must be delivered to customers with secured set of keys available
What does it take to make this manageable?

## Slide 18: The Secure Keychain Concept
In the standard, keys are identified by the tuple of owner and name
Secure keychain is an encrypted persistent database that accesses a key by its identifiers
Ability to import, remove, and export keys (maybe some other housekeeping utilities)
Only the keychain manager enabled tools can access the database
The concept has a role as a standalone program, part of encryption tool suite, and part of a compliant EDA design tool

## Slide 19: A Second Look at the Flow For Producing Protected IP
HDL
Secure
Local
Keychain
…protect me…
HDL
Markup with
protect
directives
Encrypt
…
Generate
Key(s)
Reference key(s)
Key
Import

## Slide 20: Validate Design Tool
Compliant
Design Tool
Runtime Data
Regression
Tests
Local
KeyChain
Tool Specific
KeyChain
Export/Import

## Slide 21: Validate EDA Design Tool
If necessary, export keys from your local keychain and import them into a design tool specific local keychain
Qualify the customer experience with your IP
  Run validation tests on models using your protected IP with that design tool
Qualify the tool
  Inspect all tool outputs for exposure of IP, look at runtime environment for implementation weakness
Deliver local keychain securely to vendor for hardening into a tool release(its default keychain)
Option to deliver a tool specific keychain with IP to directly customer?
  Depends on the strength of protection of the local keychain

## Slide 22: Choose Wisely
The secure keychain is just a concept to discuss principles
As an IP Provider, to give keys to my vendors I might:
  generate a key in a file, zip it, and email it…bad idea that often works
  write it to a memory stick and Fedex it or hand carry it…better
  Use PKI or web of trust to establish secure communications
As a tool provider handling my customers keys I might:
  Allows a tester to copy it to a work directory that anyone can read
  Write it to a open file that is shipped in “customer_keys” directory
  Use best practices for handling secured communications and deliver with secure keychain
The standard has sound mechanisms, but anything can be defeated by careless actions and weak implementation

## Slide 23: Simple Secret Key IP Protection Scenario
`protect data_keyowner="ACME IP Provider", data_method="aes192-cbc"
`protect begin
IP source text ...
`protect end
Notes: The IP author, ACME, has only key, so it can be referenced without naming it with a keyname directive
The data method, aes192-cbc, is a symmetric algorithm, the latest standardized by NIST, with 192 bit key length. It is block cipher

## Slide 24: Simple Secret Key IP Protection Scenario
`protect begin_protected
`protect encrypt_agent="Encryptomatic",encrypt_agent_info="2.3.4a"
`protect data_keyowner="ACME IP Provider", data_method="aes192-cbc"
`protect encoding = (enctype="base64", line_length=40, bytes=4006), data_block
encoded encrypted IP ...
`protect end_protected

## Slide 25: Default IP Protection Scenario
`protect begin
IP source text ...
`protect end
encryption tool selected key and algorithm
can only be decrypted by related tools that share key knowledge
no user generation or exchange of keys, no referencing of them
Interoperable EDA tool suites would use same defaults
Hmm…tool might enable the CAD group to configure defaults

## Slide 26: Default IP Protection Scenario
`protect begin_protected
`protect encrypt_agent="Encryptomatic", encrypt_agent_info="2.3.4a" `protect data_keyowner="Electrowizz Tool Co", data_keyname="crypto-101", data_method="des-cbc"
`protect encoding = (enctype="base64", line_length=40, bytes=4006), data_block encoded encrypted IP ...
`protect end_protected

## Slide 27: Digital Envelope Protection Scenario
`protect key_keyowner="ACME IP Owner", key_name=”For Joe Designer”,key_method="rsa", key_block
`protect data_method="aes192-cbc"
`protect begin
IP source text ...
`protect end
Key_* directives indicate digital envelope

## Slide 28: Digital Envelope Protection Scenario
`protect begin_protected
`protect encrypt_agent="Encryptomatic", encrypt_agent_info="2.3.4a"
`protect key_keyowner="ACME IP Owner", key_name=”For Joe Designer”,key_method="rsa"
`protect encoding = (enctype="base64", line_length=40, bytes=256), key_block
encoded encrypted session key ...
`protect data_method="aes192-cbc"
`protect encoding = (enctype="base64", line_length=40, bytes=4006), data_block
encoded encrypted IP ...
`protect end_protected

## Slide 29: Multiple Envelopes
`protect key_keyowner="ACME IP User1", key_method="rsa", key_block
`protect key_keyowner="ACME IP User2", key_method="elgamal", key_block
`protect key_keyowner="ACME IP User3", key_method="aes192-cbc", key_block
`protect data_method="aes192-cbc"
`protect begin
IP source text ...
`protect end

## Slide 30: A Signed Digital Envelope
`protect key_keyowner="ACME IP User", key_method="rsa", key_block
`protect data_method="aes192-cbc"
`protect digest_keyowner="ACME IP Author", digest_key_method="rsa"
`protect digest_method="sha1", digest_block
`protect begin
IP source text ...
`protect end

## Slide 31: Other Protect Directives in the Standard
Viewports
  Opens an aspect of your opaque IP for usability
  Immature aspect of the standard
Licensing
  Require a license check to access IP
  Provisioned with marginal security
Encoding
  Choose method of encoding binary ciphertext for textual representation
Documentation
  Comments and/or automatic annotation by encryption tools

## Slide 32: Standard Details
DES is the only required cipher method
  Symmetric algorithm and highly exportable
  It can be broken by brute force
SHA-1 and MD5 are only required cryptographic hash functions for computing message digests
  They are considered to be very good; SHA-1 is the better one
  Both have been broken, but spoofing IP is not a practical vulnerability
Provision is made in the syntax for virtually all known and important ciphers, cryptographic hash functions, and encoders

## Slide 33: High Quality EDA Tools for IP Protection Should…
Implement the standard
Provide additional market-driven ciphers, cryptographic hash functions, encoders
Provide utilities for key generation, keychain management, and encryption
Employ best practices for developing encryption tools
Deploy tools within the applicable law
Provide a process for establishing secure communication with IP providers
Collaborate on developing best practice for IP protection

## Slide 34: Recommendations
Advocate your requirements to the EDA vendor community
Learn how vendors will safeguard your keys in their house and in the field when the tools are in use
Qualify tools – tool-specific defaults, interoperability, performance, direct attack, runtime information compromise
Use good counsel on export laws, use of encryption, etc.
Make sure compromise doesn’t originate in your house
…and you’ll make more money with your HDL-based IP!
TRUST ME ;)

## Slide 36: Backup Material
Tremendous amount of info on the web
  Cryptographic technology
  Related export law
Experiment with Open PGP standard tools
  FSF’s GnuPG is a good choice
  No export restrictions on it to my knowledge (except known sponsors of terror)

## Slide 37: Symmetric Cipher
DES is a NIST standard, a 64 bit block cipher, with 56 bit key
A workhorse with no known structural attacks, brute force methods have cracked in ~22 hours ( ~30 2.2GHz Opteron years over 5 months was known level of effort at one time)
It is exportable to non-terrorist countries (but you want a legal opinion, not mine!)
Interim improvement is triple-DES (which is 3 times slower)

## Slide 38: Symmetric Cipher
AES is the new published NIST standard based on 128 bit blocks and 128, 256, or 512 bit keys
It was selected from a large field of candidates in a competitive process
It is unlikely to be cracked in our lifetime

## Slide 39: Asymmetric Cipher
RSA is most commonly used
Keys of >1024 bits are quite secure, 2048 should give security for decades