## Slide 1: Serdes Introduction and AMS modelling
Richard Ward
Serdes Engineering (ASIC)
25-July-2006
Notes: This presentation is designed to help you communicate TI’s 2003 priorities and your business priorities to your organization.

## Slide 2: Outline
  Serdes Introduction
  AMS Model Approach

## Slide 3: Standards for SerDes
Which Standard would you like to follow?
  802.3ap (10G Ethernet over backplane)
  OIF CEI 6G (short and long reach)
  OIF CEI 11G (short and long reach)
  PCI-Express (2.5G gen1, 5G gen2)
  XAUI (3.125G)
  Serial ATA (3.125G)
  FBDIMM/2 (4.8/6.4/8/9.6G)
  SerialRapidIO, (1.25/2.5/3.125G)
  Infiniband
  FibreChannel
  …

## Slide 4: What is the problem to solve?
3.125Gbps No EQ Tx FIR
6.25Gbps No EQ Tx FIR
~40” FR4 o/p

## Slide 5: Example Channel
Typical channel for 5 to 10Gbps (~40” FR4)

## Slide 6: Typical SerDes Block Diagram
Differential data has Clock and Data embedded into a serial stream. Most are NRZ/binary.
Keys parameters are:
  Jitter generation (Tx) and jitter tolerance (Rx)
  Equalization ability (both Tx and Rx sides) and adaption
  Asynchronous tracking rate of Rx
  PLL jitter rejection (from Refclk and chip/system noise)
Most higher rate systems are Rx DFE (analog or digital)

## Slide 7: How would an AMS model fit?
Different model requirements:
  Architectural analysis
  Customer SI and Interoperability
  Steady-state performance sims
  Higher levels of system integration than previously needed (AMS extending into the RTL/packet processing world)

## Slide 8: Performance Metrics
Pulse Response
Crosstalk Impulse
Response
Eye
StatEye (style)
Sample PDF
BER vs V Margin

## Slide 9: AMS Model Approach
Benefits
  Electrically aware
  Integration with chip and board design systems
  RTL level simulation interface
  Standard EDA toolset/languages
Drawbacks
  Performance!
    we believe this is the technical problem to solve
  Framework of statistical extrapolation from the time domain
  CAD license tie-up