## Slide 1: IBIS Interconnect SPICE Subcircuits IBIS-ISS
Supporting high-bandwidth connector, package and module interconnect modeling
Walter Katz
IBIS Summit Meeting at DAC 2009
San Francisco, CA
July 28, 2009

## Slide 2: Connector, Package, and Module Modeling Requirements
Signal Interconnect Modeling
Signal Coupling (crosstalk)
Power Distribution
  Rail voltage AC coupling
  DC drop
Coupling between Signal Interconnects and Power Distribution (SSO)

## Slide 3: Current IBIS Package Models are Not Sufficient > 1Gb/s
High speed channels require connector, package and module (e.g. DIMM) models that are:
  Broadband
  Distributed
  Coupled
  Power distribution
Consider the following simple package design
  Typical interconnect length of 1”
  11Gb/s
  Coupling between adjacent pins
  Adjacent connections are different length

## Slide 4: Electronic Module Description (EMD) Needs a Netlisting Language
The IBIS-ATM committee decided that since EMD required an interconnect sub-circuit netlisting language, IBIS-ATM should focus on this first
We would like to thank Synopsys for putting a subset of it’s HSPICE® manual into the public domain for the purpose of defining a generic interconnect SPICE language
HSPICE® is a registered trademark of Synopsys, Inc.
See http://www.vhdl.org/pub/ibis/macromodel_wip/ page for presentations about IBIS-ISS and EMD

## Slide 5: Solution Requirements
High level description language of connector, package, and module describing “pins” and “models” between pins/pads
Sub-circuit netlisting language
  Standardized wrapper describing subckt ports
  SPICE LTI Elements R,L,C,E,F,G,H,K,T,S,X
  .parameter and .include
Sparse Touchstone® File
  Standardized wrapper describing ports
  Sparse port matrix of pointers to transfer functions

## Slide 6: Sub-circuit Netlisting Language IBIS-ISS Elements
R Resistor
L Inductor
C Capacitor
Linear Controlled Sources
  E, F, G, H
  Include Pole-Zero and Laplacian
K Inductor coupling element
T Tline
W Line (RLGC/Table)
S-Parameter
V DC=0 Shunt Element
X-Element
  Subckts made of IBIS-ISS instances
Support .include
Support .parameter
Support parameter passing

## Slide 7: IBIS-ISS Design Decisions
Limited to linear time invariant (LTI) elements
Parameters are included, but some specific features such as Global Parameters, Ternary Operators and User Defined Functions have not been included
Scaling not supported (.option scale=x, M=x)
All elements must be contained inside one or more subcircuits

## Slide 8: Current Status
http://www.vhdl.org/pub/ibis/macromodel_wip/ site contains a working draft of the IBIS-ISS document
We request that IBIS members who either produce, or consume interconnect models review and comment on this proposal
IBIS-ATM meetings are held every Tuesday at noon Pacific time
To join in on the discussion
  ibis-macro@freelists.org