## Slide 1: Touchstone to Touchstone 2.0, Touchstone 2.0 to Touchstone too
Bob Ross
bob@teraspeed.com
IBIS Summit at
Design Automation Conference
San Francisco, CA
July 28, 2009

## Slide 2: Overview
Touchstone Version 2.0 ratified by IBIS April 24, 2009
Easy upgrades/downgrades a goal
  S-parameters the most common application
  Minimal addition/removal of keywords
  Transition period when tools support either original Touchstone and/or Touchstone 2.0

## Slide 3: Background
Touchstone issued 1984 by EEsof (now part of Agilent Technologies)
Touchstone is de-facto format widely used
Touchstone “Version 1.0” publicly uploaded for ICM
  http://www.eda.org/ibis/connector/
Touchstone Version 2.0
  Format rules relaxed
  Resistance per port option for PDS
  Mixed mode features for differential setups
  Some storage reductions available
  Mathematical conversions documented
  http://www.eda.org/pub/ibis/touchstone_version2.0/
  tschk2 parser planned soon

## Slide 4: Version “1.0” Block Arrangement
Option Line For example, # GHZ S MA R 50
N-port Data Block (rigid format rules)
Officially for Single-Ended Data
Optional Noise Data Block (n=2 only)

## Slide 5: “Version 1.0” Fixed Format Examples (f = frequency, s = data-pair)
S1P f s f s f s f …
S2P f s s s s f s s s s f s s s s f …
S3P f s s s s s s s s s f s s s s s s s s s f …
S4P f s s s s s s s s s s s s s s s s f s s s s s s s s s s s s s s s s f …
S5P f s s s s s s s s s s s s s s s s s s s s s s s s s f …
S6P f s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s f …
Formatting, frequency ordering, and end of file implies number of ports and frequencies values.
Etc …

## Slide 6: Touchstone Version 2.0 - Thirteen IBIS-like Keywords
Required keywords (and option line) – fixed order
  [Version] 2.0
  #(option line)
  [Number of Ports] <n>
Keywords in any order
  [Number of Frequencies] <nf> (required)
  [Two-Port Data Order] {21_12 | 12_21} (required for n=2 only)
  [Reference] <list of n reference resistances in port order>
  [Matrix Format] {Full | Lower | Upper}
  [Mixed-Mode Order] {Di,j, Ci,j, Si,j entries}
  [Number of Noise Frequencies] <nnf> (required if noise data, n=2 only)
  [Begin Information]/[End Information] (block reserved for future use)
Data block keywords
  [Network Data] (required to begin network data)
  [Noise Data] (required if noise data exists)
  [End] (required – End of file)

## Slide 7: Version 2.0 Block Arrangement
[Version] 2.0 # Option Line [Number of Ports] <n> plus keywords as req’d/needed
[Network Data]
More flexible formatted data
[Noise Data] (optional for n=2 only)
[End]

## Slide 8: Touchstone to Touchstone Version 2.0 (Single-ended S-parameters only)
Add keywords around the option line as shown
  [Version] 2.0
  #(option line)
  [Number of Ports] <n>
Add keywords in any order
  [Number of Frequencies] <nf>
  [Two-Port Data Order] {21_12 | 12_21} (if n = 2)
  [Mixed-Mode Order] {Si,j entries}
    Optional for re-ordering ports
Add keywords around the data block
  [Network Data]
  [End]

## Slide 9: [Number of Frequencies] and [Two-Port Data Order]
[Number of Frequencies] <nf> determination
  Documentation
  Count the frequencies or look at frequency interval and calculate nf
  Calculate from word count (wc) of data block
    wc = (2 n2 + 1) * nf
  Estimate nf and use tschk2 to calculate
    No Error – correct nf
    Error – tschk2 should report expected nf
[Two-Port Data Order] {21_12 | 12_21}
  Only for n=2
  Normally 21_12 for Touchstone to Touchstone 2.0

## Slide 10: Single-ended Port Re-ordering [Mixed Mode Order]
Optional
  Assumes Touchstone 2.0 processor handles [Mixed Mode Order] for re-mapping of ports
  Formulas in the Touchstone Version 2.0 Specification
Examples - next slides
  8 port connector re-mapping of the ports
  4 port re-mapping of the ports
  Argument Position applies to data block
  Diagonal-of-matrix centric indices represent Ports
  Tools can do tranforming by indexing

## Slide 11: Connector Re-ordering: [Mixed Mode Order] S1 S3 S5 S7 S2 S4 S6 S8
1
2
3
4
5
6
7
8
1
3
5
7
2
4
6
8
[Mixed Mode Order] S1 S5 S2 S6 S3 S7 S4 S8

## Slide 12: [Mixed-Mode Order] S1 S3 S4 S2 (SE-1 data re-ordered to SE-2)
1
2
3
2
1
4
SE-2
SE-1
pos entry SE-1
1 S1 1
2 S3 3
3 S4 4
4 S2 2
S11 S13 S14 S12
S31 S33 S34 S32
S41 S43 S44 S42
S22 S23 S24 S22
S11 S12 S13 S14
S21 S22 S23 S24
S31 S32 S33 S34
S41 S42 S43 S44
SE-1 uses SE-2 data notation in matrix
4
3

## Slide 13: Touchstone 2.0 to Touchstone
If Touchstone 2.0 file formed with tool using compatible Touchstone format rules
  Tool coding simplicity for dual export selection
  Then just remove keywords to convert to Touchstone
“[Matrix Format] Full” can exist and be removed
“[Two-Port Data Order] 12_21” may require interchanging the 12 and 21 columns with spreadsheet or program to the 21_12 order

## Slide 14: General Translations Probably Needs Conversion Tool
Everything would work for Y-parameters and Z-parameters except
  Normalization differences
  Check EDA tool normalization assumptions
General per-port reference impedance conversions probably needs software

## Slide 15: General Conversion Utility
Several EDA tools have built-in conversions
  Y-, Z-, S-parameter interchanges or choices
  Mixed mode interchange
  Auto port re-numbering (per physical design)
General conversion utility possible
  Normalizations and conversions
  Impose Touchstone format restrictions automatically
  Some mixed-mode port re-ordering
  [Matrix Format] Upper and Lower conversions
  (Future – sparse matrix manipulation)

## Slide 16: Closure
13 new keywords
Conversion of S-parameter data in Touchstone / Touchstone 2.0 formats needed to support leading/lagging EDA vendors, file producers and legacy files
Shorter term, simple addition or removal of keywords
Longer term, a more general conversion utility?
Touchstone 2.0 file reference checker/parser (tschk2) to promote industrial adoption