## Slide 1: VHDL-AMS and Verilog-AMS
A Dual Tutorial

## Slide 2: What is a Mixed-Signal Simulator?
"Digital" simulator
  State changes at discrete times determined by events
  State update is incremental
  Mathematical foundation is Boolean logic
"Analog" simulator
  State changes at discrete times determined by numerical error tolerances
  State update is global
  Mathematical foundation is DAEs
"Mixed-Signal" simulator
  The best of both worlds?
  An unfortunate compromise?

## Slide 3: What is a Mixed-Signal Language?
A unified notation for describing the objects of a mixed-signal simulation
  Expressive, readable, safe, modular...
Partitioning of design elements between simulators is explicit
  "digital" and "analog" statements
Synchronization between simulators is implicit
  Cross reference to a value calculated by the other simulator yields an accurate result at any time
  "Events" in one simulator can cause synchronous effects in the other
Notes: This is the speaker notes for slide 3

## Slide 4: {VHDL, Verilog}-AMS Time Line
1999
1997
1995
1993
1991
1992
1994
1996
1998
VHDL-AMS start
IEEE 1076 VHDL
Verilog-A start
IEEE 1364 Verilog
OVI Verilog-A V1.0
IEEE 1076.1 VHDL-AMS
OVI Verilog-AMS V2.0

## Slide 5: Genealogy
IEEE VHDL 1076.1 1999
IEEE VHDL 1076-1993
OVI Verilog-AMS V2.0
IEEE Verilog 1364
Verilog-A subset
OVI Verilog-A V1.0

## Slide 6: Both V-AMS Languages Feature...
Extended structural semantics
  Conservative connections to model physical systems
  Signal flow connections for abstract models
  Mixed-signal interfaces
Mixed-signal simulation
  Consistent synchronisation of mixed event-driven/continuous behaviour
  Design blocks share discrete and continuous objects
  Reading of objects is shared between simulators, writing of objects allowed by one simulator only

## Slide 7: Both V-AMS Languages Feature...
Continuous modelling extensions
  Time domain notation (ordinary differential algebraic equations)
  Conditional switching of equations
  Built-in waveform smoothing filters
  White, flicker, and frequency dependent noise sources
  Multiple energy domains

## Slide 8: Both V-AMS Languages Feature...
Frequency domain support
  Small-signal frequency simulation
  Noise simulation
  No explicit frequency domain notation, except...
  Compact notation for Laplace and Z transforms
Simulation control
  Support of tolerances
  Time step limiting
  Models can be sensitive to analysis mode

## Slide 9: Extras for VHDL-AMS
Handling of initial conditions and discontinuities
Mixed-signal initialisation well defined
Sequential or equation-based notation
Sound mathematical foundations based on differential algebraic equation theory
Formal definition

## Slide 10: Extras for Verilog-AMS
Automatic converter insertion at discrete/continuous boundaries
Automatic resolution of signal flow/conservative connections
Many built-in special case mechanisms
Equation formulation uses controlled source notation
Verilog VPI extension included
Informal definition -- user's manual

## Slide 11: What is Conservative Modeling?
V2, I2
V3, I3
V1, I1
branch equations:
  V1 == V;
  V2 == I2*R2;
  V3 == I3*R3;
KCL:
  I1+I2 == 0.0;
  I3-I2 == 0.0;
KVL:
  V1 == Va;
  V2 == Va-Vb;
  V3 == Vb;
a
b
V
Branch equations appear in the user's model
Others are derived from circuit topology

## Slide 12: A First Example: Parameterized Diode
id
RS
ic
p
m
p
m
+
Vd
-
Notes: 9

## Slide 13: … VHDL-AMS Diode
library IEEE, Disciplines; use disciplines.electromagnetic_system.all,IEEE.math_real.all; entity diode is generic (ISS, N, VT, TT, CJ0, VJ, RS: real); port (terminal p, m: electrical); end entity diode; architecture level0 of diode is quantity vd across id, ic through p to m; quantity qc: real; begin id == ISS * (exp((vd-RS*id)/(N*VT)) - 1.0); qc == TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ*vd); ic == qc'dot; end architecture level0;
Notes: 10

## Slide 14: … Verilog-AMS Diode
include disciplines.vams; module diode(p, m) electrical p,m; parameter real ISS, N, VT, TT, CJ0, VJ, RS; branch (p, m) Diode, cap; real qc; analog begin I(Diode)<+ ISS * (limexp(V(diode)-RS*id)/(N*VT)) - 1); qc = TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ*vd); I(cap) <+ ddt(qc); end endmodule;
Notes: 10

## Slide 15: Elements of a Design Entity
library IEEE, Disciplines; use Disciplines.electromagnetic_system.all,IE entity diode is generic (ISS, N, VT, TT, CJ0, VJ, RS: rea port (terminal p, m: electrical); end entity diode; architecture level0 of diode is quantity vd across id, ic through p to m; quantity qc: real; begin id == ISS * (exp((vd-RS*id)/(N*VT)) - 1.0); qc == TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ* ic == qc'dot; end architecture level0;
context
interface
Per-use constants
body
connections
declarations
statements
Which libraries?
Which packages?
Notes: Declarations create objects; statements use the objects created by declarations.

## Slide 16: Elements of a Module
include disciplines.vams; module diode(p, m) electrical p,m; parameter real ISS, N, VT, TT, CJ0, VJ, RS; branch (p, m) Diode, cap; real qc; analog begin I(Diode)<+ ISS * (limexp(V(diode)-RS*id)/(N*VT)) - 1); qc = TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ*vd); I(cap) <+ ddt(qc); end endmodule;
Per-use constants
interface
connections
declarations
body
statements
context

## Slide 17: VHDL_AMS Nature
A simple nature represents a physical discipline or energy domain
It has two aspects:
  Across: effort-like effects -- voltage, velocity, temperature
  Through: flow-like effects -- current, force, heat flow rate
A nature derived from a given simple nature may be scalar, or it may be an array or record
A simple nature includes a reference terminal
Natures are declared in VHDL-AMS packages
Notes: 12

## Slide 18: VHDL-AMS Environment Packages
package electromagnetic_system is
subtype voltage is real tolerance "default_voltage"; subtype current is real tolerance "default_current";
attribute symbol of current:subtype is "A";
attribute symbol of current:subtype is "V"; nature electrical is voltage across current through
electrical_ground reference; end package electromagnetic_system;
Simplified for illustration!
package thermal_system is
subtype temperature is real;
subtype thermal_power is real;
nature thermal is
temperature across
thermal_power through;
thermal_ground: reference; end package thermal_system;
Notes: 13

## Slide 19: Verilog-AMS Discipline
A basic discipline represents a physical discipline or energy domain
It has two aspects: effort and flow
A net may be an array of elements of a given discipline
A net is grounded using the ground declaration
Even digital nets have disciplines!
Disciplines are defined in disciplines.vams
Notes: 12

## Slide 20: Verilog-AMS "Include" File
nature Current
units = "A";
access = I;
idt_nature = Charge;
abstol = 1e-12;
endnature
nature Voltage
units = "V";
access = V;
idt_nature = Flux;
abstol = 1e-6;
endnature
Simplified for illustration!
// Conservative discipline
discipline electrical
potential Voltage;
flow Current;
enddiscipline
// Signal flow disciplines
discipline voltage
potential Voltage;
enddiscipline
discipline current
potential Current;
enddiscipline
discipline logic domain discrete enddiscipline
Notes: 13

## Slide 21: The VHDL-AMS Terminal
library Disciplines; use Disciplines.electromagnetic_system.all; … entity diode is … port (terminal p, m: electrical); end entity diode;
Ports are the connections to the outside world
Signals for digital connection, terminals for analog connection
Terminals support conservative semantics
Each terminal belongs to a nature
Notes: 11

## Slide 22: The VHDL-AMS Quantity
The unknowns in the equations of your model
Not the same as a shared variable!
Value determined by the analog solver
Scalar subelements must be of a floating-point type
Default initial value for scalar subelements is 0.0
architecture level0 of diode is … quantity qc: real;
quantity vd across id, ic through p to m;
begin …
ic == qc'dot; end architecture level0;
Notes: 14
More specifically, quantities are the unknowns in the system of differential algebraic equations described by the model.
A variable is assigned within a VHDL process, by a sequential assignment statement, when the flow of control reaches the assignment statement.
All quantities are given their values simultaneously by the analog solver at each time a solution is required. The values are such that every equation is true at that time (within the error tolerance of the analog solver).
Quantites may be arrays of one or more dimensions. The elements of the array must be of a floating point type like the predefined type real.
In the absence of explicit instructions to the contrary (which you will see later) each quantity element is given an initial value of zero. That's not the same thing as an initial condition!

## Slide 23: VHDL-AMS Branch Quantity
Branch quantities are the variables used in branch equations
Across quantity vd is the voltage between p and m
Through quantities id and ic are currents
Each through quantity defines a distinct branch
architecture level0 of diode is quantity vd across id, ic through p to m; ... begin
id == ISS * (exp((vd-RS*id)/(N*VT)) - 1.0); ... end architecture level0;
Notes: 17

## Slide 24: VHDL-AMS Free Quantity
Used to formulate arbitrary equations
Can store intermediate value to build complex expressions
architecture level0 of diode is ... quantity qc: real; begin ... qc == TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ*vd); ... end architecture level0;

## Slide 25: VHDL-AMS Implicit Quantity
Many kinds -- 'dot is just one
No explicit declaration
Underlying quantity may be a declared quantity or another implicit quantity
architecture level0 of diode is ...
begin ... ic == qc'dot; end architecture level0;

## Slide 26: The Verilog-AMS Port
Ports are the connections to the outside world
Ports of discrete discipline for digital connections
Ports of continuous discipline for analog connections
Ports of conservative, continuous discipline support conservative semantics
include disciplines.vams; module diode(p, m) electrical p,m; ...
discipline logic domain discrete enddiscipline
Notes: 11

## Slide 27: The Verilog-AMS Branch
A branch spans a pair of continuous nets
V(Diode) names the voltage between p and m
I(Diode) names the current in the p to m branch -- and sometimes creates a short!
One implicit branch between any pair of nets is accessed with V(p,m), I(p,m)
module diode(p, m) ... branch (p, m) Diode ... ... analog begin I(Diode)<+ ISS * (limexp(V(diode)-RS*id)/(N*VT)) - 1); ... endmodule;
Notes: 17

## Slide 28: Verilog-AMS Variable
Stores intermediate value -- retained, not reinitialized
Used to formulate arbitrary equations in sequential code
Digital variables and analog variables are distinct
module diode(p, m) ... real qc; analog begin ... qc = TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ*vd); ... end endmodule;

## Slide 29: Verilog-AMS Analog Operator
Many kinds -- ddt() is just one
Argument is an expression without nested analog operators, except...
ddt(ddt(…)) is allowed as a special case
include disciplines.vams; module diode(p, m) ... analog begin ... I(cap) <+ ddt(qc); end endmodule;

## Slide 30: VHDL-AMS Simultaneous Statements
Expresses a relationship among quantities
  Expressions on left and right have the same form
  Expressions may include quantities, constants, literals, signals, and functions
Quantities are determined simultaneously
Order of statements does not matter
library IEEE; use IEEE.math_real.all; architecture level0 of diode is … begin id == ISS * (exp((vd-RS*id)/(N*VT)) - 1.0); qc == TT*id - 2.0*CJ0 * sqrt(VJ**2 - VJ*vd); ic == qc'dot; end architecture level0;
Notes: 20

## Slide 31: Solvability
For solvability, #equations = #unknowns
Each (scalar) simultaneous statement creates one equation
#unknowns = #quantities (but ignore across quantities!)
architecture Bad of Vsource is quantity v across p to m; begin v == V0; end architecture Bad;
architecture Good of Vsource is quantity v across i through p to m; begin v == V0; end architecture Good;
OK
OK
library Disciplines; use Disciplines.electromagnetic_system.all; entity Vsource is generic (V0: real); port (terminal p, m: electrical); end entity Vsource;
Notes: 57

## Slide 32: Verilog-AMS Branch Contribution
Target is branch effort or flow
Can't target both effort and flow of one branch
Multiple contributions sum
Reference to a flow in a branch that is not a target creates a short
include disciplines.vams; module diode(p, m) ... analog begin I(Diode)<+ ISS * (limexp(V(diode)-RS*id)/(N*VT)) - 1); … I(cap) <+ ddt(qc); end endmodule;

## Slide 33: Piecewise Defined Behavior: VHDL-AMS
library IEEE, Disciplines; use Disciplines.electrical_system.all; use IEEE.math_real.all;
entity Compressor is
generic (vmax : REAL := 10.0;
a : REAL := 100.0;
gain : REAL := 1.0 );
port (terminal ip, im, op, om : electrical);
end entity Compressor;
architecture A_law of Compressor is
quantity vin across ip to im;
quantity vout across iout through op to om;
constant alog: REAL := 1.0 + log(a);
begin
if -vmax/a < vin and vin < vmax/a use
vout == gain * a * vin / ( alog * vmax );
elsif vin > 0.0 use
vout == gain * ( alog + log( vin/vmax) ) / alog;
else
vout == -gain * ( alog + log(-vin/vmax) ) / alog;
end use;
end architecture A_law;

## Slide 34: Piecewise Defined Behavior: Verilog-AMS
include disciplines.vams; module compressor(ip, im, op, om) electrical ip, im, op, om; parameter real vmax= 10, a= 100, gain= 1; branch (ip, im) in; real alog, vout; analog begin @(initial_step) alog = 1 + log(a); if (-vmax/a < V(in) & V(in) < vmax/a)
vout = gain * a * V(in) / ( alog * vmax );
else if (V(in) > 0)
vout = gain * ( alog + log( vin/vmax) ) / alog;
else
vout = -gain * ( alog + log(-vin/vmax) ) / alog;
V(op,om) <+ vout; end endmodule;

## Slide 35: Sample and Hold
entity shold is
port (terminal inp, inm, clk, dout: electrical);
end entity Compressor;
architecture one of shold is
quantity vclk across clk;
quantity vout across iout through inp to inm;
signal store: REAL;
begin
store <= vin when vclk'above(2.5);
vout == store'ramp(10.0e-9)'delayed(50.0e-9);
end;
module shold(inp, inm, clk, dout) electrical inp, inm, clk; input inp, inm, clk; output dout; real store; analog begin @(cross(V(clk)-2.5, 1) store = V(inp,inm); V(dout) <= transition(store, 50n, 10n); end endmodule;

## Slide 36: Dual Slope A/D: Theory
vin
-vref
ctr1
ctr2
dout
cvin
cvin'integ

## Slide 37: Dual Slope A2D: Verilog-AMS
module dual_slope(inp, vref, ctr1, ctr2, outp) electrical inp, outp, vref; input inp, vref, cntr1, ctr2; output outp; integer dir, assert; real integ, cvin; analog begin @(initial_step or posedge ctr1) begin dir=0; assert=0; end @(posedge ctr1) dir = 1; @(posedge ctr2) dir = -1; @(posedge ctr2) begin dir = 1; assert = 1; end case (dir) 1: cvin= V(inp); -1: cvin= V(vref); 0: cvin= 0; endcase integ <+ idt(cvin, 0, assert); end always @(cross(integ,+1)) outp = 1; always @(cross(integ,-1)) outp = 0; endmodule;

## Slide 38: Dual Slope A2D: VHDL-AMS
library IEEE, Disciplines; use Disciplines.electrical_system.all; use IEEE.std_logic_1164.all;
entity dual_slope is
port (
terminal inp, vref: electrical;
signal ctr1, ctr2: in std_logic;
signal outp: out std_logic);
end;
architecture one of dual_slope is
signal svin: REAL;
quantity cvin: REAL;
begin
svin <=
inp'reference when rising_edge(ctr1) else
vref'reference when rising_edge(ctr2) else
0.0;
cvin == svin;
break cvin'integ => 0.0 when falling_edge(ctr2);
outp <= '1' when cvin'integ'above(0.0) else '0';
end;