## Slide 1
IBIS .ICM
Sub-Committee Participants
Simulation Vendors
Ansoft
Cadence
HyperLynx / Pads
Innoveda
Mentor
Connector Companies
AMP / Tyco
Berg / FCI
Molex
Teradyne
End Users
EMC
Connectors
Connectors
Connectors

## Slide 2
What has the editing committee been up to?
IBIS .ICM
Our goals:
Incorporate changes requested at DesignCon 2000 IBIS meeting.
Ensure syntax is not ambiguous
Improve syntax descriptions, grammar, etc.
Release the specification for vote near DAC 2000 time frame.

## Slide 3
What has the editing committee been up to?
IBIS .ICM
What has been done so far?
Changes requested at the DesignCon 2000 IBIS meeting have been added.
Several areas of ambiguous syntax were identified and have been clarified.
Several pages of documentation have been added to improve description of keywords and syntax.
Converted the specification to Word format and formatted it using fixed point fonts so that it can be output as .doc, .txt, and .pdf formats.

## Slide 4
What has the editing committee been up to?
IBIS .ICM
Ambiguous-syntax changes:
1) The matrix descriptions did not clearly define how the matrix was to be modeled (i.e., lump or distributed). It was felt that both methods should be allowed, as was allowed in the IBIS .ebd file. We chose an additional keyword to indicate lumped v.s. distributed. We also added a keyword “Mult=” to each matrix section use to allow matrix re-use. The is similar to the len= capabilitiy of the .ebd file but more powerful as we are talking about matrices not transmision lines and we can scale with a multiplier either a lumped matrix or a distributed matrix which allows re-use of the matrix data.

## Slide 5
What has the editing committee been up to?
IBIS .ICM
Ambiguous-syntax changes:-
2) The swath method was modified to more exactly define the way in which a small matrix is utilized to simulate a much larger matrix. The mapping at the edge of the connector was not clearly enough defined. Portions of the matrix are now designated as “edge only.”

## Slide 6
What has the editing committee been up to?
IBIS .ICM
Ambiguous-syntax changes:
3) Line lengths were changed to a fixed 120 character maximum instead of having both 80 and 120 limits.
4) Line continuation is now allowed for model sections and stubs.

## Slide 7
What is a Matrix Section?...
A: A matrix section is a set of tables of numerical values that represent the electrical relationships between all conductors of a given geometry. Further, the matrices used in this specification closely follow the concepts used in the IBIS IC specification.
For example:
[Begin_Section] NameA
[Derivation Method] Lumped
[Inductance Matrix] Full_matrix
.
.
[Capacitance Matrix] Full_matrix
.
.
[Resistance Matrix] Full_matrix
.
.
[End_Section] NameA
IBIS .ICM

## Slide 8
What is a "Swath Matrix Section"?
A: It is a method of using a small matrix section to define a much larger and variable size section of a connector. This facilitates faster simulations, smaller file sizes, and makes the
creation of a family of connectors much easier.
For example:
| SwathRows SwathCols RightEdge LeftEdge TopEdge BottomEdge
[Begin_Cn_Swath] 4 6 1 1 0 0
[Cn_Z] 50
[End_Cn_Swath]
This example defines a small matrix section of 4 rows and 6 columns. The right- and left-most columns are used only for the right and left edges of the connector. This might be used to define a connector with 4 rows and 6 to 1000 columns. The edges of the small swath matrix are to be connected to 50 ohms to ground when not used at the edge of the connector.
IBIS .ICM

## Slide 9
Cascade Matrices (series)
Q: What are cascaded matrices?
A: Cascaded matrices are a series of matrix slices that walk down the connector from one side to the other. The matrices are defined the same as in the IBIS .pkg specification and may be full, spares, banded, or diagonal.
For example:
[Begin_Cn_Model] Hdi20 Hdi20Pin Hdi20Phy MLM
Cn_Section NameA Mult=1.0
Cn_Section NameB Mult=1.0
[End_Cn_Model] Hdi20
IBIS .ICM

## Slide 10
Stub Matrices (tee's)
Q: What is a stub matrix?
A: A matrix that is connected to the cascaded matrix sections
by a tee.
For example:
[Begin_Cn_Model] Hdi100 Hdi100Pin Hdi100Phy MLM
Cn_Section NameA Mult=1.0
Cn_Section NameB Mult=1.0
Cn_Stub StubNameA Mult=1.0 StubNameB Mult=1.0 Cn_Section NameC Mult=1.0
[End_Cn_Model] Hdi100
IBIS .ICM

## Slide 11
Putting the pieces together...
[Begin_Cn_Model] Hdi200 Hdi200Pin Hdi200Phy MLM [Cn_Number_of_Conductors] 40
[Cn_Columns_of_Pins] 20
[Cn_Rows_of_Pins] 2
| SwathRows SwathCols RightEdge LeftEdge TopEdge BottomEdge
[Begin_Cn_Swath] 2 4 1 1 0 0
[Cn_Z] 50
[Cn_Horizontal_Swath]
[End_Cn_Swath]
Cn_Section NameA Mult=1.0
Cn_Section NameB Mult=1.0
Cn_Stub StubNameB Mult=1.0
Cn_Section NameA Mult=1.5
[End_Cn_Model] Hdi200
[Begin_Section] NameA
[Derivation Method] Distributed
[Inductance Matrix] Full_matrix
[Capacitance Matrix] Full_matrix
[Resistance Matrix] Full_matrix
[End_Section] NameA
.
.
.
IBIS .ICM

## Slide 12
What's Next?
Short Term Goals:
  Finalize the sub-committee changes
  Vote to adopt the version 1.0 “ICM” specification.
  Ask for funds to create the golden parser to be used for syntax checking connector models.
  Update the examples to support the final syntax and keywords
  Additional accuracy confirmation of .icm model
    compare to “real” connector data
    compare to SPICE model
    compare to IBIS Package model
Version 2.x Goals:
  Add lossy modeling
  Add support for other .EBD capabilities that might address issues like cross-over pins.
IBIS .ICM