## Slide 1
EMI Parameters for IBIS
Guy de Burgh

## Slide 2: Proposed EMI parameters
Cpd Power Dissipation Capacitance.
  This is the internal parasitic capacitance + the equivalent capacitance associated with the through currents when both transistors are momentarily conducting.
  Parameter is given in the datasheets.
  Used to calculate the noise voltage on the power bus ( I(t) = Ceff dv/dt where Ceff is the total decoupling capacitance).
DIE HEIGHT Represented by package thickness.
  Used for loop area calculation.
<number>

## Slide 3: Proposed EMI parameters
HEATSINK Heatsink dimensions (Length, Width, Thickness). Dimensions used to calculate capacitance. Also need to indicate which components have a heatsink. Heatsinks can act as antennas and are driven by potential differences on the power plane.
CON_PIN Assigns a model name to a pin of a connector.
CON_SPEC Assigns parameters to CON_PIN. Parameters indicate whether the pin is unshielded, shielded, connected to the shield, has a ferrite filter, and has an explicit filter capacitor. Used to calculate an antenna impedance for the pin.
<number>

## Slide 4: Proposed EMI parameters - examples
Example 1 [Component] comp_1 CPD 6.4 # pF ICCD 61.5 # mA/MHz
Example 2 [Component] comp_2 DIE_HEIGHT 78.74 # mils HEATSINK L: 590.55 W: 590.55 T: 472:44 # mils
<number>

## Slide 5: Proposed EMI parameters - examples
Example 3 [Component] connector_1 CON_PIN 1 sig_out CON_PIN 2 sig_shield CON_PIN 3 sig_out CON_PIN G1 grounded [Model] sig_out CON_SPEC unshielded C: 6.0 # unshielded pin, C in pF [Model] sig_shield CON_SPEC is_to_shield C: 9.0 # pin connected to the shielded, C in pF [Model] grounded CON_SPEC is_shielded C: 7.0 # individually shielded pin, C in pF
<number>

## Slide 6: What’s next?
Use proper SI units E.g. e-12F instead of pF, Metric units, etc.
Prepare a more detailed specification
  Need to add more details as to why these parameters are important.
  How to measure the parameters.
Submit a Bird
<number>