## Slide 1: The IBIS-X Specification
Stephen Peters,
Intel Corp.

## Slide 2: Agenda
What is IBIS-X? How is it different from IBIS 3.2?
Backwards Compatibility Concerns
An Introduction to Defining New Models
Walk thru of the IBIS-X document itself

## Slide 3: What is IBIS-X?
More than just a ‘template tweak’ of IBIS 3.2
  Formalizes fundamental idea behind IBIS: separation of model data from the EDA tool algorithm(s) that processes data
  IBIS-X introduces the mechanism whereby a file creator can tell the EDA tool how to process the data – i.e. the user can now “create a model” by using a new [Define] keyword and a nodal-based ‘macro language’
  IBIS-X will eventually include a nodal-based package description
IBIS-X spec itself still focuses on the model data transfer standard
  IBIS Macro Language (IBIS-ML) is addressed in a separate Language Reference Manual (LRM)

## Slide 4: Backwards Compatibility
Existing IBIS keywords are unchanged
  IBIS-X capable EDA tool can still parse a 3.2 file with a 3.2 parser (or IBIS-X parser in ‘compatibility mode’)
    All existing models still work with IBIS-X (see below)
  Syntax changes to data template format are transparent to operation of simulation
Transition between IBIS -> IBIS-X?
  IBIS Open Forum will (must!) provide
    IBIS-X parser and (by default) IBIS-X to “SPICE” converter
    Library of all existing IBIS 3.2 model types written in IBIS-ML
    Existing IBIS 3.2 models documented in Library guide

## Slide 5: Introduction to Creating New Models
An I/O buffer model is a specific example of a simulation object
  Simulations objects are grouped into “classes”, different objects within a class can be of different “type”
[Model] is a class of object, while “input”, “output”, “3-state”, etc. are of different types within the class
  Notice: objects are not limited to I/O buffer models. [Test Load] is a class of simulation object, as is [Submodel].
User can create a new type within the ‘Model’ class, or create a whole new class

## Slide 6: Creating New Models (cont.)
Object (model) creation is a two step process
  The structure and behavior of a simulation object is defined using the [Define “class name”] keyword and described using IBIS-ML constructs – I.e. the model creator builds an object “template”
  The IBIS-X file then supplies a specific set of simulation data for that object – I.e. the file creator “customizes” an object template
To be used, an object has to be both ‘defined’ and ‘customized’

## Slide 7: The [Define “class name”] keyword
Syntax:
[Define “class_name”] “type name” (<optional port list>)
|
| IBIS-ML Constructs
|
[End “class name”] “type name’
[Define] keyword can be used in IBIS-X file itself – or – [Defines] are collected into a library file (‘included’ into an IBIS-X file)
Once an object is defined, it is customized as shown:
[Begin “class name”] “object name”
“class name”_type “type name”
|
| optional data specific to this instance
|
[End “class name”]
Object customization takes place in the IBIS-X file

## Slide 8: Specific Example (from section 8)
Create a template for a differential receiver (new class and type)
[Define Receiver] differential (in_pos, in_neg, pwr, gnd)
|
| IBIS-ML constructs
|
[End Reciever] differential
To create object named ‘data_receiver’, customize this template
[Begin Receiver] data_receiver
Receiver_type differential
|
| data set for this model
|
[End receiver]

## Slide 9: Specific Example (cont.)
To create a second object ‘data_receiver_alt’ from same template…
[Begin Receiver] data_receiver_alt
Receiver_type differential
|
| data set specific to data_receiver_alt
|
[End receiver]
User now has two models (objects): ‘data_receiver’ and ‘data_receiver_alt’

## Slide 10: Overview of the IBIS-X Document
7 major technical sections
  General Syntax Rules and Guidelines
  IBIS File Header & Global Keywords (2 sections)
  Component Information (unchanged from current IBIS)
  New Model Definition (replaces [Model] documentation)
  Package Modeling (placeholder for new .pkg model)
  EBD (unchanged from current IBIS)
IBIS-X spec does not address macro language, but will include a section on “data structures”

## Slide 11: General Syntax Rules & Guidelines
Like connector spec, seek to remove limits
  120 character lines (rule 7)
Clarify usage, resolve ambiguities
  Added ‘arguments’ to keywords and explicitly defined ‘text blocks’ & their termination
  Explicit definition of ‘sections’
  Allow text before [Begin Header] and after [End] (rule 13)
Also, added a keyword tree diagram

## Slide 12: IBIS File Header & Global Keywords
Same intent, with a few additions
  Added begin/end blocking and IBIS-X specific version marker
    [Begin Header], [End Header], [IBIS-X Ver]
  Added Support for model library include function
    [Include Library]
“steal with pride” connector spec ideas
  Added support and redistribution information keywords
    [Support], [Redistribution], [Redistribution Text]
Added a keyword for “include text” function
  [Include] includes a text file, is global is scope

## Slide 13: Component & “Model” Section
Component section basically unchanged from current IBIS 3.2
  Clarified that [Model Selector] is global in scope
  Added [End Component] to match [Begin Component]
New “Models” section documents the model definition process
  Introduces concept of object classes and types within a class
    [Define “class name”] mechanism for creating a new object (model)
  Discusses object template and customizing an object
    [Begin “class name”] keyword for supplying data to object (model)
  Need to add discussion on model data ‘types and structures’

## Slide 14: Package Modeling & EBD sections
Package modeling is part of IBIS-X spec
  IBIS-X will incorporate, by reference, current .pkg file syntax
  Section is placeholder for nodal-based package modeling
Electrical Board Description (EBD) is incorporated unchanged from IBIS 3.2
  EBDs still serves a useful purpose