## Slide 1: IBIS-X and the IBIS Macro Language
Author: Stephen Peters
AV&T group, IBIS Vice-Chair
Edited by: Arpad Muranyi
Intel Corporation

## Slide 2: Background
Current IBIS up against limits
  Description lagging new technologies
  Limited support for return path modeling
  Limited support for coupled package modeling
  No support on horizon for receiver models
  No support for frequency domain analysis
IBIS-X Goal: provide the path to a ‘next generation’ I/O buffer description language.

## Slide 3: IBIS-X requirements
Keep the good stuff
  standardized description
  protect IP
  document SI parameters
  continue support for board level (behavioral) simulators
Expand format, structure to fix problem areas
  expandability, flexibility (add nodal connectivity, get away from fixed assumptions and keywords)
  enable accurate modeling of SSO, power delivery and package effects
  support behavioral receivers
  enable generalized equations, S-parameters, etc.

## Slide 4: IBIS-X Approach
Nodal descriptions are a necessity
  die interconnect (pin - pad - buffer) descriptions
  power delivery and pin-pin coupling
  connections for black boxes
Macro language for creating new model prototypes
  flexible, extendable, allows existing IBIS models to be reused
  enables a wide variety of descriptions
Bottom Line: user will have the ability to create his/her own custom buffer (model_type), and specify a package model in a standard format.

## Slide 5: Overview of Model Type Creation
User creates a new model type using the [Define] keyword
User describes new type using macro language
  interconnect L/R/C elements and sources, data/values are parameterized
  programming flow statements/operators available
  special statements for trigger events, etc.
User then instantiates model in .ibs file ([Model] statement) and supplies data for that instance, just as before.

## Slide 6: Example (define the model)
[Define Model] simple_driver (gnd, pin, control)
node T1
Vsource (T1 gnd) V=Rise[T-TR] || Fall[T-TF]
Rsource (pin T1) R=Rsrc[T-TR] || Rsrc[T-TF]
trigger TR (Logic(control) == 1)
trigger TF (Logic(control) == 0)
[End Define Model]

## Slide 7: Example (supply the data)
[Model] driver_1
Model_type simple_driver
[Rise]
0n 0
2n 1
5n 4
5
[Fall]
0n 5
2n 4
5n 1
7n 0
[Rsrc]
0n 7
2n 1k
3.5 100k
5n 1k
7n 5

## Slide 8: Basic Elements
SPICE Compatible
Resistor (R) (defines v = f(I,t); r=constant or f(t))
Capacitor (C) (defines q = f(v,t); c=constant or f(t))
Inductor (L) (defines flux = f(I,t); L= constant or f(t))
VCVS (E) (defines Vout = f(Vin,t))
VCCS (G) (defines Iout = f(Vin,t))
Isource (I) (defines fixed I or I= f(t))
Vsource (V) (defines fixed V or V= f(t))
Diode (D) (basic diode, subset of Spice parameters)
Subckt (X) (used for submodel, driver schedule)
Extended (some, but not all SPICE support)
Voltage controlled Resistance (VCR) (defines R = f(v))
Voltage controlled Admittance (VCG) (defines Y = f(v))
Voltage controlled Cap (VCCAP) (defines C = f(v))
Uncoupled transmission lines
Coupled transmission lines

## Slide 9: Basic Elements (cont.)
Syntax for elements should be familiar
<type> <instance name> (<nodes>) <value>
Example: Resistor R12 (2 4) R=10k
Values can take on several forms
simple value (10k)
scalar symbolic value (C_comp)
built-in symbolic value (VT)
    uses the value of an internal variable, such as TIME
1D table symbolic (I=Pullup[V])
2D table symbolic (I=Pullup[V,T] or I=Series_mosfet[Vc,Vo])
Expressions can be made of combinations of above.
Operators are: +, -, *, || with usual bindings.
|| is evaluated as in Perl, allows for optional data sets / keywords
Example : Vx (Vcc gnd) V=(Pullup Reference) || (Voltage Range)

## Slide 10: Extended Blocks Beyond Spice
Needed now for Supporting drivers & receiver blocks
Driver (a complex device for backward compatibility)
Reshape (generates a digital pulse, reshaped from it’s input)
Delay (out = in, but delayed)
Voltage Controlled Delay
Possible (likely) extensions for future work
Behavioral voltage source (“B” element)
Behavioral current source (“B” element)
Integrator block
Differentiator block
Behavioral integrator
Behavioral differentiator

## Slide 11: .Extended (.dot) Elements
Model Creation/Functionality Related
trigger (time value expression) – generates a trigger event when condition is met
node – declares node name to be local
inherit – inherit properties of another model or base structure
Debug/Visibility Related
export – list of local symbols that can be made visible to the user
alarm (time value expression) – notifies user when some event happens, used for error checking and the like
assert (static logic expression) – check for a condition to be true, again for error checking

## Slide 12: More Extended (.dot) Elements
Programming Flow
if (static logic expression)
else if (static logic expression)
end if
select
case
end select
foreach (index) in (pointer to data structure) – sets up an array of objects tied to a keyword. Used to implement driver schedule and submodel functionality

## Slide 13: Equation Based Modeling
General equations (Berkley B-element) not supported directly in initial release
  Looking for quick implementation/adoption using existing technology.
  Equation support planned for future release based on feedback
  However, no reason one can’t turn equations into tables which are supported.
Nothing in IBIS-ML prevents the support of equation based modeling (i.e. support for Berkley B-element) in future release.

## Slide 14: Current Status
IBIS 3.2 has been implemented in IBIS-ML
Working group meets bi-weekly to work on writing formal specification(s)
  Overall IBIS-X specification
  Library guide
  Programmers Language Reference Manual
Much work remains on die interconnect section
  Coordinating with IBIS connector spec
  Need for additional volunteers