## Slide 1
Signal Integrity Software, Inc.
LVDS IBIS Models @ 1.25GHz
Douglas J. Burns
Steven R. Coe
Kevin M. Fisher

## Slide 2: Low Voltage Differential Signaling
Higher signaling speeds
Lower voltage swing
Lower power consumption
Less susceptible to common-mode noise
Reduced EMI

## Slide 3: Challenges in using IBIS to model LVDS
IBIS specifically designed for single-ended I/O buffers
Behavioral (IV) curves show current as a function of voltage applied to pad
Current of LVDS buffer dependent on voltage at both pads, and common-mode voltage (vcm)

## Slide 4: Extracting & Using LVDS IBIS Models

## Slide 5: Generating an LVDS IBIS Model
Step 1: Find vcm of device
Drive into expected loading conditions &
topology to obtain

## Slide 6: Generating an LVDS IBIS Model
Step 2: Sweep vout on one output pad, keeping vcm constant throughout sweep
Step 3: Extract the curves, convert to IBIS format

## Slide 7: Using an LVDS IBIS Model
Two instantiations of extracted model: one for true, one for complement
Complement stimulus 180° out of phase with true stimulus

## Slide 8: Accurate LVDS IBIS Model @ 1.25GHz
SPI4 interface: 1.25GHz, target pad, VDDQ=2.375

## Slide 9: Potential Issues
Some simulators may modify LVDS’s “non-traditional” IV curves
  Some versions of Hspice modify IV curves not passing through (0, 0) if IV table does not have entry at i=0
LVDS IBIS models are accurate only when same VDDQ model was generated with is used
  Changing VDDQ leads to very inaccurate results

## Slide 10: Effects of Changing VDDQ
SPI4 interface: 1.25GHz, target pad, VDDQ=2.325,
Model generated w/VDDQ=2.375

## Slide 11: Potential Issues
LVDS IBIS models assume constant Vcm
  Must generate multiple models for different values of vcm to obtain consistent accuracy driving different loads and topologies
Device asymmetry will affect accuracy of model
  Model generated for both pads assumes perfect driver symmetry
  Etch lengths of nets in differential pair matched

## Slide 12: Conclusion
It is possible to generate IBIS models for LVDS devices and obtain accurate results at speeds exceeding 1GHz
Improper use of properly generated LVDS IBIS models can & will lead to inaccurate results
Issues with LVDS IBIS models do exist, but can be avoided with proper knowledge of:
  Device and application of device
  How target simulator handles these models

## Slide 13
Signal Integrity Software, Inc.