## Slide 1: IBIS Interconnect Specification
Stephen Peters, Intel Corp.

## Slide 2: Current Status
In the process of final editorial review
  Rev 1.0 release set for June 20, 2002.
  Available on IBIS website under the “Connector Info” link
Major changes/enhancements since the last report:
  Removed auto pinmap functionality, removed redundant info, streamlined keyword organization.
  Added the “G” to LRGC matrices
  Added support for non-regular interconnect (nodal path descriptions)
  Added support for freq dependent transmission line parameters (via S-parameters)
“Connector” spec now encompasses both connectors and package interconnect!

## Slide 3: Overview
A .icm file supports one (1) interconnect family
  Each interconnect family includes one or more individual interconnect descriptions
Individual interconnect descriptions include the following:
  Basic info like manufacture, description, mating conditions, model limit (max slew rate), etc.
  The model type (MLM, SLM or S-parameter).
  A path description, either ‘tree’ or ‘nodal’, that describes how the matrices are interconnected.
  Where applicable, info that allows pin swathing.
  Mapping between external pins/node of interconnect and the rows of the matrix.
Matrixes contain either LRGC or S-parameter data (via external Touchstone file).

## Slide 4: Overview (cont.)
Specification supports three different types of interconnect:
  Regular (no pins missing) rectangular connectors
    Swathable, can use either path description
  Regular, non-rectangular connectors
    Not swathable, can use either path description
  Irregular connector/interconnect
    Not swathable, must use nodal path description
Nodal vs. Tree type path descriptions
  [Tree Path Description] cascades matrices back to back, each row of matrix corresponds to a single pin, same # of pins front and back
  [Nodal Path Description] connects matrices via explicit node names, can build arbitrary structures with missing pins, different size matrices, etc.

## Slide 5: MLM and SLM Models
MLM = Multi-line (coupled) models
  Use for including pin-to-pin coupling
  Spec specifies partial inductance values and Maxwell capacitance values in matrix
  Intent is to support xtalk and return path simulations.
SLM = Single lines (un-coupled) models
  SLM_EvenMode/OddMode/Quiescent models have documented ground return paths(!)
  SLM_General only documents GSR ratio
  Spec specifies loop inductance in matrix
  The intent is to ‘bracket’ interconnect performance under specific conditions
S-parameter models
  By definition are coupled models, unused terminals terminated by reference impedance

## Slide 6: Length vs. Multiplier Matrix Specification
Path description specifies how to interpret the data in an RLGC matrix
  Len = per-unit-length, intended for distributed transmission line elements. Expansion by multiplication.
  Mult = lumped elements, intended to be rendered into circuit netlists. Expansion by cascading sections.
  S-parameter is always lumped, non-cascade
[Derivation Method] keyword in matrix section provides a cross reference
Two styles for two different purposes…
  Per unit length results from a 2-D extraction of parallel structures (I.e. package traces)
  Unit multiplier results from a 3-D extraction of non-regular structure (I.e. connectors)