## Slide 1: Multi-Lingual Modeling Applications and Issues Bob Ross June 13, 2002 IBIS Summit Meeting New Orleans, Louisiana
Notes: NOTES: I can’t see what I am typing when I enter the presenter’s
name & title.
This is an issue with PowerPoint. Here is the current work around, not the most elegant solution but it works.
- Select the area/
- Type a word
    - Highlight the word.
    - Change font color to back.
    - Finish typing
    - Select all
    - Change font color to white.

## Slide 2: Benefits of Multi-Lingual Support
Model advances beyond IBIS
  True differential buffers, current buffers
  SCSI driver/terminator advances
  More detailed over-clocked buffer detail
  SSO effects and gate modulation
  Code based modeling
Die interconnect advances
  Die interconnect and complex package modeling
  External voltage rail, power integrity interactions
  External buffer strength control
Closer digital and analog analysis (AMS)

## Slide 3: Application: Die (left) & Package (right)

## Slide 4: Why/How Multi-Lingual Modeling?
Leverages existing IBIS, Spice, VHDL-AMS, Verilog-AMS
  Still use IBIS where appropriate
  Extension uses IBIS for Pinout, Pkg., Info. & Spec.
  Executes external code files
Multi-lingual EDA tools from many companies
  Mentor, Cadence, Synopsys (Avanti), …
Faster response to industry - IBIS & few keywords
  [External Model]: Buffer level external models
  [External Circuit]: Die circuitry
  [Node Declarations], [Circuit Call]: Interconnects

## Slide 5: Digital (logic) and Analog Ports and Reference Models for I/O Buffers

## Slide 6: Existing IBIS or [External Model]s
[External Model] under [Model] <model_name>
[External Model]
  Language <selection>
  Corner <typ,min,max files and model names>
  Ports <analog and digital port list>
  D_to_A <digital signals to Spice ramps>
  A_to_D <Spice thresholds to digital signals>
Internal or external reference supplies
Direct connection or interconnection syntax

## Slide 7: Controlled Model & [External Circuit]
[External Circuit] <circuit_name>
  Language <selection>
  Corner <typ, min, max files, names>
  Ports <port list>
[External Model] and [External Circuit] connected using internal and die nodes:
[Node Declarations]
  <internal node list>
[Circuit Call] <model or circuit name>
  Port_map <port to node mapping>
  Cell_port <die node>

## Slide 8: Proposal Includes More
True and single-ended Differential buffers
Series elements
Predefined signal names support all combinations
  IBIS [Model] to die nodes (existing standard)
  IBIS [Model] through [External Circuit]
  [External Model] to die nodes
  [External Model] through [External Circuit]
  [Circuit Call] required for last three cases, optional for first, but its usage overrides conflicting IBIS connections

## Slide 9: Two Examples
SSO Impact on Timing with Lossy Die Power Net
  Opposite phase adjacent drivers: power burst, less delay
  In phase adjacent drivers: power droop, more delay
Integrated Circuit Electromagnetic Model (ICEM) from Europe
  Core noise model for statistical currents drawn by internal clocks added to power nets for EMI current distributions

## Slide 10: Adjacent Drivers Out of Phase

## Slide 11: Adjacent Drivers In Phase

## Slide 12
5. Emission Model with IOs
Add IBIS I/O data
Zsub: basically a 1-10 serial resistance
Cio : decoupling capacitance for IO supply
IO block: reuse of IBIS
Ib
Rvdd
Core VDD
Core VSS
Cd
Lvdd
Rvss
Lvss
Cb
I/O
Zsub
I/O VSS
I/O VDD
Cio

## Slide 14: Some Issues and Discussions
Why [External Model] and [External Circuit]?
  Several syntax differences
Why [Node Declarations]?
  Supports variable declarations in some languages
Format of tables and names?
  Up for review and discussion
Cell_port usage
  Associate displaced model to pins
Interaction with other keywords
  Rules can be made more exclusive

## Slide 15: Implementation/EDA Vendor Issues
How to isolate nets of interest
  Small set of dedicated models
  Method of selecting nets of interest
Control of stimulus
  Through interconnection with other nets in analysis
  Built in generators
  Controlled in sync. with a model as an [External Model]

## Slide 16: What’s Next?
BIRD75.1 to describe details are now being reviewed
Planned for vote and IBIS Version 4.1 release