## Slide 1: IBIS 4.1 Status and Update Lynne Green IBIS Summit June 2003

## Slide 2: IBIS 4.1
IBIS 4.0 status
IBIS 4.1 status
Approved BIRDs
Open BIRD
Next steps

## Slide 3: IBIS 4.0 Status
Voted in July 2002
Parser expected Q3/03
IBIS 4.0 contains
  11 new BIRDS
    Expanded input threshold specifications
    Golden waveforms
  The usual parser bug fixes

## Slide 4: IBIS 4.1 Status
First pass document
http://www.eda.org/pub/ibis/wip/ver4_1a.ibs
Five approved BIRDs
  BIRD75.8, BIRD77.2, BIRD78.1, BIRD80.1, BIRD81.1
  The usual parser bug fixes
One open BIRD
  Not expected to be in IBIS 4.1

## Slide 5: Five Approved BIRDs BIRD75.8
Multi-lingual support
First submitted: 3/29/02
Approved: 1/10/03
Supports SPICE 3f5, Verilog-AMS, VHDL-AMS
External model files (subcircuits)
No parameter passing into model files

## Slide 6: Five Approved BIRDs BIRD75.8
  |-- [Component]
  | ...
  |-- [Node Declarations]
  |-- [End Node Declarations]
  | ...
  | ...
  |-- [Circuit Call]
  |-- [End Circuit Call]
  | ...
  |-- [Model]
  | | ...
  | |-- [External Model]
  | |-- [End External Model]
  | | ...
  | ...
  |-- [External Circuit]
  |-- [End External Circuit]
  | ...

## Slide 7: Approved BIRDs BIRD77.2
New model types
  Input_diff
  Output_diff
  I/O_diff
  3-state_diff
New timing subparameters
  Rref_diff
  Cref_diff
_________
| |
| |\ | Rref
|Driver| \|--o---o---o----/\/\/\--o Vref
| | /| | | |
| |/ | | | === Cref
|_________| / | |
\ | GND
Rref_diff / ===
_________ \ | Cref_diff
| | | |
| |\ | | | Rref
|Driver| \|--o---o---o----/\/\/\--o Vref
| | /| |
| |/ | === Cref
|_________| |
GND

## Slide 8: Approved BIRDs
BIRD78.1
  Extend line length to 120 char
BIRD80.1
  Add ext_ref as new [Pin Mapping] column
BIRD81.1
  Clarification of models in [Pin] section
  Using [Series Pin Mapping] description earlier

## Slide 9: Open BIRDs
BIRD 74.4, EMI Parameters
  Add EMI parameters to IBIS
  First submitted, March 19, 2002
  Discussions in IBIS Open Forum
  Several revisions

## Slide 10: Next Steps
IBIS Futures Committee edits rough draft
Draft version of 4.1 goes to IBIS Open Forum
Open Forum discusses draft
  Revisions
  Additions
  On third meeting, can come up for a vote
Parser development (bidding, funding, coding)
Submit to EIA as IBIS 656-B

## Slide 11: Examples of AMS models
Dan Fitzpatrick and Ira Miller, “Analog Behavioral Modeling with the Verilog-A Language”, Kluwer Academic Publishers, 1998. Includes software and models on CD.
http://www.eda.org/verilog-ams/htmlpages/examples.html
Lynne Green, DesignCon 2003 Summit.
Arpad Muranyi, today.

## Slide 12: Late-breaking News
Business Wire, June 2, 2003 Accellera Approves Four New Design Verification Standards
NAPA, Calif.--(BUSINESS WIRE)--June 2, 2003--Accellera, the electronics industry organization focused on language-based electronic design standards, today announced that its Board and Technical Committee members -- systems, semiconductor and design tool companies -- have approved four new standards for language-based design verification. The new Accellera standards include Property Specification Language (PSL) 1.01, Standard Co-Emulation Application Programming Interface (SCE-API) 1.0, SystemVerilog 3.1 and Verilog-AMS 2.1.