## Slide 1
Signal Integrity Software, Inc.
IBIS Models @ 1.25GHz and Beyond
DesignCon East June 23, 2003
Bob Haller
Barry Katz
Kevin M. Fisher

## Slide 2: IBIS models @ 1.25 Ghz
System designs challenges
  Interconnect
    Etch
    Connectors
  Return path
    SSO
    Vias
    Splits and Swiss cheese planes
  High Speed Links
    For example - LVDS
Can IBIS be utilized ?

## Slide 3: LVDS Low Voltage Differential Signaling
Higher signaling speeds
Lower voltage swing
Lower power consumption
Less susceptible to common-mode noise
Reduced EMI

## Slide 4: Challenges creating IBIS model @1.25Ghz and Beyond
IBIS specifically designed for single-ended I/O buffers
Behavioral (IV) curves show current as a function of voltage applied to pad
Current of LVDS buffer dependent on voltage at both pads, and common-mode voltage (vcm)

## Slide 5: Extracting & Using LVDS IBIS Models

## Slide 6: Generating an LVDS IBIS Model
Step 1: Find vcm of device
Drive into expected loading conditions &
topology to obtain

## Slide 7: Generating an LVDS IBIS Model
Step 2: Sweep vout on one output pad, keeping vcm constant throughout sweep
Step 3: Extract the curves, convert to IBIS format

## Slide 8: Using an LVDS IBIS Model
Two instantiations of extracted model: one for true, one for complement
Complement stimulus 180° out of phase with true stimulus

## Slide 9: Accurate IBIS Model @ 1.25GHz HSPICE vs. IBIS
SPI4 interface: 1.25GHz, target pad, VDDQ=2.375

## Slide 10: Issues
Some simulators modify “non-traditional” IV curves
  IV curves not passing through (0, 0)
LVDS IBIS models are accurate only when same VDDQ model was generated with is used
  Changing VDDQ leads to inaccurate results
Some LVDS IBIS models accurate only under same Load conditions (i.e. 100 Ohms)

## Slide 11: Inaccurate IBIS Model Effect of Changing VDDQ
SPI4 interface: 1.25GHz, target pad, VDDQ=2.325,
Model generated w/VDDQ=2.375

## Slide 12: Issues
LVDS IBIS models assume constant Vcm
  Must generate multiple models for different values of vcm to obtain consistent accuracy driving different loads and topologies
Device asymmetry will affect accuracy of model
  Model generated for both pads assumes perfect driver symmetry
  Etch lengths of nets in differential pair matched

## Slide 13: Conclusion
We can generate accurate IBIS models @ 1.25 Ghz and beyond !
It takes significant effort and attention to detail
  You must know operating conditions and application (I.e. VDDQ and termination values).
  You must understand and test in target simulator
Improper use of IBIS models can & will lead to inaccurate results
Improper built IBIS models exist & will lead to inaccurate results.

## Slide 14
Signal Integrity Software, Inc.