## Slide 1
IBIS Interconnect Modeling Specification (ICM) Status
By
Michael Mirmak
Intel Corporation
IBIS Summit at DesignCon East 2003
June 23, 2003

## Slide 2: Agenda
ICM Refresher
  Purpose
  Structure
  A Partial Example
Recent History
Changes in Final Draft 1.0
Short Term Future
The Longer View
  Potential technical improvements
  Touchstone® issues
  Cookbook
Summary
Backup
  S-parameter background
  Improved Example Model

## Slide 3: ICM Refresher
ICM = IBIS Interconnect Modeling Specification
Purpose: to establish a human-readable standard format for exchanging interconnect modeling data
  “Interconnect” can be connector, cable, PCB traces or even an IC package
ICM uses a two-part format:
  Description of model in terms of one or more sections with terminals mapped to named pin/node lists
    Nodal arrangement with explicit interconnections
    Tree arrangement with implicit interconnections
  Electrical data describing each section
    RLGC matrix data
    S-parameter data (external Touchstone® file)

## Slide 4: A Partial Example
Pins
Tree Description
Nodal Description
A more formal example is available
at the end of this presentation…
[Begin ICM Model] MyModelExample7
ICM_model_type MLM
[Nodal Path Description]
Model_nodemap Port1
N_section (A1 A2 A3 A4 A5 11 12 13 14 15) Len=1.0 A
N_section (11 12 13 14 15 21 22 23 24 25) Len=1.0 B
N_section (21 22 23 24 25 31 32 33 34 35) Len=1.0 C
N_section (31 32 33 34 35 s1 s2 s3 s4 s5) Len=1.0 D
N_section (s1 s2 s3 s4 s5 F1 F2 F3 F4 F5) Len=1.0 F
Model_nodemap Port3
N_section (s1 s2 s3 s4 s5 E1 E2 E3 E4 E5) Len=1.0 E
Model_nodemap Port2
[End ICM Model]

## Slide 5: ICM History
Initial concept developed 1995 - 1997
  IBIS Connector/Futures Subcommittee
Sporadic revisions 1999 – 2002
Internal Draft 1.0 released Sept. 19, 2002
Committee Internal Drafts 1.0a – 1.0g
Final Draft 1.0 released publicly May 16, 2003
  See IBIS web site under “Connector Info”

## Slide 6: What Changed in Final Draft 1.0
Over 63 issues formally logged since Sept. 2002
  More than two dozen additional small issues resolved
Most changes were editorial
  Spelling, punctuation and grammar
  Standardization to improve software parsing
  Name changes for consistency with IBIS 4.0
Some technical limitations established
  RLGC and S-parameter sections not permitted within the same model (allowed in the same file)
  S-parameter data only to be used with [Nodal Path Description] keyword
  Implicit use of single-ended ports for S-parameter data
More details under “Long-Term Issues”

## Slide 7: Short-Term Future
ICM now in IBIS Open Forum Review
  Officially introduced at May 30 meeting
  Minimum of three Open Forum meetings must consider the document before an official vote
  Parser in development – tentatively available for initial testing after Open Forum approval
Interested parties strongly encouraged to provide feedback and test models
  Feel free to provide or construct ICM models using “favorite interconnects” for testing
  Example: package which is inconvenient or impossible to describe using IBIS .PKG

## Slide 8: Future Improvements
After 1.0 is approved by the Open Forum, several technical issues may be considered for future revisions
  Allow multiple types of data within a single [Begin ICM Model]/[End ICM Model] pair
    Example: Include S-parameter AND RLGC data
  Include frequency-dependence in RLGC data
    Example: Matrix parameters for 1 MHz, 100 MHz, etc.
A formal “BIRD-like” procedure will be established to document and process change proposals

## Slide 9: Long Term Issues
Using ICM with IBIS models
  No explicit links to IBIS in ICM or vice-versa
  Implied that data files are linked through tools
  IBIS or ICM BIRDs for cross-referencing?
Touchstone® and mixed-mode S-parameters
  ICM maps section nodes to ports
  Ports are implied to be single-ended
  Touchstone® format establishes regular data format
    Comments, options, frequency and S, Y, Z, H, G data
    Interpretation of data assumes single-ended (S12, etc.)
  Mixed-mode (SDD12, SCD22, etc.)?
    Some authors release mixed-mode Touchstone® files
    Data format is standard, but interpretation is not
  New Touchstone needed for mixed-/multi-mode?

## Slide 10: Long Term Issues
ICM cookbook needed!
  Need to provide guidance to model builders
  Take approach from 1997 IBIS 2.1 Cookbook
Cookbook topics
  Summary of keywords
  Explanation of key concepts
    Ground references
    Return paths
  Summary of best known modeling methods
    Measurement vs. simulation
  Several complete examples

## Slide 11: Summary
ICM is an evolution of IBIS package and PCB modeling formats
Official 1.0 pending Open Forum approval
  Please review the ICM Final Draft
  Comments and test models are appreciated!
Thanks to the Connector Subcommittee
  John Angulo Arpad Muranyi
  Kelly Green Augusto Panella
  Lynne Green Stephen Peters
  Bob Ross
and to the many other individuals
and groups who contributed!

## Slide 12
Questions and
Free Discussion

## Slide 13
BACKUP

## Slide 14: S-parameter Data Formats
Single-ended
  Data defined per node + reference: S12, S21
Mixed-mode (usually differential pairs)
  Common & Differential excitation and response
  Data defined per node pair: SDD12, SDD21
  Data defined per node pair + reference: SCC11
“Multi-mode” (not covered by any spec.)
  Excitation and response for n-node groups
  Example: SD12C458

## Slide 15: S-parameter Data Formats
Single-ended
Mixed-mode (usually differential pairs)
“Multi-mode” (not covered by any spec.)
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
N

## Slide 16: Touchstone® Variations
Spec. defines data placement convention
Many model authors use general format, but define data placement through comments
# MHz Y MA R 50
! Data is Freq SDD11 SDD12 SDD21 SDD22
! SCC11 SCC12 SCC21 SCC22
10 1.7784797E-01 -80.863279 1.7863314E-01 99.053834
3.8696562E-02 104.003821 3.8770346E-02 -76.072136
2.4735915E-07 151.207214 2.4624379E-07 -29.142657
3.1760443E-07 -166.479698 3.1562825E-07 13.585246
4-port network description
<frequency value> <N11> <N12> <N13> <N14>
<N21> <N22> <N23> <N24>
<N31> <N32> <N33> <N34>
<N41> <N42> <N43> <N44>

## Slide 17: ICM Example
[Begin Header]
[ICM Ver] 1.0
[File Name] iconm_hdi_202.icm
[File Rev] 1.0
[Date] May 29, 2003
[Source] Results from field simulation
[Notes] This is a test model only.
[Disclaimer] This information is for modeling purposes only, and is not guaranteed.
[Copyright] Copyright 2003, XYZ Corp.,
All Rights Reserved
[Support] http://www.VendorNameIbisModels.com
[Redistribution] Yes
[Redistribution Text] This file is freely redistributable.
[End Header]

## Slide 18: ICM Example (2)
[Begin ICM Family] High_Speed_Interconnect
[Manufacturer] XYZ Incorporated
[ICM Family Description]
High Density square pin connector for use on IEEE 99999 buses.
|====================================================================
[ICM Model List]
| Name Mating Min_Slew_Time Image
|--------------------------------------------------------------------
My ModelExample3 Mated 100ps HDI_202_Mated.jpg
|HDI_202_UnMatedA Unmated_side_A 100ps HDI_202_UnMatedA.jpg
|HDI_202_SMT_to_Cable Mated 25ps HDI_TEST_202_Mated.jpg
|HDI_202_SMT_to_ThruHole Mated 25ps HDI_202_Mated.jpg
|====================================================================

## Slide 19: ICM Example (3)
[Begin ICM Model] MyModelExample3 | Has a stub fork!
ICM_Model_Type MLM
[Begin ICM Model Description]
High Density 0.1 center square pin with PCB effects
[Tree Path Description]
Model_PinMap Baseboard_side
Section Mult=1 SectionA
Fork
Section Mult=1 StubSection1
End_fork
Section Mult=1 SectionB
Model_PinMap Output_side
[End ICM Model]
| SectionA SectionB
| Baseboard_side >---------+--------< Output_side
| |
| | StubSection1

## Slide 20: ICM Example (4)
[ICM Pin Map] Baseboard_side
Pin_order = Row_ordered
Num_of_columns = 4
Num_of_rows = 2
Pin_list
|Pin Name
A1 PERR#
A2 STOP
A3 AD12
A4 AD15
B1 STOP
B2 GND
B3 PAR
B4 GND
|[ICM Pin Map] Output_side omitted for clarity
[End ICM Family]
A1
A2
A3
A4
B1
B2
B3
B4

## Slide 21: ICM Example (5)
|-----------------------------------------------------------
[Begin ICM Section] SectionA
[Derivation Method] Lumped
[Inductance Matrix] Full_matrix
[Row] 1
3.04859e-07 4.73185e-08 1.3428e-08 6.12191e-09
1.74022e-07 7.35469e-08 2.73201e-08 1.33807e-08
[Row] 2
3.04859e-07 4.73185e-08 1.3428e-08 7.35469e-08
1.74022e-07 7.35469e-08 2.73201e-08
|.
|.
|.

## Slide 22: ICM Example (6)
[Capacitance Matrix] Sparse_matrix
[Row] 1
1 2.48227e-10
2 -1.56651e-11
5 -9.54158e-11
6 -7.15684e-12
[Row] 2
2 2.51798e-10
3 -1.56552e-11
5 -6.85199e-12
6 -9.0486e-11
|.
|.
[End ICM Section]
| SectionB and StubSection1 omitted for clarity
[End]