## Slide 1: The IBIS Model Review Committee
Lynne Green
Green Streak Programs
lgreen22@mindspring.com

## Slide 2: The IBIS Model Review Committee
Process
Current members
Review of a typical model
Relationship to IBIS Quality Document

## Slide 3: The IBIS Model Review Process
Model Received by EMAIL
Quick Sanity Check
IBIS 3.2 or 4.0 Parser
File Distributed to
Committee Reviewers
Reviewers Respond to
Model Originator

## Slide 4: Current Committee Members
Chair: Lynne Green, Green Streak Programs
EDA Reviewers
  John Angulo, HyperLynx/Mentor Graphics
  Lance Wang, Cadence Design Systems
  Michael Schraeder, Zuken
  Robert Haller, SiSoft
  Weston Beal, Mentor Graphics
EDA companies test models with their products/tools.
Reviewers keep models confidential.

## Slide 5: Review of a Typical IBIS Model
Start with IBIS parser
Check components & pins
Check selected models in the IBIS file
Optional: check component and models against data sheet

## Slide 6: Review of a Typical Buffer Model
Graphical check of data tables
  Monotonicity
  Separation of clamp tables
  V-t table settles and ends
Check data
  Driver: Vmeas, Cref, Rref, Vref
  Receiver: Vinh, Vinl
  Temperature: Typ > 25 C.

## Slide 7: Review of a Typical Model: Waveforms
Notes: <number>
<footer>
<header>
<date/time>
What problems do you see here?
The V-t curves actually look nice, although a shorter end time could have been used.
If you were to look closely at the transition regions, you would notice that there are less than 10 points. A better model would have more points in the transition region and fewer outside the transition region.

## Slide 8: Review of a Typical Model: Waveforms
Notes: <number>
<footer>
<header>
<date/time>
What problems do you see here?
The V-t curves actually look nice, although a shorter end time could have been used.
If you were to look closely at the transition regions, you would notice that there are less than 10 points. A better model would have more points in the transition region and fewer outside the transition region.

## Slide 9: Review of a Typical Model
Run other checks as time permits
  Example: [Driver Schedule]
  Items from IBIS Quality checklist
Translate
  Example: Cadence DML
  Check error/warning messages
Simulate ! ! !
  Input mode
  Output mode
  Sanity check simulation waveforms

## Slide 10: Review of a Typical Model: Simulation
Notes: <number>
<footer>
<header>
<date/time>
The acid test is running an actual simulation, and comparing simulation results with what you would expect.
In this model, the simulation can be checked for the “DC” levels at the beginning and end of each transition, as well as the transition time. Note that rising and falling transition times should match the times given for the [Ramp] parameter.

## Slide 11: Relationship to IBIS Quality Document
Input from reviewers on the Quality Committee
Problems seen in models
  Reviewed models
  Released models
Quality checks used by reviewers
  Feedback from reviewers to Quality Committee
  Recommendations to model originators

## Slide 12: Relationship to IBIS Quality Document
Quality checklist has proven helpful
for model review
Many thanks to both Committees 