## Slide 1: Simultaneous Switching Noise in IBIS models
Ambrish Varma
akvarma@ncsu.edu
Prof. Paul Franzon, Prof. Michael Steer
IBIS SUMMIT
Design and Automation Conference 2004
June 8, 2004

## Slide 2: Outline
Background
IBIS V Spice
  Buffer Cct
  B Model
  Results
IBIS V Spice V Spline
  Spline Functions and Finite Time Difference approximation
  Methodology
  Results
  Conclusion
Future Work

## Slide 3: Background
s2ibis1 and s2ibis2
SSN issues.
IT table and other proposed solutions.

## Slide 4: Comparing SPICE and IBIS
Cascaded Driver
Non-Inverting

## Slide 5: Comparing SPICE and IBIS..
Each driver connected to a lossless 25 ohms T Line.
25 ohm terminations used.
3 drivers given simultaneously switching inputs
4th driver kept quiet.
Power/Ground supplied through pin parasitics.
Quiet Line
Pkg Parasitics
Power
Wire Bond and Pin Parasitics
Wire Bond and Pin Parasitics
T Line

## Slide 6: B Element in HSPICE
  Sub-Circuit of driver is recreated using IBIS model.
  To simulate power/ground bounce and SSN, internal Power Sources are not used.

## Slide 7: Comparing SPICE and IBIS
s2ibis3
IBIS MODEL
B Element (Hspice)
Reads in IBIS model of buffer from *.ibs file
Construct Equivalent circuit of 4 drivers

## Slide 8: Output from Drivers
Output in the Switching Drivers
Output in the Quiet Driver

## Slide 9: Power/Ground Bounce
Power
Ground

## Slide 10: Spline Functions and Finite Difference Approximation1
BLACK BOX
  Knowledge of Internal circuitry not necessary.
Output load independent
Static Characteristic Modeling + Dynamic Characteristics (by capturing the previous time instances)
Macro-Modeling of Non-Linear I/O drivers using Spline Functions and Finite Time Difference Approximation, B Mutnury,
Jim Liibous and Madhavan Swaminathan, EPEP 2003.

## Slide 11: Spline Functions (cont)
Non-Linear relation is drawn between driver O/P current and voltage.
f1 and f2 are submodels relating O/P currents and voltages when driver is set high(f1) and low(f2) and have both static and dynamic information
Static values can be obtained using DC sweep and using nth order cubic spline.
C
R =1
E
fn(k) = Anmvom(k) + Anm-1vom-1(k) +…

## Slide 12: Spline Functions (cont)
Dynamic values can be obtained by including the previous time instances of the driver output current.
W1 and W2 are used for transitioning from 1 logic state to the other. They are obtained by estimating submodels (f1 and f2) for 2 loads and by linearly inverting
and are represented as PWL voltage source.
C
R =1
E
=
-1

## Slide 13: Static Modeling Using Spline Driver Output Current Vs Time
STATIC MODEL
(Using 3rd Order Cubic Spline)

## Slide 14: Capturing Dynamic Behavior
Spline Function with Finite Time Difference
(Using 1 previous time instance)

## Slide 15: Spline Modeling Spice Netlist
Spice Macromodel generated using VCVSs (E elements) and CCCs (F elements).
  Static Characteristics can be represented using VCVS
  Dynamic Characteristics represented using state equations
  Non-Linear relation between driver o/p current and voltage is now a subcircuit.
    .subckt driver1 out1 gnd
    …
    ...
    .ends (driver1)

## Slide 16: Comparing SPICE, IBIS & SPLINE
Spline method is complex and no IBIS like automation exists.
The models resulting from IBIS, and SPLINE are compared with SPICE simulation of the transistor model.

## Slide 17: Comparing SPICE, IBIS & SPLINE Ground Bounce
Spice
IBIS
SPLINE

## Slide 18: Comparing SPICE, IBIS & SPLINE Output Comparison
Spice
IBIS
SPLINE

## Slide 19: Comparing SPICE, IBIS & SPLINE
IBIS and Spline method compared with Spice
Simulation of the Transistor Model

## Slide 20: Comparing SPICE, IBIS & SPLINE Conclusions
SPLINE Pros
  More accurate than IBIS
  More general than IBIS
    Mathematical
SPLINE Cons
  Not automated
  Computationally intensive
  Complex to implement
  Slower

## Slide 21: Questions
Is it worth having a 50% improvement in SSN simulation accuracy?
  How much is speed valued when IBIS is used?
Can SPLINE models be generated using measurements?

## Slide 22: Future Work
A combination of Spline method and IBIS is under study.
The integrated solution would include
  the accuracy and the mathematical background of the spline methodology and
  the automation and the simplicity of IBIS.

## Slide 23: Acknowledgments
Prof. M. Swaminathan and B. Mutnury, Georgia Instt. of Technology for sharing code to model using Spline functions and Finite Time Difference Approximation