## Slide 1: I-T Tables and BIRD42.3 Revisited
Bob Ross
Teraspeed Consulting Group
IBIS Summit Meeting
Design Automation Conference 2004
San Diego, California
June 8, 2004

## Slide 2: Some IBIS Summit Presentations Regarding Power Rails for SSN and I-T
See IBIS home page Articles, summits on the eda.org IBIS summits site
Raymond Chen, Sigrity: Feb. 2004 (add Cdie)
Bernhard Unger, Siemens: Jan. 2000 (adds Cpre and adjustment for rail collapse)
Ambrish Varma, NCSU: June 2004 (simultaneous switching noise and rail collapse)
Norio Matsui, Applied Simulation Technology: Jan. 2001 (LSI power and ground model for EMI simulation with internal clock and paths)
Etienne Sicard, INSA: Sept. 2001, Sebastien Calvet INSA Jan. 2002 (chip core I-T model for EMI)
  I-T source for supplies derived from statistical switching model simulations (with AMS or SPICE or simplified SPICE)
  Part of ICEM model and IC-Emit freeware (Feb. 20, 2004)
  Can be modeling using multi-lingual extensions
C. Kumar, Cadence: Jan., Feb. 1998, Bob Ross Feb. 1998: (I-T tables in buffers and BIRD42.3)

## Slide 3: Adding Cdie (Chen, February 2, 2004)

## Slide 4: Chen, Continued

## Slide 5: Rail Collapse Adjustment (Unger, January 31, 2000)

## Slide 6: Unger, Continued

## Slide 7: Unger, Continued

## Slide 8: Core Emission I-T Model for EMI (Calvet, Jan. 28, 2002)

## Slide 9: Core Model I-T Emission Models as Multi-Lingual SPICE Extension of IBIS

## Slide 10: BIRD 42.3 - IBIS 2.1 Buffer Model
Package
Fixed Clamps and C_comp
Drivers

## Slide 11: V-T Tables and Fixture Loads to get Ku(t), Kd(t) for Rise, Fall Edges
Recommended Loads:
50  to Vcc
50 to Gnd

## Slide 12: BIRD42.3 Proposal (V-T and I-T tables)
Ipulldown_reference(t)
(0, 1, or 2 current tables allowed)
Ipullup_reference(t)

## Slide 13: Current Definition Problem? EDA Spec., Processing Ambiguity
Ipulldown_reference(t)
(0, 1, or 2 current tables allowed)
Ipullup_reference(t)

## Slide 14: BIRD42.3 Assumptions and Limitations
Adds V-T and I-T PAIRS for a given fixture load
  Under [Rising Waveform] or [Falling Waveform] table
    Keep V-T table and its fixtures
    [Pulldown Reference Current], [Pullup Reference Current] tables (None, both, or either - such as one easiest to isolate)
    Could support Open_drain, Open_source and ECL models
Currents might need to be separated from clamps or other current paths in the model
  Permanent (internal terminator “clamps”)
  Individual capacitance to each rails
  Very complex for tools to automatically do this

## Slide 15: Some Format Considerations
Referenced to driver rails since clamps are optional, and clamp currents hard to isolate
Extension limitations may exist
  Driver Schedule – rails not necessarily common or inherited, nor currents easily allocated to scheduled models
  Submodels – same rails, but triggered internal behavior needs triggered I-T data
  True differential buffer current allocation not considered
  ECL Pullup Reference Current allocation/algorithm issue

## Slide 16: EDA Tools: Several Choices for Over-specified Cases
Voltage based solution option
  Use the V-T table information first for V-T data matching via existing Ku(t), Kd(t) extraction methods
  May not capture as accurately the rail currents
Current based solution option
  Use the current information first (more direct solution of Ku(t) and Kd(t) with excess common “crowbar” currents)
  But not match the V-T data as well
Augmented model for voltage and current matching
  Adds Idelta(…) and Vdelta(…) variables for more matching options and strategies
    (E.g., match V-T tables, then match currents with Idelta)
  Idelta(), Vdelta() could be a function of Iu and Id currents
  More research needed

## Slide 17: Augmented Model (Ross, Feb. 26, 1998)

## Slide 18: I-T Extraction Issues
SPICE based (most practical)
  Still must carefully isolate rail currents and then post-process them to fit topology
  Can use ideal current sense mechanism (0 V voltage sources)
  Still may deal with fast current edges and spikes
  Best R_fixture, V_fixture choices need to be investigated for overall accuracy (V_fixture = GND, Vcc, Vcc/2, etc.)
Measurement based (many issues and may be impractical)
  Includes the package
  Current probe bandwidth & impedance vs. 50 ohm measurements
  Or standard 1 ohm test load distortion
  Several buffers on same power line
  Unrelated currents from non-driver circuits

## Slide 19: Package Model for Supplies (not explicit in IBIS)
R_pin - L_pin - C_pin
  Implied, but puts C_pin across voltage source
  Could be distributed model (small T-line)
R_pin - C_pin – Lpin
  C_pin to reference rail, to ideal GND or across L_pin to Vcc
  Moves C_pin from rail

## Slide 20: Summary and Observations
BIRD42.3 explained
  Issues and compromises to fit in IBIS
  EDA simulation options
Other approaches given
  SSN model extensions
  Core I-T models for ICEM
What is the problem?
  Simultaneous switching noise of selected buffers?
  Board power distribution issues and internal core noise?
Do I-T tables help solve the problem?
  I-T IBIS buffer extension or other proposals?
  Multi-lingual extensions?
  EDA tool support?