## Slide 1: IBIS Summit @ DAC 2005: Library Characterization & Modeling: Issues, Recommendations and Possible Solutions June 14, 2005
Sumit DasGupta, PhD
Vice President, Technology
Silicon Integration Initiative (Si2)
Austin, TX, USA
H. John Beatty
Senior Technical Staff Member
IBM Corporation
Hopewell Junction, NY, USA

## Slide 2: Sponsors
Si2’s Design Technology Council (DTC) |  | 
Ericsson | IBM Corporation | Philips Semiconductors
Freescale Semiconductor | Infineon AG | Sun Microsystems
Hewlett Packard | LSI Logic | Intel

## Slide 3: Reality: 90nm onwards!
All tough problems at 130nm are still here,… and there are some new ones at 90nm…

## Slide 4: Challenges: 90nm onwards!
Significant divergence between predicted & measured performance due to variability in process & temperature
  Requires more complex and accurate libraries, including models for interconnect
Chips designed with multi-Vt and multi-voltage regions
  Requires multiple libraries
Semiconductor processes will get more complex at 65nm…and beyond… which will lead to…
  Even more complex libraries

## Slide 5: Objective
Increased accuracy to silicon at 90nm and 65nm
Extendable to future technology nodes
Support new capabilities (e.g. statistical timing)
Maintain consistent modeling methodology
Modeling & characterization environment:

## Slide 6: Issues
Accuracy/consistency of library models
Gap between requirements and capability
Cost/Expertise needed to build accurate libraries
Existing formats cannot express modeling needs
Design tools closely “linked” to library

## Slide 7: Model Accuracy
Table lookup (piecewise linear)
Arbitrary polynomials
Current source models
User definable equations / models
Consistency across libraries
Requirements:

## Slide 8: Capability Gap
Delay, power & signal integrity analysis
Multiple voltage libraries
Statistical modeling of process & other variations
Electromigration
Requirements:

## Slide 9: Library Cost…
Automate characterization & modeling flow
Remove manual processes
Automate curve-fitting & model generation
Support hierarchical characterization
Requirements:

## Slide 10: Library Format
Unambiguous syntax and semantics
Supported by popular industry tools
Independent of any specific tool
Community control / evolution
Requirements:

## Slide 11: Tool “Linkage”
Separation of tools from timing data / models
API interface to modeling information
Consistent results across all tools
Silicon calculations defined by library provider
Requirements:

## Slide 12: Roadmap
Statistical timing
Improved accuracy
  Timing and noise
  Leakage and total power
Temp variation
Library support for:

## Slide 13: Modeling System
Characterization System
Simulator Results
Curve fit & model gen.
Macro block model gen.
Model Compilation
IEEE 1481v2 Rules
Tool Flow
Dynamic
Static
Legend:
In-Scope
External
Design DB
Process Technology, BSim, and Spice Decks
ECSM/CCS/.lib formats
Simulator control system

## Slide 14: Create New Coalition
Technology
contributions
Define
standard interfaces
Develop characterization
subsystem
Develop migration
support
EDA vendor
adoption
Time
Collect
Requirements
Start Coalition
Modeled after OpenAccess Coalition

## Slide 15: OMC Structure
Open Modeling Coalition
Si2 members in good standing
Chair, Vice-Chair, Secretary
Owners of reference flow and overall implementation
Majority voting for decisions
Technical Steering Group
Upto 12 members
Led by 2 chief architects
2/3 super-majority voting
Owns roadmap, implementation plans
Charters working groups
Appoints champions for working groups
Working Groups
Created and disbanded by TSG
Champion from TSG is a member
Participants are from coalition
Chair appointed by TSG
Initial list of WG’s:
  Interface to modeling subsystem
  Interface for foundry information
  Statistical timing
  Static formats

## Slide 16: Targeted Participants
Integrated device manufacturers
Silicon foundries
Design automation vendors
End user companies
IP or library vendors

## Slide 17: Open Library Modeling Meeting
Date: June 15, 2005
Time: 10:00 – 11:30AM
Place: Anaheim Convention Center, Room 202A

## Slide 18: Summary
8 Letters of intent from DTC members
4 companies have submitted technology
BOD approval at April 7th meeting
Engaging industry players
Moving forward with formation of coalition
Open Modeling Meeting at DAC on 06/15