## Slide 1: Things You Can Learn From V/I Curves IBIS Summit / DAC 2005 Todd Westerhoff Cisco Systems, Inc.

## Slide 2: Components of a [Model] Declaration
V/T Curves
V/I Curves
Pullup/Pulldown
PWR/GND Clamps

## Slide 3: For Purposes of this Presentation …
Td = 2 nS
Z0 = 50 ohms
Td = 25 pS
Z0 = 50 ohms
500 pS edge rate
Zout = ???
Ccomp = 5 pf
Rseries (optional) = ??? ohms

## Slide 4: Electrically …
Td = 2 nS
Z0 = 50 ohms
500 pS edge rate
Zout = ???
Ccomp = 5 pf
Rseries (optional) = ??? ohms

## Slide 5: Rising Edge Behavior, t=0
0V
VDDQ
t =0
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
Ccomp = 0 pf for now

## Slide 6: Rising Edge Behavior, t=500ps
0V
VDDQ
t = 500 ps
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 7: Rising Edge Behavior, t=1ns
0V
VDDQ
t = 1 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 8: Rising Edge Behavior, t=2ns
0V
VDDQ
t = 2 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 9: Rising Edge Behavior, t=2.5ns
0V
VDDQ
t = 2.5 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 10: Rising Edge Behavior, t=3ns
0V
VDDQ
t = 3 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 11: Rising Edge Behavior, t=4ns
0V
VDDQ
t = 4 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 12: Rising Edge Behavior, t=4.5ns
0V
VDDQ
t = 4.5 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now

## Slide 13: Observations
The buffer output changes voltage only when the edge is launched and the reflection is received
  Launch: 0 to 0.5 ns
  Reflection: 4 to 4.5 ns
The buffer spends most of its time in the steady-state condition, where behavior is determined by the V/I curve
  Reflection behavior is also determined by the V/I curve

## Slide 14: Dynamic vs. Steady State Behavior
0V
VDDQ
t =0
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
Ccomp = 0 pf for now
Steady State

## Slide 15: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 500 ps
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Dynamic 0 to 0.5 ns

## Slide 16: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 1 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Steady State

## Slide 17: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 2 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Steady State

## Slide 18: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 2.5 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Steady State

## Slide 19: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 3 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Steady State

## Slide 20: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 4 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Steady State

## Slide 21: Dynamic vs. Steady State Behavior
0V
VDDQ
t = 4.5 ns
Td = 2 nS
Z0 = 50 ohms
Assume Zout +
Rseries = 50 ohms
VDDQ/2
Ccomp = 0 pf for now
Dynamic 4.0 to 4.5 ns

## Slide 22: … So What Determines Steady-State Values?
0V
VDDQ
t = 1 ns
Td = 2 nS
Z0 = 50 ohms
VDDQ/2
Voltage divider effect determines step voltage
VDDQ
Zout
Rseries
Zout + Rseries = 50 ohms
Tline looks like 50 ohms to GND

## Slide 23: How to Determine Zout?
If we know Zout, we can compute step voltage
Can select Rseries such that Zout + Rseries = Z0
Td = 2 nS
Z0 = 50 ohms
VDDQ
Zout = ???

## Slide 24: Remember Transistor Curves and Load Lines?
We used them to find DC bias points for amplifier circuits back in college
They’re equally valid for digital circuit analysis
  Digital circuits simply operate with VGS saturated

## Slide 25: 1.8V HSTL Class 1 Pulldown V/I Curve
Look like a transistor curve? That’s because it is!
  Special case where VGS = VDDQ
Load line analysis will find the operating point

## Slide 26: 1.8V HSTL Class 1 Pulldown Load Line
Since this is a pull down, load line should be 50 ohms to VDDQ
Step voltage for unterminated line is 0.64V
This buffer will overdrive a 50 ohm line in the nominal case
23 mA
0.64V
1.8V
50 ohms

## Slide 27: Simulation Results
Step voltage is 645 mV
Overshoot is 509mV below GND
Dummy load has no
effect; gives simulator
a node to measure

## Slide 28: What Else Do We Know?
Pulldown will operate along the V/I curve from the origin to the load line intersection
The slope of the V/I curve corresponds to Zout, if the curve is linear, the device will behave as a resistor

## Slide 29: Serial Termination Basics
Initial voltage launched down the line determines overshoot at receiver
Combined value of Zout and Rseries determines how well reflections are absorbed

## Slide 30: It’s a Current Thing …
Ideal step voltage is VDDQ/2
  From Ohm’s law: E=IR, I=E/R
  E = VDDQ/2, R=50 ohms
  I = (VDDQ/2)/50 = VDDQ/100
Our 1.8V receiver requires 1.8/100 = 18mA of line current for ideal reflection behavior
What current gives us the ideal response at the receiver input?
Z0 = 50 ohms

## Slide 31: How Strong Is Our HSTL Output?
At 50 ohm operating point, R=E/I
  E = 0.64V, I = 23 mA
Effective output impedance = 28 ohms

## Slide 32: … So, What Value of Rseries ?
Effective Output Impedance, R=E/I
  E = 0.9V, I = 18mA, so R = 50 ohms
Zout + Rseries = 50, Rseries = 22 ohms
Zout = 28 ohms
Rseries = ???
We know current = 18mA
We also know step voltage = 0.9V

## Slide 33: Updated Simulation Results
Negative reflection
off driver’s C_COMP
Still slight overshoot;
25mV below GND

## Slide 34: Why Is There Still Overshoot?
The series resistor changes the transistor’s operating point
Load line is now 72 (50 + 22) ohms to VDDQ
If the V/I curve isn’t linear between the new and old operating points, Zout will change
New Zout = 0.47V/18mA = 26 ohms

## Slide 35: Simulation Results For New Load Line
Negative reflection
off driver’s C_COMP
Overshoot is basically gone

## Slide 36: How Do We Determine Zout and Rseries ?
Determine ideal current from I=VDDQ/100
Find corresponding current point on V/I curve
Compute Zout,eff = Ecurve/Icurve
Assign Rseries such that Zout,eff + Rseries = Z0
Zout = ???
Rseries = ???

## Slide 37: For Our 1.8V HSTL Buffer …
I = 1.8V/100 = 18mA
From the pulldown curve, E=470mV at I=18 mA
Zout,eff = 0.47/0.018 = 26.1 ohms
Rseries = 23.9 ohms
18 mA
470 mV

## Slide 38: Pullup Curves Work The Same Way
I = 1.8V/100 = -18mA (IBIS convention)
From the pullup curve, E=371mV at I=-18 mA
Zout,eff = 0.371/0.018 = 20.6 ohms
Rseries = 29.4 ohms
-18 mA
371 mV

## Slide 39: Pullup/Pulldown Simulation Results
Overshoot on rising edge
Rseries well matched for falling edge

## Slide 40: Observations
This is a HSTL Class 1 buffer; we’d expect it to be designed for point to point operation without termination (50 ohm Zout)
Zout,eff ranges from 21-26 ohms, requiring a series resistor to avoid overshoot
Pullup/Pulldown are not well matched (21 vs. 26 ohms)
This could either be a buffer design issue or a modeling issue

## Slide 41: More On V/I Curves
Where the load line intersects the V/I curve says a lot about how the device will behave
Linear Region
Saturated Region
Nonlinear Region

## Slide 42: 3.3V, 4mA LVTTL Buffer Pulldown Curve
50 ohm, 3.3V load line
This device can’t drive a 50 ohm line; we need 30 mA, the output can only supply 17 mA
Current at this point determines overshoot / undershoot at the receiver
The slope of the V/I curve at this point determines how the driver absorbs reflections

## Slide 43: Simulation Results, 4mA Buffer
As expected, the driver cannot drive the line or adequately control the reflections

## Slide 44: 3.3V Clock Output Buffer Pulldown
Load line suggests buffer will drive about 42mA into a 50 ohm line; we only need 30mA
Step voltage E=IR, 42 mA*50 ohms = 2.1V, so we expect about 900 mV overshoot
Slope of V/I curve at load line is very high; expect very poor absorption of reflections by driver

## Slide 45: Simulation Results – Falling Edge
Overshoot slightly exceeds expectations
“Ringing” occurs because of slope of V/I curve at the load line

## Slide 46: More Simulation Results …
“Ringing” amplifies over time; the model essentially spins out of control

## Slide 47: Eliminate Reflections And …
Ideal termination at the end of the line eliminates reflections off the driver
Now we have a voltage threshold problem
This may be a modeling problem anyway; should be investigated further

## Slide 48: Summary
Depending on the ratio of edge rate to line length, drivers can spend much of their time in “steady state” conditions
“Steady state” behavior is driven by V/I curves
Understanding the details behind V/I curve can provide valuable insight into
  Buffer behavior
  Model quality
  Termination selection

## Slide 49: Yoda Says ….
Mind your V/I curves!
  Important, they are!
  Save you, they can!