## Slide 1: Power Integrity Proposal Regarding BIRD 95
Ken Willis, Lance Wang
Cadence Design Systems
DAC IBIS Summit
June 2005

## Slide 2: Agenda
Part One – Power Integrity Proposal
Part Two - Study:
  Is [Composite Current] good enough for improving PI/SSN simulation using IBIS?

## Slide 3: Part One – Power Integrity Proposal
Issues with BIRD 95
Proposed direction

## Slide 4: Issues with BIRD 95
Is “Pin-level” the best approach?
Proposed additions to go under the [Model] keyword (buffer level)
Power/ground parasitics can be different for different instantiations of the same buffer type on a component; should not really group together with the buffer model
On-die power/ground parasitic networks are essentially a “grid”, difficult/impossible to break out into individual IO-specific elements
Is this truly scalable to multiple drivers switching?
Does it really help answer the question of interest:
  “What is the effect seen when multiple drivers on the same rail switch simultaneously?”

## Slide 5: Issues with BIRD 95 (cont)
[Composite Current] “messy” as defined now
Currently defined at the [Model] level
This current is load dependent; better approach may be to define a Pre-Driver circuit.
Combined together with the existing IBIS buffer model
  TV curves already “open to simulator interpretation”
  building more on top of existing TV curve definition is problematic
Should define the pre-driver as an independent and separate (but associated) circuit entity
  leave existing IO structure as-is for compatibility
  maintains consistency with what IBIS has done so far
  pre-driver simply absent if not tied to same rail as IO buffer

## Slide 6: Proposed Direction
Break the Power Integrity problem up into 2 separate areas of focus
  Power delivery
  SSN
Attack “top down” from [Component] level instead of “bottom up” from the [Model] level
Use IBIS to enable the flow of required information to the SI community so they can do analysis

## Slide 7: Power Delivery
Enable systems companies to better design their board-level Power Distribution System (PDS)
Typically a frequency domain approach, focused on planes and caps
Start out at the [Component] level
  list out each of the power rails on the component (ex. 2.5v IO, 1.8v core, etc.)
  provide the current profile and operating frequency for each of these rails
This would enable SI engineers to figure out initial decoupling schemes for parts
Could then look “across the board”, including specific stack-up and make decoupling trade-offs at the PCB level
Can expand to the package, then to the chip level in the future
  address different frequency bands
  will require additional information from IC suppliers

## Slide 8: SSN
Enable IC & systems companies to better understand and combat the effects of SSN
Typically a time domain approach, focused on high speed signals and drivers
Start out at the [DC Grid] level
  “DC grid” defined by IO power and ground pin groups per the [Pin Mapping] keyword
  specify a [Grid Model] for each unique DC grid
    some ports on the [Grid Model] have power or ground pin names, to correspond to external power and ground pins of the [Component]
    some ports on the [Grid Model] have signal pin names, to correspond to specific IO buffer connections
  specify the “C_bypass” for specific DC grid pairs, for on-chip capacitance

## Slide 9: SSN (cont)
Refine the IO model
  specify a separate [Pre Driver Model] for each driving IO buffer
  specify the parasitic capacitance for the specific IO model pwr-gnd feeds (if known)
Give the [Switching Schedule] (or statistical probability) of how many drivers may actually switch together
Can easily add detailed package and board-level models to analysis
Cooperation from IC suppliers will be crucial in enabling this flow of information.
This would provide the pieces needed to start understanding SSN effects

## Slide 10: Part Two – Study: Is [Composite Current] good enough for improving PI/SSN simulation results using IBIS?
Static Currents
Is [Composite Current] good enough for PI/SSN simulations?
  Ground Bounce Current
  Current vs. Time Table (IT)
  Current profile in Single (Individual) condition vs. in Multiple driver (network) condition
Conclusions

## Slide 11: Static Currents
Ipwr
Ignd
Iout
Ipwr = Iout + Ignd
Assumptions:
Static Analysis
Individual block
Known Iout
Ipwr – Total current from power
Ignd – Total current to Ground
Iout – Current to Output

## Slide 12: Test Setups
Tests
  HSpice simulations with transistor level models
  Tests for a 1.8v single end, serial structure (4 cells back to back), no internal feedback
    Single Driver alone and in a Multi-Driver Network
    Multiple Drivers in Network
    Loads: 50, 100 and 250 Ohm to Node 0, “Pure” Resistors
    Stimulus: PULSE ( 0 1 -3.33333e-016 2.95e-009 2.98667e-009 3.71667e-009 1.33333e-008 )
    Power Parasitics: L (2nH) and C (2pF)
    Ground Parasitics: L (2nH) and C (2pF)

## Slide 13: Single Driver Case
PWR
GND
LOAD
INPUT
R
Single Driver Test Circuit
Current Probes

## Slide 14: Multiple Driver Case
PWR
GND
LOAD
INPUT
R
Multiple Driver Test Circuit
(Identical 7 drivers parallel)
Current Probes

## Slide 15: Ground Bounce Current
Is Ground Bounce Current directly synchronized with Power Bounce Current?
Does current IBIS give correct Output Current when Power/Ground current switching?
Can we use Static assumptions to model this behavior?

## Slide 16: Ground Bounce Current
1 driver active in the 7-driver network
Falling edge, 50, 100, 250 Ohm loads
(Waveform captured at Active Driver)
Ignd
Ipwr
Vout, 250Ohm

## Slide 17: Ground Bounce Current
1 driver active in the 7-driver network
Rising edge, 50, 100, 250 Ohm loads
(Waveform captured at Active Driver)
Ignd
Ipwr
Vout, 250 Ohm

## Slide 18: Ground Bounce Current
7 drivers active in the 7-driver network
Falling edge , 50, 100, 250 Ohm loads
Ignd
Ipwr
Vout, 250 Ohm

## Slide 19: Ground Bounce Current
7 drivers active in the 7-driver network
Rising edge, 50, 100, 250 Ohm loads
Ignd
Ipwr
Vout, 250 Ohm

## Slide 20: Ground Bounce Voltage
7 drivers active in 7 driver network
50, 100, 250 Ohm loads

## Slide 21: Power Bounce Voltage
7 drivers active in 7 driver network
50, 100, 250 Ohm loads

## Slide 22: IT Tables
Can IT tables be used as the “Profile” for SSN?
Can this scale cleanly to different load conditions?

## Slide 23: IT Tables
1 driver active in 7-driver network
50, 100, 250 Ohm loads
Ipwr
Ignd
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: IT Tables
7 drivers active in 7-driver network
50, 100, 250 Ohm loads
Ipwr
Ignd
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Individual Profile vs. Profile in the Network
Can the individual profile for one driver be applied to the network case?

## Slide 26: Individual Profile vs. Profile in the Network
250 Ohm
Falling
100 Ohm
50 Ohm

## Slide 27: Individual Profile vs. Profile in the Network
50 Ohm
100 Ohm
250 Ohm
Rising

## Slide 28: Conclusions
Ground Bounce Current Should be considered in the Profile
  These are not “Static” entities
  Active devices might store energy somewhere inside the “black box”
  Otherwise, leaves ground current profile “open to interpretation”
IT curves seem insufficient to be the sole Profile Data
  Difficult to scale volatile IT curves for different loading & network conditions
Profile data should be captured in the context of its Network
  There are significant differences between “individual” profile and “network” profile

## Slide 30: BACK UP SLIDES
Ambrish Varma’s VCCAP Slides
A possible solution for Buffer (Pin) Signature in SSN/PI

## Slide 31: A Solution
Quiet Line
Pkg Parasitics
Power
Wire Bond and Pin Parasitics
Wire Bond and Pin Parasitics
VCCAPs
No Changes to the IBIS spec
Considerable improvement in SSN noise representation
Depends on the buffer
Customizable, depends on the end user
Implemented for Voltage and Current mode drivers
Notes: <number>
<footer>
<header>
<date/time>
Downside could be that every designer could come up with different value for the parameters.

## Slide 32: Ground
Plain IBIS
IBIS With VCCAPS
HSPICE

## Slide 33: POWER
Plain IBIS
IBIS With VCCAPS
HSPICE

## Slide 34: Quiet Driver
Plain IBIS
IBIS With VCCAPS
HSPICE