## Slide 1: IBIS Quality Report
A progress report of the IBIS Quality Task Group
Mike LaBonte, Cisco Systems
IBIS Summit Meeting, 5 June 2007

## Slide 2
[Package]
[Pin] RLC
[Diff Pin]
[Model Selector]
IQ0
IQ3
IQ2
IQ1
IQ4
M
S
X
[Receiver Thresholds]
C_comp
Rat hole
IQ
[Model Spec]
[Temperature Range]
[Voltage Range]
[Pulldown]
[Pullup]
Symbol swamp
[GND
Clamp]

## Slide 3: Regular IQ Meeting Participants
David Banas, Xilinx
Moshiul Haque, Micron Technology
Kim Helliwell, LSI Logic
Mike LaBonte, Cisco Systems, chair
Eckhard Lenski, Siemens
Roy Leventhal, Leventhal Design & Communications
Bob Ross, Teraspeed Consulting Group

## Slide 4: Brief History
Barry Katz started IBIS-Quality in March 2002
Review of 1.0 IQ specification completed October 2004
IQ checklist released October 2004
Parser bug 90 submitted and approved August 2005
Parser bug 94 submitted and approved March 2006
Book “IBIS Model Creation & Validation” discusses IQ
Version 1.1 IQ specification initiated August 2006

## Slide 5: Specification Version 1.1
IBIS Quality Levels
  IQ0 – Not Checked
  IQ1 – Passes IBISCHK
  IQ2 – Suitable for Waveform Simulation
  IQ3 – Suitable for Timing Analysis
  IQ4 – Suitable for Power Analysis
Special Designators
  S – Simulation correlated
  M – Measurement correlated
  X - Exceptions
IQ0
IQ3
IQ2
IQ1
IQ4
M
S
X

## Slide 6: IQ Check Example
    3.2.5 {LEVEL 3} [Pin] RLC parasitics are present and reasonable
For a LEVEL 2 model, pin parasitics are optional, but they are mandatory for a LEVEL 3 model (that is, a model suitable for timing). To pass this check the RLC values must be present for all signal pins in the [Pin] section, or [Package Model] must be present. Pin parasitics should either be measured or extracted using a 2D or 3D solver. Reasonable signal pin parasitics will result in impedance and delay characteristics that fall in the ranges:
TD = SQRT(LC) < 300ps
Z0 = SQRT(L/C) < 100ohm
Note that IQ check 3.1.2. also requires that each [Pin] RLC value falls within the min/max range as given by the [Package] keyword. The [Package] keyword can be adjusted to accommodate.

## Slide 7: Current Activities
Working on feature-selective validation for correlation
Reviewing IQ checks
  Updating to new level numbering system
  Rationale documented to avoid future confusion
  Last reviewed check 3.3.4, end of [Diff Pin] section
  Jumped ahead to discussion of [Receiver Thresholds]

## Slide 8: Summary of 1.1 Review Progress
2.0 General Header Section
  8 of 8 checks reviewed
3.0 Component Section
  17 of 19 checks reviewed
4.0 Model Section
  0 of 68 checks reviewed
5.0 Possible Errors
  Needs rework, maybe a name change
6.0 Correlation
  David and Roy working on this
7.0 Model Limitations and Model Maker Notes
  ???

## Slide 9: IBIS Quality Task Group
Web:
  http://www.vhdl.org/pub/ibis/quality_wip
Email list:
  http://www.freelists.org/list/ibis-quality
  Or send email
  To: ibis-quality-request@freelists.org
  Subject: subscribe
Meetings:
  Tuesdays from 11:00am to 12:00pm Eastern Time
Questions? Mike LaBonte milabont@cisco.com