## Slide 1: The 3S Proposal: A SPICE Superset Specification for Behavioral Modeling
Michael Mirmak
Intel Corporation
June 5, 2007

## Slide 2: Legal Disclaimer
THIS DOCUMENT AND RELATED MATERIALS AND INFORMATION ARE PROVIDED "AS IS" WITH NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION, OR SAMPLE. INTEL ASSUMES NO RESPONSIBILITY FOR ANY ERRORS CONTAINED IN THIS DOCUMENT AND HAS NO LIABILITIES OR OBLIGATIONS FOR ANY DAMAGES ARISING FROM OR IN CONNECTION WITH THE USE OF THIS DOCUMENT.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel may make changes to specifications, product descriptions, dates and plans at any time, without notice.
Copyright © 2007, Intel Corporation. All rights reserved.

## Slide 3: An Additional Disclaimer
  The following information is presented as the opinion of one person at Intel. This presentation does not necessarily represent Intel policy, commitments or preferences.
  This is not presented on behalf of the IBIS Open Forum and does not represent the official IBIS Open Forum direction.
Notes: Note that you will speak from a PCB SI simulation perspective, and not an RF perspective.

## Slide 4: Agenda
  The What and Why of SPICE
  Analog Behavioral Modeling Today
  Pros/Cons of SPICE in General
  SPICE Compatibility
    Elements as a Case Study
  Outline of a Behavioral SPICE Specification
    What it must include
    What it should exclude
  What a Standard SPICE Wouldn’t Address
    Alternatives
  Summary

## Slide 5
SPICE Review: A Tool and Modeling Method
************************************************
.MODEL NMOS NMOS
+ (LEVEL=3 UO=400.0 VTO=1.00
+ TPG=1 TOX=15E-9 NSUB=1.00E17
+ VMAX=200.0E3 RSH=50 XJ=100.0E-9
+ LD=120.0E-9 DELTA=20.0E-3 THETA=0.10
+ ETA=10.0E-3 KAPPA=20.0E-18 PB=0.40
+ CGSO=2.00E-10 CGDO=2.00E-10 CJ=0.30E-3
+ CJSW=0.20E-9 MJ=350.0E-3 MJSW=200.0E-3)
************************************************
“Simulation Program with Integrated Circuit Emphasis”
Developed by Donald Pederson at UC Berkeley in 1960s
Not standardized, but the general format is widely recognized
Berkeley still develops process models (BSIM3, BSIM4, etc.)
SPICE 3F6 program available from Berkeley
    http://bwrc.eecs.berkeley.edu/Classes/IcBook/SPICE/
Many commercial SPICE flavors are available
Most IC vendors have their own flavors, for their own processes
  Usually not compatible with any commercial SPICE variant
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: The Need for Analog Alternatives to “Old” IBIS
For a time, traditional IBIS (3.2/4.0) was “going out of style”
IBIS is well-tuned to single-ended, simple designs (e.g., CMOS)
IBIS 3.2/4.0 increasingly hard to use when modeling complex buffers
    SerDes buffers with multi-tap equalization
    Complex impedance modeling (frequency- and voltage-dependent C_comp)
SPICE returned briefly as a popular alternative
    IBIS Macromodeling Task Group emerged to support IBIS+ behavioral SPICE
IBIS
‘98
‘04
‘05
SPICE Models
(Transistor & Behavioral)
diagram courtesy T. Westerhoff; used with permission
Notes: Not talking algorithmic modeling here, just simple analog; recall Don Telian’s presentation

## Slide 7: Why Use Behavioral SPICE for Signal Integrity?
For buffers, address “traditional” (3.2/4.0) IBIS shortcomings above
    IBIS 4.1/4.2 supports Berkeley SPICE code
Many vendors use SPICE to address IBIS package shortcomings
    IBIS package support is clearly inadequate (see previous IBIS Summits)
    ICM available but new; automated extraction for packages WIP
    Integration into IBIS still not done
IC/IP Vendor Needs
    For complex systems, device/package models are not enough
    Many customers expect full system decks, for analysis and correlation
≠
C_comp
Notes: Data-dependence and single-value C_comp are particular problems; full system decks in one tool get around the analysis/interpretation problem

## Slide 8: Which SPICE?
In early 2007, IBIS-ATM took up the challenge
    Asked a major proprietary SPICE vendor to release its manuals to the public
    This was politely declined
Can we define a standard SPICE superset
for behavioral modeling, “3S”?
Vendor B’s SPICE
Vendor A’s
SPICE
Berkeley
SPICE
Notes: SPICE isn’t standard!

## Slide 9: “SPICE” Pros and Cons
Something more than transistor models or traditional IBIS is needed
How best to address advanced modeling and analysis needs?
For
Against
Not standard
A format, not a language
Analog-only
Not suited to algorithmic modeling (numeric processing instead of V, I analysis)
Still data-driven
Can be used behaviorally
Simple to understand
Familiar to most engineers
Versions implemented in most EDA tools
Fairly flexible: if you can describe it with electrical elements, you can describe it with SPICE
SPICE has a value for behavioral modeling.
It is more flexible than table-driven IBIS with
wider support at lower cost
Notes: Talk about 4.1 vs. 4.2. IBIS responded to the split
Talk about the SPICE standardization movement.
Talk about proprietary general purpose mathematical languages

## Slide 10: Problems of Implementation: Elements
Some Berkeley SPICE definitions are effectively universal…
But evolution from Berkeley SPICE has caused deviations
    The elements below are completely different under different implementations
    These elements are implemented in some tools but not all
Notes: A case study…

## Slide 11: SPICE Problems
Inconsistency
    As shown above, even basic elements are inconsistent between SPICEs
    Shared element functions are often inconsistent (e.g., V sources)
    Some analysis functions are proprietary (e.g., S-parameter generation)
  Lack of expandability
    Users cannot define new elements or analyses, only new subcircuits
      At least one proprietary SPICE defines a “macro” element, but the macros are under the control of the tool vendor, not the user or author
  Lack of control
    In an age of 10 Gbps signals, obtaining inconsistent results for “standard” models is no longer tolerable
These have been the hurdles to widespread
SPICE usage for behavioral modeling

## Slide 12: What Would A Standard Behavioral SPICE Look Like?
Any standard SPICE would have to support the following:
    “First-letter” name + node + function syntax for elements
      Including the truly common elements and formats
    Subcircuit syntax and approach
    “Dot” syntax for functions, parameters and analysis types (e.g., “.OPTIONS”)
      Common analysis types and functions TBD
    Other common structural assumptions
      No ordering requirements aside from title and .END
What would be excluded from the standard definition?
    Transistors and other active elements
      Process files and “LEVEL” would also be excluded
      Do we need diodes?
    Any element name that is inconsistent among proprietary implementations
    Functions or capabilities outside circuit solving
      Field solvers, digital logic functions, links to other languages or tools
This is readily achievable

## Slide 13: What Would A Standard Behavioral SPICE Add?
Major additions
    The A-element
      Undefined in any SPICE, based on informal survey
      Could be used as a specification-level “catch-all” macro alias
      Allow 3S elements new to some SPICEs to be easily implemented through extended parsing in more sophisticated SPICEs
      Specification would control associated function definitions
    .COMPAT/.UNCOMPAT switch
      “Wrapper” for standard behavioral SPICE text
      Netlist-level flag to tool to enforce behavioral SPICE standard rules
      Enables use of 3S code within a proprietary netlist
These should not represent a
significant industry burden
Axxxx macroname n1 n2 …
Nxxxx n1 n2 …
Wxxxx n1 n2 …
?xxxx n1 n2 …
SPICE 1
SPICE 2
SPICE 3

## Slide 14: Issues
A format-only specification may be insufficient
    Different tools may still interpret data differently
    Complex SI measurements (DDR2) would still be painful
    IC/IP vendors want more control over analysis methods (algorithms)
      e.g., causality and passivity enforcement on transmission lines
    This favors language-based rather than format-based approaches
  Can we truly exclude active devices (transistors)?
    BSIMx is still highly popular, useful and effectively a standard
  Administrative burdens are considerable
    Maintenance, including adding new macro functions, would be required
    Development of a syntax parser would also be needed
Is this still worth doing?
Are there alternatives?
Notes: Language-based drive is a commoditization factor among EDA tool vendors
IP protection can be as simple as compilation for algorithmic models.

## Slide 15: “The Split”
Both models and tools have to address varying market segments
IBIS-ATM work shows that model creation and use are growing apart
    System designers need relatively simple models in inexpensive tools
    IC designers need more detail on the digital, data-processing side
IC Vendors
System Designers
Lower-cost tools
Analog focus (no digital support needed)
Model use, not development
With multiple suppliers, model portability is key
Higher-cost, highly capable tools
Digital and analog support needed
Same environment for model development and testing
Portability less important until export stage

## Slide 16: A Better Solution than SPICE?
Is Verilog-A a more compelling analog
modeling solution than SPICE?
  Verilog-A is already a SPICE superset
    Verilog-A is already standard, widely supported (IBIS 4.2!) and available
      At least one major SPICE vendor supports Verilog-A today
    Supports analysis control without requiring digital language support
      IC vendors get control over model interpretation
    Addresses both the element naming and function definition problems
      Element names are separate from instance names
  Anyone recall the IBIS Macromodel library using Verilog-A for SPICE?
  Transmission lines and S-parameters are a significant omission
    An enhanced Verilog-A could support SI features, system netlists
IBIS_R #(.Rval(R_val), .Scale(Scale_val)) R1 (Node1, Node2);
Notes: Remember – the AMS problem is the $$$ of digital language support and commitment to two languages!
Note that this would work very well with IBIS-ATM algorithmic proposal -> Verilog-A would only be for the analog portion

## Slide 17: If We Go Ahead with 3S, Next Steps…
  Outline and document the basic features, common to most SPICEs
    Element names and formats
    Element functions
    Options and analysis types
    Other key syntax and netlist structural assumptions
  Define the new features, unique to 3S
    The A-element syntax
    A-element macro names and data formats
    .COMPAT/.UNCOMPAT usage
  Define analysis requirements (“the hard part”)
  Create illustrative test cases
  Write the relevant specification documents
    Likely in parallel with the steps above
Delaying work on a unified analog solution means
more “lost ground” for IBIS and standards
Notes: Language-based drive is a commoditization factor among EDA tool vendors. Industry “faith” in IBIS is dropping rapidly.
IP protection can be as simple as compilation for algorithmic models.