## Slide 1: Ibischk4 Version 4.2.1 and Funny IBIS Models
Bob Ross
IBIS Summit Meeting, DAC 2007
San Diego, California
June 5, 2007

## Slide 2: Version 4.2.1 Release
IBISCHK4 version 4.2.1 complete
  Source code delivered
  Executables uploaded
    1 for dos32 (for Windows)
    4 for Unix (Sun_5, Solaris_6, Solaris_8, HP_11i)
    2 for linux (Redhat, SUSE)
    Details in changes_421.txt
Major changes from 7 BUG reports
  Monotonic checks – consistency for all versions
  Caution flag – Quality Committee addition
  [Receiver Thresholds] – correct a defect
  Other – Model_type Warning to Error, etc.

## Slide 3: Monotonic – Summations and Notes
Warnings for non-monotonic summations only
  E.g., [Pullup] and both clamp tables together for driving
  For non-driving, both clamps together
  Also for Submodel Clamps for the modes of interest
  Model_type and submodel mode logic considered
Notes for all individual tables
  Still allows locating the specific problem for analysis
  Notes are less serious than Warnings
Check same for IBIS Version 2.0 through 4.2
  Version 3.2 and below used to give Warnings for each table

## Slide 4: Example
[IBIS Ver] 3.2 code for combined non-monotonicity:
IBISCHK4 V4.2.0
Checking bug94.ibs for IBIS 3.2 Compatibility...
WARNING (line 29) - Pulldown Typical data is non-monotonic
WARNING (line 29) - Pulldown Minimum data is non-monotonic
WARNING (line 29) - Pulldown Maximum data is non-monotonic
Errors : 0
Warnings: 3
IBISCHK4 V4.2.1
Checking bug94.ibs for IBIS 3.2 Compatibility...
NOTE - Pulldown for Model: BUFFER Typical data is non-monotonic
NOTE - Pulldown for Model: BUFFER Minimum data is non-monotonic
NOTE - Pulldown for Model: BUFFER Maximum data is non-monotonic
Errors : 0

## Slide 5: However … Version 4.2.2
BUG96
  Line numbers not reported in NOTEs
    Post processing change versus first pass
    Restore older Warning code and change to Notes
BUG97
  Larger file issue (Notes + Warnings) less than older Warnings
  Need to understand

## Slide 6: The –caution Flag
Ibischk4 –caution syntax for .ibs, .pkg, and .ebd
  Usage: ibischk4 -caution <IBS filename>
  : ibischk4 -caution -ebd <EBD filename>
  : ibischk4 -caution -pkg <PKG filename>
For all versions 2.0 through 4.2
Placeholder for future tests
  Caution because real exceptions exist such as with some PCIX models for Vmeas
  IBISCHK4 V4.2.1
  Checking bug90.ibs for IBIS 4.2 Compatibility...
  CAUTION - Vmeas is >= Vinh for model DATA
  Errors : 0
  Cautions: 1
  File Passed

## Slide 7: [Receiver Thresholds] Logic Fixed
Several serious defects
  Combined test for DDRII with [Diff Pin], [Model Selector] and single-end or differential subparameters under [Receiver Thresholds] incorrect
    Practical situation with DDRII and selectable on die terminations
  Differential subparameters not allowed when needed
    Impossible to put in complete information
    Models with missing information passed
    [Model Selector] indirection not handled
Warning messages used instead of Error messages
  Allows existing flawed models to still be loaded
  Expect Warning messages with ibischk4 Version 4.2.1 and above
Both single-ended and differential subparameters allowed
  Some DDRII
  USB models

## Slide 8: BUG93 Test – Fixed in Version 4.2.1 with 0 Errors and 0 Warnings
IBISCHK4 V4.2.0
Checking bug93.ibs for IBIS 4.2 Compatibility...
ERROR - Model DQS_FULL Receiver Thresholds: Vth must be specified for single ended receivers
ERROR - Model DQS_FULL Receiver Thresholds: Vinh_ac must be specified for single ended receivers
ERROR - Model DQS_FULL Receiver Thresholds: Vinl_ac must be specified for single ended receivers
ERROR - Model DQS_FULL Receiver Thresholds: Vinh_dc must be specified for single ended receivers
ERROR - Model DQS_FULL Receiver Thresholds: Vinl_dc must be specified for single ended receivers
ERROR - Model DQS_FULL Receiver Thresholds: Tslew_ac must be specified for single ended receivers
WARNING - Model DQS_FULL Receiver Thresholds: Vcross_low must not be specified for single ended receivers
WARNING - Model DQS_FULL Receiver Thresholds: Vcross_high must not be specified for single ended receivers
WARNING - Model DQS_FULL Receiver Thresholds: Vdiff_ac must not be specified for single ended receivers
WARNING - Model DQS_FULL Receiver Thresholds: Vdiff_dc must not be specified for single ended receivers
WARNING - Model DQS_FULL Receiver Thresholds: Tdiffslew_ac must not be specified for single ended receivers
ERROR - Model DQS_HALF Receiver Thresholds: Vth must be specified for single ended receivers
ERROR - Model DQS_HALF Receiver Thresholds: Vinh_ac must be specified for single ended receivers
ERROR - Model DQS_HALF Receiver Thresholds: Vinl_ac must be specified for single ended receivers
ERROR - Model DQS_HALF Receiver Thresholds: Vinh_dc must be specified for single ended receivers
ERROR - Model DQS_HALF Receiver Thresholds: Vinl_dc must be specified for single ended receivers
ERROR - Model DQS_HALF Receiver Thresholds: Tslew_ac must be specified for single ended receivers
WARNING - Model DQS_HALF Receiver Thresholds: Vcross_low must not be specified for single ended receivers
WARNING - Model DQS_HALF Receiver Thresholds: Vcross_high must not be specified for single ended receivers
WARNING - Model DQS_HALF Receiver Thresholds: Vdiff_ac must not be specified for single ended receivers
WARNING - Model DQS_HALF Receiver Thresholds: Vdiff_dc must not be specified for single ended receivers
WARNING - Model DQS_HALF Receiver Thresholds: Tdiffslew_ac must not be specified for single ended receivers
Errors : 12
Warnings: 10
File Failed

## Slide 9: However … Version 4.2.2 New False Warning Problem
BUG95: Incorrect Warnings not in earlier versions
  IBISCHK4 V4.2.1
  Checking bug95.ibs for IBIS 3.2 Compatibility...
  WARNING - Pin A2 is not defined as a Diff Pin though the associated Model Selector INOUT was determined to be Differential
  WARNING - Pin B3 is not defined as a Diff Pin though the associated Model Selector INOUT was determined to be Differential
  WARNING - Pin Z3 is not defined as a Diff Pin though the associated Model IN was determined to be Differential
  WARNING - Pin Z4 is not defined as a Diff Pin though the associated Model IN was determined to be Differential
  Errors : 0
  Warnings: 4
  File Passed

## Slide 10: [Receiver Thresholds] De-rating Tables?
Designed for single-ended and differential specifications
Targeted for DDRII and above
Needs de-rating tables for real adoption
  Otherwise, vendor-specific syntax needed
  Or code based de-rating (VHDL-AMS, etc.)
A future BIRD?

## Slide 11: Other Fixes
Other minor fixes including a parser crash
BUG91 for Model_type Open_* with non-zero content in the extra [Pullup] or [Pulldown] table
  E.g., Open_drain with non-zero [Pullup]
  Elevated from Warning to Error
    Based on real issue since model is ambiguous and the waveform check may be misleading
  Cannot rely on EDA tool defaults

## Slide 12: Proposed ibischk4 Version 4.2.2
BUG95 – Fix incorrect single-ended, differential Warnings
BUG96 – Add line numbers to Notes
BUG97 – Resolve differences in summation of Notes plus Warnings versus original Warnings

## Slide 13: Investigate Parser Friendly Fixes
Parser code suggestions for EDA tool integration
  Unique file names (e.g., ibisxx_string.h versus string.h)
  Printf for command line mode needs to be globally edited for parser integration
  Filter Errors, Warnings for complete file for specific model of interest
  Other issues with names, globals, undefined code, etc.
If accepted, then targeted beyond Version 4.2.2

## Slide 14: Funny Models
0.ibs
  As many 0’s as possible (or 1f)
  Ibischk4 does not check everything
  Uncommon developer and customer issues
  Pathological cases shows what can be missed
inverse.ibs

## Slide 15: 0.ibs
[IBIS Ver] 4.0
[File Name] 0.ibs
[File Rev] 0
[Date] 0
[Source] 0
[Disclaimer] 0
[Notes] 0
[Copyright] 0
|
[Component] 0
[Manufacturer] 0
[Package]
R_pkg 0 0 0
L_pkg 0 0 0
C_pkg 0 0 0
|
[Pin] signal_name model_name R_pin L_pin C_pin
0 0 0 0 0 0
00 0 0 0 0 0
[Diff Pin] inv_pin vdiff tdelay_typ tdelay_min tdelay_max
0 00 0 0 0 0
|
[Model] 0
Model_type I/O
Vinh = 0
Vinl = 0
Vmeas = 0
Rref = 0
Vref = 0
|
C_comp 0 0 0
C_comp_pullup 0 0 0
C_comp_pulldown 0 0 0
C_comp_gnd_clamp 0 0 0
C_comp_power_clamp 0 0 0
|
[Temperature Range] 0 0 0
[Voltage Range] 0 0 0
[Pullup Reference] 0 0 0
[Pulldown Reference] 0 0 0
[Gnd Clamp Reference] 0 0 0
[Power Clamp Reference] 0 0 0
[External Reference] 0 0 0
|
[TTgnd] 0 0 0
[TTpower] 0 0 0
|
[Pulldown]
0 0 0 0
1f 0 0 0
|
[Pullup]
0 0 0 0
1f 0 0 0
|
[Gnd Clamp]
0 0 0 0
1f 0 0 0
|
[Power Clamp]
0 0 0 0
1f 0 0 0
|

## Slide 16: 0.ibs Problems
Problems
  I-V tables 0.0 and voltage references 0.0
  Waveform tables from 0.0 to 1f, passes waveform check
  Redundant V-T tables not checked
  All subparameters and text information set to 0
0.ibs – 0 Errors, 0 Warnings 0 Cautions
But still produces waveform in some tools and errors in others!
Not worth fixing
[Ramp]
dV/dt_r 1f/1f 1f/1f 1f/1f
dV/dt_f 1f/1f 1f/1f 1f/1f
R_load=0
|
[Rising Waveform]
R_fixture=0
V_fixture=0
C_fixture=0
L_dut=0
R_dut=0
C_dut=0
0 0 0 0
1f 0 0 0
|
[Rising Waveform]
R_fixture=0
V_fixture=0
C_fixture=0
L_dut=0
R_dut=0
C_dut=0
0 0 0 0
1f 0 0 0
|
[Falling Waveform]
R_fixture=0
V_fixture=0
C_fixture=0
L_dut=0
R_dut=0
C_dut=0
0 0 0 0
1f 0 0 0
| <snip>
[End]

## Slide 17: inverse.ibs
Inspired by real IBIS file creation issue
  Pulldown in [Pullup] table and visa-versa
    Vtable2 = Vdd - Vtable1
  Gnd Clamp in [Power Clamp] table and visa-versa
    Vtable2 = Vdd - Vtable1
  Rising Waveform in [Falling Waveform] table and visa-versa
    Change Rising to Falling and Falling to Rising
  Polarity Inverting
    Moves “low” state to High, and “high” state to Low
Passes IBISCHK4 Version 4.2.1
  Cannot fix timing test load Warning
Simulations identical
  Brute force way to avoid the Polarity subparameter!
Strange, but technically correct model

## Slide 18: normal.ibs and inverse.ibs [Pulldown] and [Pullup] Tables
inverse.ibs
[Pullup]
[Pulldown]
normal.ibs

## Slide 19: normal.ibs and inverse.ibs [Rising/Falling Waveform] Tables
inverse.ibs
normal.ibs
[Rising Waveform]
Opposite for [Falling Waveform]

## Slide 20: Conclusions
Ibischk4 Version 4.2.1
Fixes for expected Version 4.2.2
Pathological cases show that
  Ibischk4 does not check everything
  EDA tools may trap some funny cases
  Some might turn out to be tricks
  Uncommon, not worth fixing