## Slide 1: IBIS-ATM Update: SerDes Modeling and IBIS
Presented by: Todd Westerhoff, SiSoft
DAC IBIS Summit
June 5, 2007

## Slide 2: Who Needs SerDes Models?
System Designers
  Predict end-end link BER
  Evaluate system-level design tradeoffs
ASIC designers
  Evaluate different TX/RX behavior
SerDes circuit designers
  Validate with standard test setups
Test Equipment Vendors
  Model device-specific equalization & clock recovery

## Slide 3: Serial Link Analysis Needs
Analyze link behavior > 107 bits
Model transmit / receive equalization
Model clock recovery behavior
Serial link analysis is best addressed through a combination of analytical methods
  Characterization of the analog channel
  Equalization & clock recovery modeling

## Slide 4: Why Use Separate Steps?
Exploit linear behavior of serial channel analog components for computational efficiency
Leverage existing techniques for modeling equalization and clock recovery
  Communication systems theory
Enable multiple analytical approaches
  Commercial EDA tools
  Matlab / StatEye
  IP vendor tools

## Slide 5: Serial Link Analysis
Transmit Equalizer
Package Interconnect
System Interconnect
Clock
Recovery
Data
Recovery
Serializer
Package Interconnect
Receive Equalizer
TX
RX
Channel & Analog I/O
Linear, Time-Invariant
RX EQ, CDR LTI or non-LTI
TX EQ
LTI or non-LTI
Channel Characterization
(Impulse response)
TX Equalization
TX Optimization
RX Equalization
RX Clock Recovery
RX Optimization

## Slide 6: Serial Link Modeling Assumptions
Analog channel can be considered LTI
  Does not apply to fiber optics
Equalization cannot always be considered LTI
  e.g. DFE involves quantization of received signal
  Time-varying (adaptive) behavior
On-die noise and associated jitter is important, but measurement / modeling is not well defined
  This will evolve as techniques improve
IP vendors want to supply models that correspond to silicon as closely as possible

## Slide 7: IBIS-ATM Effort
Goal: SerDes Rx/TX model interoperability
  Multiple EDA environments
  Multiple SerDes vendor models
  Protect SerDes vendor IP
IBIS-ATM committee participation
  EDA: SiSoft, Cadence, Mentor, Agilent
  Semiconductor: IBM, TI, Intel, Micron, Xilinx, ST-Micro
  System: Cisco
Two part modeling standard
  Electrical model: TX / RX analog characteristics
  Algorithmic model: equalization, clock recovery, device optimization algorithms

## Slide 8: IBIS-ATM Activities Since DesignCon
Weekly IBIS-ATM calls
EDA vendor meetings
  Cadence/SiSoft/Mentor meeting in Chelmsford, MA
  Weekly conference calls
Regular meetings with IP vendors
  Weekly conference calls
Developed & refined draft BIRD

## Slide 9: Required SerDes Device Models
Characterization (analog)
  Existing IBIS 4.2 syntax
Communications models
LTI
  Equalization
  RX clock PDF
Non-LTI
  Nonlinear equalization
  Adaptive equalization
  Clock recovery behavior
Clock
Recovery
Equalizer
Sampler

## Slide 10: IBIS-ATM Algorithmic Models
Models provided as executable [binary] code
  Fast, efficient execution
  Protects vendor IP
  Extensible modeling capability
  Allows models to be developed in multiple languages
Standardized execution interface
  Module loading mechanism & call signature
  Data input/output formats
Standardized model parameter interface
  “Reserved parameters” interpreted by EDA platforms
  Model-specific parameters can be exposed to and set by end-users

## Slide 11: IBIS-ATM Algorithmic Models
TX
“GETWAVE”
RX
“GETWAVE”
Stimulus
With TX EQ
With TX, RX EQ
Recovered Clock
Non-LTI
TX
“INIT”
RX
“INIT”
Channel Impulse Response
With TX EQ
With TX, RX EQ
Model Setttings
Model Settings
LTI
Model Settings
Model Settings

## Slide 12: Executable Model Architecture
INIT
LTI Behavior
Impulse response processing
GETWAVE
Non-LTI Behavior
Time-domain Waveform Processing
CLOSE
Model clean-up & exit
Impulse response
Model settings
Impulse response
Model data
Model-specific outputs
Continuous time-
domain waveform
Continuous time-
domain waveform
Clock samples

## Slide 13: Executable (DLL) Call Arguments
Init (impulse response processing)
  Bit time
  Number of waveform samples per bit
  Number of crosstalk aggressors
  Channel impulse response(s)
  Model parameters and values
  Pointers to free memory, data return area
Getwave (waveform processing)
  Input waveform(s)
  Pointers to data return area
    Equalized waveform
    Clock times
    Optimized parameters

## Slide 14: Model Parameters
Additional data passed between executable model & simulator
Model-specific parameters
  Allow IP vendors to define data required for / provided by a specific model
  Defined parameter declaration and usage format
    Allows end-users to set and display model-specific data
Reserved parameters
  Predefined parameter list used by EDA tools to alter analysis flow
  Allows models to tell EDA platform what data the model does/doesn’t provide

## Slide 15: Current IBIS-ATM Status
Original proposal submitted by Cadence in 2006
Current proposal authored by Cadence, SiSoft, Mentor
Technical issues settled between EDA vendors
Proposed solution reviewed with IP vendors
Detailed documentation in development
Plan to distribute sample models and “wrapper code” to aid model developers

## Slide 16: Next Steps
Preliminary approval by IBIS-ATM subcommittee
Complete BIRD documentation
  Target: June 2007
Develop sample models & prototype EDA integration; resolve detailed issues with spec
  Target: September 2007
Bring to IBIS-ATM committee for final approval
Bring to IBIS committee for approval
* Note: Steps 3 and 4 in parallel