## Slide 1: Case Study of Scheduled Single-Ended Driver Featuring [Test Data]
Michael Mirmak
with Priya Vartak and Ted Ballou
Intel Corporation
Chair, EIA IBIS Open Forum
michael.mirmak@intel.com
IBIS Summit at DAC 2008
Anaheim, California
June 10, 2008

## Slide 2: Legal Disclaimer
THIS DOCUMENT AND RELATED MATERIALS AND INFORMATION ARE PROVIDED "AS IS" WITH NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION, OR SAMPLE. INTEL ASSUMES NO RESPONSIBILITY FOR ANY ERRORS CONTAINED IN THIS DOCUMENT AND HAS NO LIABILITIES OR OBLIGATIONS FOR ANY DAMAGES ARISING FROM OR IN CONNECTION WITH THE USE OF THIS DOCUMENT.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel may make changes to specifications, product descriptions, dates and plans at any time, without notice.
Copyright © 2008, Intel Corporation. All rights reserved.

## Slide 3: An Additional Disclaimer
  The following information is presented as the opinion of one person at Intel. This presentation does not necessarily represent Intel policy, commitments or preferences.
  This is not presented on behalf of the IBIS Open Forum and does not represent the official IBIS Open Forum direction.

## Slide 4: Agenda
  Introducing an Unusual Design
    “Buffer X” on “Interface X”
  Describing the Design with IBIS
    [Driver Schedule]
  Hurdles to Cross-tool Operation
    [Driver Schedule] Implementation
  Applying [Test Data] to Aid Correlation
  Tool Correlation
  Comments and Recommendations
  Q & A

## Slide 5: An Unusual Design
“Buffer X” for “Interface X”
A real interface, in use on real systems
Many familiar aspects, making IBIS a good modeling approach
    Interface is single-ended and multi-drop
    Buffers are complementary (pullup/pulldown) or open-source
    Edge rates in (low) nanoseconds, with MHz switching rates
  But… several bizarre features confound simple model-making
    Device contention: multiple components drive simultaneously
    Logic is both time-and voltage-based
      “1” and “0” defined by percent duty cycle at high or low voltages
    At least one device uses staged buffer turn-on/turn-off
Notes: Note: this is a real design, not a proposed or theoretical application. [Test Data] is, in fact, included in the file.

## Slide 6: Example of Timings and Logic
Device B
has
staged
turn-on/
turn-off
in this
case
study

## Slide 7: Describing Buffer X with Traditional IBIS
Need [Driver Schedule]!
Contention poses no issue for IBIS per-se
    Buffer description does not “care” about other buffer states
    Most tools support multiple-driver topologies
  Unusual logic is a minor hurdle
    Device A duty cycle for logic “1” or ”0” is 25% high V /75% low V
    Device B is in high-impedance (high-Z) state for logic “0”
    Device B duty cycle for logic “1” is ~ 75% high V /25% high-Z
    Contention (and buffer impedances) creates final interface states
    Can handle logic at tool level, without special IBIS considerations
  Describing Device B requires only a few IBIS features
    Open-source, using traditional I-V and V-t tables, plus C_comp
    Buffer uses stages of different impedances
    Stages are driven by a fixed internal clock, unrelated to interface switching speed
Notes: Time does not permit discussion about unusual logic treatment here; a separate discussion can be held

## Slide 8: [Driver Schedule] Refresher (IBIS Cookbook)
[Driver Schedule] describes buffer behavior using individual [Model]s controlled by timings given relative to the input stimulus
“Some applications require that a buffer change its strength or transition speed characteristics at fixed times after input stimulus changes.”
[Driver Schedule]
|
| Model_Name Rise_on_dly Rise_off_dly Fall_on_dly Fall_off_dly
|
P0_stage 0.0000ns 5.0000ns NA NA
N0_stage 0.0000ns NA 0.0000ns NA
N1_stage 0.3006ns NA 0.0549ns NA
N2_stage 0.5481ns NA 0.1163ns NA
Inverter [Driver Schedule]
Rise_on_dly = NA
Rise_off_dly = 0 ns
Fall_on_dly = NA
Fall_off_dly = 0 ns
P0 on for 5 ns at/after
rising input edge
N0, N1 and N2 staggered
after any input edge
Notes: It’s weird! Filling out all four columns isn’t necessary, as tools can make assumptions about missing behaviors from data in the filled columns.

## Slide 9: Specific Implementation
Device B IBIS Implementation
    Five “legs” or stages, [Pullup] only
    First stage turns on immediately
    Following stages turn on at regular periods
    Only Rise_on_dly and Fall_on_dly used
    Stage impedances range from ~1500 ohms to ~100 ohms
    “Top-level” buffer [Model] is a duplicate of leg 1, plus clamp data

## Slide 10: Hurdles to Cross-Tool Operation
[Driver Schedule] has not been consistently supported in the past
    Behavior under different tools varied widely (and may still)
    BIRD88.3 written to ensure better signal initialization of [Driver Schedule]
To build confidence, we need a way to verify tool output vs. transistor- level design performance and intent
    Traditional IBIS models are created from transistor-level data
    Correlation using same conditions produces the same IBIS I-V, V-t data
    [Driver Schedule] combines several buffers, making correlation of tool interpretation of IBIS data critical
IBIS has such a feature:
[Test Data], in Version 4.0
Notes: BIRD88.3 explicitly defined the startup logic states and other relationships within [Driver Schedule]

## Slide 11: [Test Data] and [Test Load]
[Test Data]
    Contains simple rising and/or falling V-t tables (typical, minimum and maximum)
    Supports single-ended and differential buffers
    Links to a particular model by [Model] name
    Links to a particular load by [Test Load] name
    Not actually for use in simulations of the associated buffer – correlation only!
[Test Load]
    Describes the loading used for the [Test Data] waveform
    Supports parallel and serial elements, plus at-driver and receiver measurement points
Procedure for “Buffer X” Device B and [Test Data]/[Test Load]
    Simply imported the transistor V-t data for a resistive at-pad load from a spreadsheet
      1 Rising Waveform and 1 Falling Waveform, “Near End”, single-ended
    Specified [Test Load] as 330 ohms, 0 V, “Near End”
V_term2
V_term1
Ls_near
Rs_near
Rp1_far
Rp1_near
Rp2_far
Rp2_near
C1_near
C2_near
Ls_far
Rs_far
C2_far
C1_far
Notes: The actual buffer model is only distributable under NDA; no actual information from the model file is included here.

## Slide 12: Testing “Buffer X”
“Buffer X” with
Resistive Load
Tool B:
External
EDA SI Tool
& IBIS
[D. Schedule]
Raw
Transistor-
Level
Waveform
([Test Data])
Tool A:
External
EDA SI Tool
& IBIS
[D. Schedule]
How do the tools “measure up?”
Notes: Names have been removed, to permit more open comparison between them. Note the figure may seem familiar…

## Slide 13: Correlation Overlays – Falling Edge
Min corner, 330 ohm load to ground at pad
Notes: Using same plotting and timestep options between the IBIS tools

## Slide 14: Correlation Overlays – Falling Edge Zoom
Zoom reveals potential value of [Test Data]
Notes: Key question – would this additional feature in the waveform make a difference to design or performance?

## Slide 15: Correlation Overlays – Rising Edge
Min corner, 330 ohm load to ground at pad

## Slide 16: Correlation Overlays – Rising Edge Zoom
Zoom reveals potential value of [Test Data]

## Slide 17: Correlation Overlays – Rising Edge Zoom (2)
Again, zoom reveals potential value of [Test Data]

## Slide 18: Findings from [Driver Schedule] and [Test Data]
First, the bad news…
    Neither of the tools tested supported [Test Data]/[Test Load]
    The keywords did not cause errors per se, but were simply ignored
    Therefore, no automated means was available for comparing tool output to [Test Data] information
  Now the good news…
    Manual comparison of tool to transistor-level data showed good correlation
    Tools are therefore processing [Driver Schedule] (in this case) correctly
    Comparisons using [Test Data] transistor-level waveforms vs. tool outputs can reveal tool usage and user setup issues
    User must decide which differences are relevant to design targets
[Test Data] has value in correlation,
particularly if comparisons could be automated
Extracting [Test Data] places no significant burden
on design/simulation engineer
Notes: Customers may not be happy about receiving a model they can’t automatically correlate – this speaks to an automation enhancement needed in today’s tools.

## Slide 19: Comments
[Test Data] can add value!
    For tool vs. transistor or lab correlation, [Test Data] is a clear advantage
    The keyword is very easy to implement, for simple loads
Creating [Driver Schedule] models poses problems for model makers
    Syntax is difficult to understand, even with examples
    Data almost impossible to gather without:
      Applying math to extracted tables
        Buffer ends cycle with apparent impedance of leg 1 || leg 2 || leg 3…
        We want each leg in its own [Model] section
        Design may not enable single-leg transient V-t extraction
      “Cutting” the schematic into pieces
      Relying on design test modes (not always available)
  Annoyance: Vref, Cref, Rref, Vmeas required for individual leg [Model]s
    Clearly Vref, etc. are only really are needed at the top-level
    Individual legs may not even pass through Vmeas level

## Slide 20: Recommendations
[Test Load]
    Support loss descriptions for transmission lines
    Clarify whether load is at-pad or at-pin (intent seems to be at-pad)
  [Test Data]
    Permit custom, defined data patterns (e.g., PRBS)
    Clarify support of series devices
    Clarify distinction between simulated and lab-captured data
    Add Cookbook entries for both [Test Data] and [Test Load]
  [Driver Schedule]
    Remove requirement for Vmeas, etc. in scheduled models (below top-level)
    Add additional examples to Cookbook and specification
    Permit “Combination [Model]” or additive model data, rather than require data for isolated legs individually
      Pushes math manipulation of driver data to tool rather than to maker
      Would probably drive tool-to-tool divergence of results
Thanks to the IBIS Quality Task Group for
several of the suggestions above and their
continuing [Test Data] analysis!

## Slide 21: Q & A