## Slide 1: Power Integrity for Single Ended Systems
Vishram S. Pandit, Myoung Joon Choi
Intel Corp.
IBIS Summit at DAC
June 10, 2008
Acknowledgements:
Michael Mirmak, Julius Delino, Woong Hwan Ryu, Sanjiv Soman
Copyright © 2008, Intel Corporation. All rights reserved.

## Slide 2: Outline
  Objective: To demonstrate the Power Integrity (PI) methodology for Single ended systems with the emphasis on the buffer models.
  Single Ended systems
    Driver Types
      Open drain, Open source, Push-pull
    Termination schemes for push-pull
      Vss, Center-tap, Vcc termination
  PI only analysis:
    Icc(t) generation and usage
  PI/SI analysis
    PD noise impact on the jitter and voltage margin
  IBIS* involvement

## Slide 3: Open Sink Driver
Rt1
A
i1+i2
Z0
i1
Driver
i2
A
A
i2 Return Current
Other
PDN
Elements
(Pkg , Board,
VR)
Rt2
Vcc term
A
Ammeter
Cdie
Vss referenced Tline
Vcc
Vss
Receiver
PDN: Power Distribution Network

## Slide 4: Open Source Driver
A
Z0
i1+i2
Vss
i2
Rt1
A
i2 Return current
Rt2
Vss term
A
Ammeter
Cdie
i1
Other
PDN
Elements
(Pkg , Board,
VR)
Driver
Vss referenced Tline
Receiver
Vcc
A

## Slide 5: Push-pull Driver, Vcc Termination
R
R
A
i1+i2
Z0
i1
Vss
A
Driver
Receiver
i2
R
A
A
i2 Return Current
Other
PDN
Elements
(Pkg , Board,
VR)
A
Vss ref. Tline
Vcc
Cdie
A
Ammeter
P1
P2
P3

## Slide 6: Push-pull: Other terminations
R
R
Z0
A
R
R
R
A
Vss term
CTT: Center Tap Term
A
A
Ammeter
Cdie
P1
P2
A
A
P3
P4
P4
Vss ref. Tline
Vss
Driver
Receiver
Vcc
Other
PDN
Elements
(Pkg , Board,
VR)

## Slide 7: Push-pull Driver
Four push-pull devices are used with SI/PD† model
Currents are probed at the Vcc and Vss of the Driver node
Currents at P1 node (Vcc)
mA
mA
Vcc Term
CTT
Vss Term
Current Profiles at the Driver power domains vary significantly based on the termination schemes at the Receiver
    Need to consider realistic termination schemes and not just capacitive loading
Currents at P2 node (Vss)
† PD: Power Delivery

## Slide 8: PDN Currents at Driver
Receiver Term Driver currents | Vcc Term | Vss Term | CTT
Vcc Currents Ivcc | Crowbar current | DC Step + Crowbar current | ½ DC step + Crowbar current
Vss Currents Ivss | DC Step + Crowbar current | Crowbar current | ½ DC step + Crowbar current
  Driver PDN currents are dependent on termination schemes at the Receiver
    DC step due to termination scheme
    IBIS* application: Does BIRD 95 enable to include Ivcc and Ivss based on termination schemes?
  Crowbar currents for all configurations: Behavioral models need to include accurate Crowbar currents

## Slide 9: Push-pull Driver
Currents at P3 node (Vcc)
Current at P4 node (Vss)
mA
A
Vcc (P3) currents: di/dt for Vcc Term is higher than that for CTT.
System level model need to be considered with Driver and Receiver PDN
Four push-pull transistors are used with SI/PD model
Currents are probed at the Vcc and Vss of the Receiver node
Vcc Term
CTT
Vss Term

## Slide 10: PDN currents at Receiver
Receiver Term Receiver currents | Vcc Term | Vss Term | CTT
Vcc Currents | DC Step | N/A | ½ DC step
Vss Currents | N/A | DC Step | ½ DC step
  CTT produces smaller step than other two
    Due to the resistor divider the DC step is half of that for the other cases
  Smaller the step, smaller is the di/dt.

## Slide 11: Icc(t) Generation
Icc(t) is Ivcc and Ivss at the Driver PD node w.r.t. time
    It provides a means to estimate the noise on the PDN as a function of SSO
      Advantages: It gives first pass noise information
      Disadvantages: It cannot model the buffer/ PDN dynamic interaction.
Icc(t) for a single Driver is expanded to the interface
    It can be scaled by total number of Drivers switching at the same time.
Then, generate a PDN network and test different patterns, as PDN has some resonance.
    Maximum data rate
    Data rate at PDN resonance frequency
    Interconnect resonance frequency

## Slide 12: Icc(t) Usage Models
For calculating the PDN noise
    Different currents in Vcc and Vss need to be accounted for.
    Need two out of three currents for modeling: Ivcc, Ivss and Ipad
    IBIS* application: BIRD 95 can include these currents
Transmission lines
    For PDN-noise only analysis, Use individual transmission lines OR use a scaled model of multiple transmission line. Terminate the line/ lines at the far end
Receiver-Vcc
Driver-Vcc
Vss
Ivcc
Ipad
R1
Z1
Ivss
Vss referenced Tline

## Slide 13: Example: Noise Profiles
Noise at the Driver and Receiver End for two termination schemes
Receiver side noise for
Vcc term
Receiver side noise for CTT
Driver-noise
Driver side noise is very similar for CTT and Vcc terminations
Receiver side noise is different based on the termination schemes.

## Slide 14: PDN Noise impact on timing
SI-PI
SI only
SI-PI comprehensive deck is generated
10 Buffers switching simultaneously 1010
Cycle to cycle DQ-DQS jitter is measured.
Inclusion of Icc(t) from different no. of buffers on power node, produces the jitter in SI-PI simulations.
On-die PDN
Package
Board
Receiver
And
Term.
Ivpd X N

## Slide 15: PDN Optimization
System Level PI-SI models are generated
Icc(t) is created for 66 buffers
Two cases are studied: 1333MTPS, 267MTPS
mV
267MTPS
1333 MTPS
EYE margin vs. Cdie
EYE diagram includes effects due to ISI, crosstalk and SSO
Cdie/ IO is varied and EYE margin is plotted.
Higher the Cdie, lower is the SSO noise, hence higher is the EYE margin

## Slide 16: Conclusions
Power Integrity for the single ended systems
    SSO Noise on the PDN
      Icc(t) computation comprise of
        Termination schemes, Driver type, Data Pattern
    Jitter due to PDN
      Driver side PD to signal coupling (primary source)
      Channel PD to signal coupling
    EYE margin impact due to PDN
      Cdie optimization
Behavioral Buffer Model needs to have
    Ivcc, Ivss, Ipad
    Dependency on the termination schemes
    Ability to have noisy voltage source
  Can IBIS* BIRD95/98 address all that?