## Slide 1: Simple ODT Extraction
Bob Ross
Design Automation IBIS Summit
Anaheim, California
June 15, 2010
bob@teraspeed.com

## Slide 2: ODT = On-Die Termination
Earlier presentation for combined Thevenin equivalent “pullup” and “pulldown” ODT
  DEC September, 2005
  http://www.eda.org/ibis/summits/sep05/ross2.pdf
Simplified process
  Tuned for calculating Typ/Min/Max clamps at the same time
  Defaults to proportional allocation of currents
Example of DDR2 [Submodel] extraction

## Slide 3: Default DEC Algorithm (2005) Proportional Allocation of Currents
0 ma
Vg
Vp
Total I-V
[Gnd Clamp]
[Power Clamp]
Calculate
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta
delta*Ip/(Ip+Ig)
delta*Ig/(Ip+Ig)

## Slide 4: Simple Transformation Process (One Clamp at a Time)
[Gnd Clamp] extraction
  Extract total I-V curves just beyond 0 to Vdd(max) range
    E.g., -0.2 to Vdd(max)+0.1
  Transform curves to the range I(V(0) and I(Vdd(typ/min/max))
  Extrapolate at both ends
[Power Clamp] extraction
  Same process, but use the Vdd referenced data from about -0.2 to Vdd(max)+0.1

## Slide 5: Real Example for 75  ODT DDR2 [Submodel]
Vdd Typ/Min/Max = 1.8/1.7/1.9 V
Modified gc* and pc* ranges:
  -0.2 V to 2.0 V from s2ibis2/3 setup
Spread sheet processing (but direct equation implementation possible)
(Here, ESD clamps at Gnd and Power extracted separately by turning off ODT and modeled at top-level)

## Slide 6: Total I-V and [Gnd Clamp] Typ/Min/Max by Mapping
Calculated ODT [Gnd Clamp]
0 V referenced Total I-V gc*
0,0

## Slide 7: Map Typ/Min/Max 0 V to 1.8/1.7/1.9 V Ranges
Typ at 1.8V
Max at 1.9 V
Min at 1.7 V
After mapping, extrapolate both tables (not shown)

## Slide 8: Total I-V to [Power Clamp] Typ/Min/Max Mapping – Same Process
Vdd referenced Total I-V pc*
Calculated ODT [Power Clamp]
0,0

## Slide 9: [Gnd Clamp] and [Power Clamp] with Extrapolations for [Submodel]
[Gnd Clamp]
[Power Clamp]
ESD clamps, if needed

## Slide 10: Summary of Simplified Process (One Clamp at a Time)
Use Total I-V just beyond 0 to Vdd(max) range
  0 V based for [Gnd Clamp] (gc*)
  Vdd based for [Power Clamp] (pc*)
Map Total I-V curves to (0, 0) value and I(Vdd(typ,min,max) values
Extrapolate to full –Vdd to 2*Vdd range
(Easy subtractions for including ESD clamps possible, but not covered here)