## Slide 1: IBIS Quality Control Through Scripting
Justin Butterfield
DAC IBIS Summit
San Francisco, CA, USA
June 5, 2012

## Slide 2: Outline
Motivations
Scripts to automate IBIS generation
  Building an IBIS template
  Importing table data into the template
  Formatting package RLC data
Script for checking IBIS parameters
Scripts for EBDs
  EBD generation
  EBD connectivity report

## Slide 3: Why Use Scripts for Quality Control
IBIS files can be very large and complex
Micron 2Gb DDR3 SDRAM IBIS model statistics:
  154 [Model]s, 20 [Submodel]s, 40+ parameters per [Model]
Large number of [Model]s due to combinations of features
  Including: Drive strength, ODT, Speed Grade (Vinl/Vinh levels & Overshoot)
  Most [Model]s only vary a few parameters
Prone to copy and paste errors and typos
  Incorrect Vinl/Vinh, Overshoot, and C_comp values
  Incorrect table data and Submodel mapping
ibischk does not check accuracy!

## Slide 4: IBIS Generation Flow
Build an IBIS template
Generate table data (I-V, V-t, Ramp, etc.)
Import table data into IBIS template
Format and add package models
Check IBIS file
Generate EBD files
Check EBD files

## Slide 5: Build IBIS Template: Concept
IBIS Template = IBIS file without table data
[Model] INPUT_1600
Model_type Input
|
Vinl = 575.000mV
Vinh = 925.000mV
| typ min max
C_comp 0.600pF 0.500pF 0.700pF
|
[Model Spec]
Vinl 0.5750V 0.5375V 0.6125V
Vinh 0.9250V 0.8875V 0.9625V
|
[Voltage Range] 1.5000V 1.4250V 1.5750V
[Temperature Range] 50.0 110.0 0.0
|
|***************************************************************************
| (table data here)
|***************************************************************************
[Model] INPUT_1866
...

## Slide 6: Build IBIS Template: Requirements
Define base models
  E.g. DQ, DQS, CLK
  These can match the [Model Selector] names
Distinguish between IBIS parameters that are
  Standard – fixed for the interface specification
    E.g. [Voltage Range], Vinl/Vinh, Vref/Cref/Rref, Overshoot
  Variable – vary from device to device
    E.g. C_comp, [Temperature Range]
Script builds the template ensuring consistent results

## Slide 7: Build IBIS Template: Input Examples
Standard parameters
  Read in as a predefined technology file
  Tables of parameters for combinations of [Models] to be created
Variable parameters
  Input text file specified by the user
  Directs the script to a subset of the technology file
Base_Model | DQ | DQ | DQ | DQ | DQ | DQ
Speed_Grade | 800 | 1066 | 1333 | 1600 | 1866 | 2133
Vil_ac | -0.175 | -0.175 | -0.15 | -0.15 | -0.135 | -0.135
Vih_ac | 0.175 | 0.175 | 0.15 | 0.15 | 0.135 | 0.135
Vil_dc | -0.1 | -0.1 | -0.1 | -0.1 | -0.1 | -0.1
Vih_dc | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
D_overshoot_ampl_h | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
D_overshoot_ampl_l | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
D_overshoot_area_h | 0.25n | 0.19n | 0.15n | 0.13n | 0.11n | 0.10n
D_overshoot_area_l | 0.25n | 0.19n | 0.15n | 0.13n | 0.11n | 0.10n
Speed_Grades | 1066 | 1600 | 1866 | 2133
C_comp | typ | min | max
DQ | 1.200 | 1.125 | 1.275
DQ_ODT20 | 1.078 | 0.966 | 1.223
DQ_ODT30 | 1.118 | 1.019 | 1.240
DQ_ODT40 | 1.134 | 1.044 | 1.238
DQ_ODT60 | 1.161 | 1.074 | 1.259
DQ_ODT120 | 1.174 | 1.097 | 1.255

## Slide 8: Build IBIS Template: Process Flow
Technology
Parameter File
Basic Parameters
Base Models & Attributes
Parameter Tables
User
Parameter File
Build List of [Model]s/ [Submodel]s
Create Parameter Data Structures
Print Template Section for each [Model]/[Submodel]

## Slide 9: Build IBIS Template: Details
Build list of [Model]s
  Loop over base models and features requiring separate [Model]s
  Preserve the attributes of each [Model]
Data structures created for each parameter
  Data{Base_Model}{Speed_Grade}{Parameter_Name}
Iterate for each [Model] to print the template section
  Look up parameter values in the data structures
  Subroutines to print each set of parameters to the template
  Different cases of print routines for each Model_type

## Slide 10: Import Table Data
Read in the table data from IBIS files with a single [Model]
Use a mapping file to assign each [Model] to its table data
Script pastes the table data into the IBIS template
[Model] DQ_34
...
[Pulldown]
...
[GND Clamp]
...
[Pullup]
...
[POWER Clamp]
...
[Ramp]
...
[Falling Waveform]
...
[Rising Waveform]
...
Table Data (dq_34.ibs)
DQ_34_1600 dq_34.ibs
DQ_34_1866 dq_34.ibs
...
Mapping File
[Model] DQ_34_1600
Model_type I/O
...
|************************
| (table data here)
|************************
[Model] DQ_34_1866
Model_type I/O
...
|************************
| (table data here)
|************************
IBIS Template

## Slide 11: Format Package RLC Data
Create [Package] and [Pin] list RLC data from a spreadsheet
  Align columns and calculate typ/min/max [Package] values
Calculate Z0 and time delay then check for outliers
[Pin] | signal_name | model_name | R_pin | L_pin | C_pin
B3 | DQ0 | DQ | 0.307 | 1.337E-09 | 3.680E-13
C2 | DQ2 | DQ | 0.404 | 1.710E-09 | 4.585E-13
C7 | DQ1 | DQ | 0.288 | 1.258E-09 | 3.676E-13
C8 | DQ3 | DQ | 0.406 | 1.598E-09 | 4.789E-13
Signal | Zo | Time Delay
DQ0 | 60.28 | 2.218E-11
DQ2 | 61.07 | 2.800E-11
DQ1 | 58.51 | 2.151E-11
DQ3 | 57.76 | 2.766E-11
[Package]
| typ min max
R_pkg 307m 208m 421m
L_pkg 1.64nH 1.059nH 2.514nH
C_pkg 0.35pF 0.261pF 0.479pF
|
[Pin] signal_name model_name R_pin L_pin C_pin
B3 DQ0 DQ 307m 1.337nH 0.368pF
C2 DQ2 DQ 404m 1.710nH 0.459pF
C7 DQ1 DQ 288m 1.258nH 0.368pF
C8 DQ3 DQ 406m 1.598nH 0.479pF

## Slide 12: IBIS Parameter Check
Script to search the IBIS file for a parameter
  E.g. C_comp, Vinl/Vinh, Vref/Cref/Rref, Overshoot, etc.
Creates a report detailing the parameter’s values in each [Model]
Results can be filtered by [Model] names
DQ_34_1066 | C_comp | 1.200pF | 1.125pF | 1.275pF
DQ_34_ODT20_1066 | C_comp | 1.078pF | 0.966pF | 1.223pF
DQ_34_ODT30_1066 | C_comp | 1.118pF | 1.019pF | 1.240pF
DQ_34_ODT40_1066 | C_comp | 1.134pF | 1.044pF | 1.238pF
DQ_34_ODT60_1066 | C_comp | 1.161pF | 1.074pF | 1.259pF
DQ_34_ODT120_1066 | C_comp | 1.174pF | 1.097pF | 1.255pF

## Slide 13: Build EBD Model
Generate EBD model from spreadsheet data
  Useful for fixed topologies such as stacked die packages
  Input RLC & Len values and Pin & Node connections
[Path Description] CS0#
Pin J2
Len=1 R=0.086 L=1.067e-09 C=5.879e-13 /
Fork
Len=0 R=0.054 L=2.944e-10 C=4.220e-14 /
Node U1.119
Endfork
|
[Path Description] BA0
Pin J3
Len=1 R=0.110 L=1.533e-09 C=7.118e-13 /
Fork
Len=0 R=0.054 L=2.950e-10 C=4.230e-14 /
Node U1.117
Endfork
Fork
Len=0 R=0.060 L=3.254e-10 C=4.666e-14 /
Node U2.117
Endfork
Pin | Signal | Sub R | Sub L | Sub C | Ref.Pin | Ref.Pin
J2 | CS0# | 0.086 | 1.067E-09 | 5.879E-13 | U1.119 | 
J3 | BA0 | 0.110 | 1.533E-09 | 7.118E-13 | U1.117 | U2.117
Substrate RLC
Wire Bond RLC

## Slide 14: EBD Connectivity Report
Report showing EBD Pin to Node
  Script prints out an entry for each Pin to Node connection
Helpful for checking:
  EBD Path names and IBIS Signals match
  Correct number of node connections exist on each Path
EBD |  |  | IBIS |  |  | 
Path Name | Pin | Node | File Name | Component | Signal | Model
DQ31 | B5 | U0.6 | g69a_bd.ibs | MT42L64M32D1G69A | DQ31 | DQ
DQ31 | B5 | U1.6 | g69a_bd.ibs | MT42L64M32D1G69A | DQ31 | DQ
DQ29 | B6 | U0.9 | g69a_bd.ibs | MT42L64M32D1G69A | DQ29 | DQ
DQ29 | B6 | U1.9 | g69a_bd.ibs | MT42L64M32D1G69A | DQ29 | DQ
DQ26 | B7 | U0.13 | g69a_bd.ibs | MT42L64M32D1G69A | DQ26 | DQ
DQ26 | B7 | U1.13 | g69a_bd.ibs | MT42L64M32D1G69A | DQ26 | DQ
DQ25 | C9 | U0.15 | g69a_bd.ibs | MT42L64M32D1G69A | DQ25 | DQ
DQ25 | C9 | U1.15 | g69a_bd.ibs | MT42L64M32D1G69A | DQ25 | DQ
DQ30 | D7 | U0.7 | g69a_bd.ibs | MT42L64M32D1G69A | DQ30 | DQ
DQ30 | D7 | U1.7 | g69a_bd.ibs | MT42L64M32D1G69A | DQ30 | DQ

## Slide 15: Conclusions
Cons
  Must invest time to write and validate scripts
  Risk of propagating errors
  Possibility of incorrect usage by inexperienced users
Pros
  Improved model consistency and quality
  Efficient checks on large models
  Save time creating and validating models