## Slide 1: Surrogate Model-based High-speed IO Macromodel
IBIS Summit, DAC 2012
Ting Zhu*↑, Paul D. Franzon* and Michael B. Steer*
{tzhu, paulf, mbs}@ncsu.edu
*ECE, North Carolina State University, Raleigh, NC
↑Signal Integrity Group, Enterprise Server Storage, Hewlett-Packard
DAC 2012 IBIS Summit
San Francisco, CA
June 5th, 2012
Notes: <number>

## Slide 2: Motivation
<number>
IBIS models
- Simple, portable, IP-protected, and fast in simulation.
- Model the responses in the worst-case PVT situations only.
- Unable to simulate continuous variations.
- Unsuitable for statistical analysis.
- Limits in representing complex effects dependent on multi-parameters.
This work
- To develop high-fidelity and continuous scalable high speed IO macromodels.
IBIS Summit, DAC 2012

## Slide 3: Proposed Surrogate-based IBIS Model
<number>
IBIS Summit, DAC 2012
An equivalent circuit structure with lumped elements capturing the static and dynamic circuit behaviors
Use surrogate modeling methodology to model each element accurately over a range of PVT parameters.
Model structure
Notes: <number>

## Slide 4: Key Features
<number>
Model physically-based elements individually rather than approximating the overall dynamic behavior.
Handle multi-dimensional parameters and highly nonlinear circuit characteristics.
Scalable over continuous PVT parameters and all of the parameters are directly accessible in simulations.
Stores data in numerical expressions which are portable and IP-protected, reducing both data size and the uncertainty caused by ad hoc interpolation.
IBIS Summit, DAC 2012

## Slide 5: Publications
<number>
T. Zhu, M. B. Steer, and P. D. Franzon, “Accurate and scalable IO buffer macromodel based on surrogate modeling,” IEEE Trans. on Components, Packaging and Manufacturing Technology, vol. 1, no. 8, pp. 1240–1249, Aug. 2011.
M.B. Yelten, T. Zhu, S.Koziel, P.D.Franzon, M.B.Steer, “Demystifying surrogate modeling for circuits and systems,” IEEE Circuits and Systems Magazine, vol.12, no.1, pp.45-63. 2012
T. Zhu and P.D. Franzon.“ Application of surrogate modeling to generate compact and PVT-sensitive IBIS models,” in Proc. 18th Electrical Performance of Electronic Packaging and Systems, Portland, OR., pp. 77-80, Oct. 19-21, 2009.
IBIS Summit, DAC 2012

## Slide 6: Technical Approach - Surrogate Modeling
<number>
IBIS Summit, DAC 2012
Definition
Computational cheap(er) approximation models, also called metamodels, response surface models.
Basic modeling problem
Predict the global behavior of the system with limited number of samples.
- approximation error
Data
Surrogate model
Fitting

## Slide 7: Adaptive Modeling Flow
<number>
IBIS Summit, DAC 2012
Variations, Circuits, Configurations
SUrrogate Modeling
(SUMO) toolbox
Ghent Univ.
Surrogate Models Equations
Multi-dimensional model surface plots
Notes: <number>

## Slide 8: Modeling Data Extraction
<number>
IBIS Summit, DAC 2012
(a) Pull-up current
(b) Pull-down current
Vs: 0.7VCC ~1.3VCC ; P = ΔVth /Vth0: -0.2 ~ 0.2
T: 0 ~ 100 ℃
Vpu: -VCC ~ +2VCC
Vpd: -VCC
~ +2VCC
(c) Output Capacitance
(d) Timing coefficients
Vbias: -VCC ~ +2VCC
time:
0 ~ 3 ns
Notes: <number>

## Slide 9: Model Surface Plots - Ipu
<number>
IBIS Summit, DAC 2012
Slice plot of 4D rational function model Ipu (Vs, Vpu, T, P).
3 slices in each plot is for three temperatures at 100 ℃, 50 ℃, 0 ℃.
P = ΔVth /Vth0
T=
Notes: <number>

## Slide 10: Verilog-A Implementation
<number>
IBIS Summit, DAC 2012
analog function real Ipu;
input vsi, vpui, tempi, deltavthi;
real vsi, vpui, tempi, deltavthi;
begin
Vpu = (vpui - 1.65) / 4.95;
Vs = (vsi - 3.30) / 9.90e-01;
deltavth = (deltavthi - 0) / 2.00e-01;
temp =(tempi - 50) / 50;
Ipu = -2.983745e-02 - 4.983961e-02*Vpu + 1.382028e-01 *pow(Vpu,2) - 2.673657e-01 *pow(Vpu,3)+ 2.732403e-03*temp +5.928865e-03*pow(Vpu,1)*temp -1.184873e-02*Vs-1.805515e-01
*pow(Vpu,2)*temp + 1.877605e+04 *pow(Vpu,9)- 5.646272e-02 *Vpu*Vs - 7.271323e-02 *pow(Vpu,3)*temp+ 1.641660e-03*deltavth + ...;
end
endfunction
- Verilog-A IBIS template (M. LaBonte and A. Muranyi)
- Implementation example: model equation for pull-up current Ipu (all the inputs are normalized to -1 to 1)
Notes: <number>

## Slide 11: Simulation Results – Supply Voltage Variations
<number>
IBIS Summit, DAC 2012
IBIS
Transistor
Surrogate
 | Max Timing Error | Max Relative Voltage Error
Traditional IBIS | 128 ps | 28.11％
Proposed model | 79 ps | 6.77％
Notes: <number>

## Slide 12: Simulation Results (cont.)
<number>
IBIS Summit, DAC 2012
Pseudorandom bit sequence (PRBS) test
Max timing error 0.07ns (3.5% bit-time)
Max relative voltage error 6.45%
Surrogate-IBIS model matches transistor-level model very well
Surrogate
Transistor
Eye-diagram width (W) difference at height
(H) = 1V is 0.0297ns (1.48% of the bit-time)
Notes: <number>

## Slide 13: Summary
<number>
The proposed surrogate-based IBIS model
Integrates equivalent circuit models and adaptive multivariate surrogate modeling for IO buffer macromodeling.
Useful in developing scalable macromodels with application to analysis of IO buffers with highly nonlinear circuit characteristics and multiple variations.
IBIS Summit, DAC 2012

## Slide 14: Q&A
<number>
Thanks for your attention!
Contact: Ting Zhu (tzhu@ncsu.edu)
IBIS Summit, DAC 2012

## Slide 15: Backup: Surrogate Modeling Techniques
<number>
IBIS Summit, DAC 2012
Initial sampling | Latin Hypercube
Adaptive sampling | Error-based, Density-based
Model template | Kriging model, Rational function
Validation | Cross-validation, Validation set
Error function | Root relative square error (RRSE) Maximum relative error (MRE)
Rational function
P and Q are polynomial functions
Kriging function
Notes: <number>
[Notes] Put this page into backup