## Slide 1: IBIS Interconnect BIRD
Walter Katz
Signal Integrity Software, Inc.
IBIS Summit, San Francisco, CA
June 5, 2014

## Slide 2: Overview
IBIS Interconnect Task Group
  Meets Wednesdays 8AM PDT
  http://www.eda.org/ibis/interconnect_wip/
Similar Approach for Both IBIS and EBD
Interconnect Modeling Capability
IBIS (.ibs) Interconnect Model Terminals
Touchstone Model Shortcut
Pre and Post Layout IBIS Files
Corners
[Interconnect Model Selector]
[Interconnect Model]
[Begin Model]
Terminal
Terminals
Next Steps

## Slide 3: Similar Approach for IBIS and EBD
IBIS (.ibs) Interconnect Model Terminals
  Pins ([Pins])
  Die Pads
  Buffers
EBD (.ebd) Interconnect Model Terminals
  Pins ([Pin List])
  reference_designator.pin

## Slide 4: IBIS Interconnect Model Terminals
Pins
Die Pads
  Signal (I/O)
  Supply (POWER and GND)
Buffers
  Signal (I/O)
  Supply
    Pullup Reference
    Pulldown Reference
    Power Clamp Reference
    Ground Clamp Reference
    External Reference

## Slide 5: Touchstone Model Shortcut
Touchstone models can be referenced directly without wrapping them in an IBIS-ISS subckt:
[Begin Model] TouchstoneSortucutExample
Source Touchstone_File
File Typ xyz.s2p
Number_of_Terminals 2
Terminals Pin:A1 Buf:A1
[End Model]
Is equivalent to:
[Begin Model] TouchstoneSortucutExample
Source IBIS_ISS
File Typ xyz.mod
Subckt Typ xyz
Number_of_Terminals 3
Terminals Pin:A1 Buf:A1 GND
[End Model]
File xyz.mod
.subckt xyz 1 2 Ref
S1 1 2 Ref mnname=s_xyz
.model s_xyz TSTONEFILE=‘xyz.s2p’
.ends xyz

## Slide 6: Pre and Post Layout IBIS Files
Post Layout
  Signal (I/O) Terminals
    Pin, Die Pad and Buffer terminals are referenced by Pin_name (Pin Number)
  Supply Terminals
    Pin terminals are referenced by Pin_name or Signal_name
    Die Pad terminals are referenced by Die_Pad_name or Signal_name
    Buffer terminals are referenced by Pin_name or Signal_name
Pre Layout
  Signal and Supply terminals can also be referenced by Model_name

## Slide 7: Corners
File, Subckt and Parameter can have either a single value or three corner values
If three values then they can be interpreted as
  Delay
    Typ/Slow/Fast
  Crosstalk
    Typ/Min/Max
  …
File_Tip, Subckt_Tip and Parameter_Tip
  Subparameters that can be used to document the three corner conditions for each parameter

## Slide 8: [Interconnect Model Selector]
[Interconnect Model Selector]
  <Interconnect Model> * | In this file
  <Interconnect Model> <File Name>
[End Interconnect Model Selector]

## Slide 9: [Interconnect Model]
[Interconnect Model] <Interconnect Model>
  [Begin Model] <interconnect model name>
    …
  [End Model]
  [Begin Model] <interconnect model name>
    …
  [End Model]
  …
[End Interconnect Model]

## Slide 10: [Begin Model]
[Begin Model] <interconnect model name>
  Source <IBIS_ISS | Touchstone_File>
  File <Typ | Min | Max> <file name>
  File_Tip <Typ | Min | Max> <Tip>
  Subckt <Typ | Min | Max> < Subckt >
  Subckt_Tip <Typ | Min | Max> <Tip>
  Parameter <name> <Typ | Min | Max> <Value>
  Parameter_Tip <name> <Typ | Min | Max> <Tip>
  Unused_Terminal_Termination
  Number_of_Terminals <# Terminals>
  Terminal | Terminals
[End Model]

## Slide 11: Terminal
Terminal <terminal number> <Pin | DiePad | Buffer …>
One line per terminal
Supports both Pre and Post Layout
Example Terminal records
Terminal 1 Pin Pin_name M8
Terminal 2 Pad Pin_name M8
Terminal 3 Buffer Pin_name M8
Terminal 4 Buffer Pin_name M8 Pullup_Reference
Terminal 5 Pin Model_name DQ
Terminal 6 Pin Model_name DQS Diff_pos
Terminal 8 Pin Model name DQ SE
Terminal 9 Buffer Pin_name M9 Aggressor
Terminal 10 Buffer Pin_name M10 Victim
Terminal 11 Buffer Signal_name VDDQ

## Slide 12: Terminals
Terminals <terminal 1> <terminal 2> <terminal 3> …
One line lists all terminals of subckt.
Limited to Post Layout
Example Terminals records
Terminals Pin:A7 Buf:A7
Terminals Pin:A7 Pad:A7
Terminals Pin_SIG:VDD Buf_SIG:VDD
Terminals Pin_SIG:VDD Pin_SIG:VSS Buf_PUR:A7 Buf_PDR:A7

## Slide 13: Next Steps
Ongoing work refining interconnect IBIS and EBD BIRDs.
Reviewing decision to support both Terminal and Terminals
Reviewing how to handle Unconnected Terminals