## Slide 1: Co-Optimization of SerDes Channels using AMI Modeling
Walter Katz
Signal Integrity Software, Inc.
IBIS Summit, San Francisco, CA
June 5, 2014

## Slide 2: Overview
Co-Optimization background
Why Co-Optimize?
Co-Optimization Methods
Optimization Examples
Two proposals, two methods
SiSoft proposal: IBIS AMI – Tx, IBIS AMI – Rx
Optional Private Protocol
Advantages of SiSoft Approach
Next Steps

## Slide 3: Co-Optimization Background
What is Co-Optimization
  An operation in which the Equalization characteristics of the TX and RX are simultaneously adjusted to identify the optimal setting that maximizes one or more characteristics of a channels performance
    Characteristics include Eye height, Eye width, Power, BER, etc.
How does Co-Optimization work in the hardware
  Performed via communication protocol between the TX and RX via a “Back channel” connection
    Current SerDes protocols that define a backchannel
      802.3kr
      802.3bj
      PCIe Gen3

## Slide 4: Why Co-Optimize?
Emulate backchannel adaptation defined by current SerDes protocols (802.3kr, 802.3bj, PCIe Gen3)
Sequentially optimizing TX and RX SerDes settings does not maximize system margin:
“Simulating Large Systems with Thousands of Serial Links”
SI Guys / Ericsson / SiSoft
DesignCon 2012

## Slide 5: Backchannel Adaptation
Multiple standards support it
    802.3kr
    802.3bj
    PCIeG3
    PCIeG4
Simulation can model the adaptation process and predict how the hardware will converge
  Co-optimize Tx and Rx settings based on simulation of hardware adaptation protocol
  Simulated Tx and Rx settings can be compared to hardware results

## Slide 6: Protocol-Agnostic Co-Optimization
Simulation can also be used to explore different Tx – Rx combinations and optimize for different design criteria:
  Maximum eye height at Rx
  Maximum eye area at Rx
  Minimal Tx output power
  …
Tx / Rx settings for these criteria may or may not correspond to settings resulting from the standard hardware backchannel adaptation algorithms

## Slide 7: Tx Taps Optimized for Eye at Input to Rx

## Slide 8: Tx/Rx Co-Optimization Example
This is an example of the performance gains possible with backchannel adaptation approaches

## Slide 9: Tx/Rx Co-Optimization: Power
Total CPM (Consolidated Power Metric)
Traditional Optimization > 37,500
Optimization w. Tx Power < 9,000
These types of performance gains require more than just emulating hardware adaptation protocols

## Slide 10: Co-Optimization Methods
Time-Domain (GetWave) Training (Backchannel)
  Targeted at emulating hardware adaptation protocol
    Training may take millions of UI to converge
    Assuming just 106 UI, simulations will take ~ 1 minute
    5000 channels will take ~5000 minutes (~100 hours)
Statistical (Init) Co-Optimization
  Targeted at exploring options and optimizing based on different metrics
    Simulation times are ~ 1 second
    5000 channels will take ~5000 seconds (~2 hours)
    System Integrators can (and do) evaluate many engineering decisions such as
      PCB materials
      IC Vendor and buffer IP selection
      Via manufacturing technology

## Slide 11: Two Proposals
 | SiSoft | Cadence
Primary Focus | Enable System-level exploration and optimization | Model hardware backchannel adaptation
Secondary Focus | Model hardware backchannel adaptation | Enable System-level exploration and optimization
Method | Protocol-agnostic parameters in .ami files | Protocol-specific .bci files

## Slide 12: SiSoft Proposal: IBIS AMI - Tx
Add Reserved Parameters to enable Tx to publish its tap configuration
  Number of Pre-Cursor Taps
  Number of Post-Cursor Taps
  Tap Coefficient Ranges
  Tap Resolution (Tap Indexes)
  Peak to Peak Voltage
Add to Tx DLL (Init and GetWave) the ability to accept tap configuration recommendations
  Tap Coefficients
  Tap Indexes
  Tap Increments
  Peak to Peak Voltage

## Slide 13: SiSoft Proposal: IBIS AMI - Rx
Add Reserved Parameters to enable Rx to discover the Tx published tap configuration
Add to Rx DLL (Init and GetWave) the ability to adjust the TX tap configuration
Add Reserved Parameters to control training and co-optimization.
  Turn on and off training
  Define training pattern stimulus pattern

## Slide 14: Private Training Protocol
Allow a new Reserved String Parameter to both Tx and Rx to allow message to be sent back and forth between Tx Init, Rx Init, Tx GetWave and Rx GetWave.
This is a true Black Box protocol, that will work with any EDA tool that will support this message passing method.

## Slide 15: Advantages of SiSoft Approach
Existing Tx DLLs can be used for co-optimization through new Reserved Parameters
Tx model can report optimized tap coefficients through standard means (AMI Parameters_Out)
No.bci files or associated approval processes
Enables EDA tools to co-optimize channels that do not support backchannel training
Enable EDA tools to optimize beyond solutions found by hardware backchannel adaptation

## Slide 16: Next Steps
The IBIS-ATM working group meets each Tuesday from Noon – 1PM Pacific time.
The group is currently deciding which proposal to use as the basis for its efforts
Work Archives at
  http://www.eda.org/ibis/macromodel_wip/archive-date.html