## Slide 1: Main Subjects
Simulation is one of the most powerful tool to solve our problem.
To establish an appropriate simulation environment is essential.
But ・ ・ ・ ・ ・
１. What to choose as the major simulation model?
IBIS , IMIC , SPICE or X
What to do with the non-semiconductor device model?
Package , Connector , Capacitor ,Filter etc
2. When and how to make the model(s) available?
Public or NDA
3. How to judge the model accuracy?
Limitation or CAD function

## Slide 2
Contents
1. Introduction of ECALS-2
2. Status of Consumer Electronics Design
3. Discussion meeting between Users and Providers
Non-IC EMC/EMI models
3.1 Passive Components
3.2 Connectors
3.3 Discrete Semiconductor Devices
4. Conclusion

## Slide 3
3. Discussions Meeting
1st Meeting on March 18
Model Users
Fujitsu (1)
Matsushita (5)
Sony (2)
Model Providers
Passive Components
Murata (3)
TDK (1)
Connectors
Honda Communications (1)
Discrete Power Semiconductors
Shindengen (1)
Advisor
Applied Simulation Technology(1)
Total 15 members
Items to be investigated
Hard to get model
What makes getting models hard?
Possibility of collaboration by model users
and providers
Quality of models depends on
Accuracy
Purpose (SI, PI or EMI)
Frequency Range
Various End-Systems
Time to get models

## Slide 4
3. Non-IC EMC/EMI Models
3.1. Passive Components : Current Modeling Method
Measurement
Model Release
Vector Network Analyzer
S-parameters (Frequency Dependent)
Hard to accurately measure intrinsic characteristics
(Measurement contains parasitic effects)
Correlated S-parameter Models on Web and CD

## Slide 5
3. Non-IC EMC/EMI Model
3.1 Passive Components : Needs & Problems
Two applications
3D-field solver in frequency domain with linear devices
Method of curve fitting in frequency domain with knowhows
SI/PI/EMI simulation with nonlinear devices.
Start providing SPICE Models
SPICE LCRK Network model contains proprietary information
Models for EMI needs beyond 1GHz bandwidth
Interaction between components and PCB is important
Expensive and time consuming modeling
Time and cost depend on required accuracy.

## Slide 6
3. Non-IC EMC/EMI Models
3.1 Passive Components : Requirements
More accurate model at higher frequencies needs
to be described by more than 8-10 SPICE elements.
Some EMI filter has more than two terminals.
Array passive components need coupling effect.
Parasitic effect with PCB becomes important.

## Slide 7
3. Non-IC EMC/EMI Models
3.1 Passive Components : IBIS vs IMIC
IBIS
IBIS 3.1 model is too simple.
Can’t cover more than three terminal devices.
Need network description and mutual inductance.
SPICE model is convenient to time domain simulation.
SPICE LCRK Network model can improve accuracy.
SPICE models must be provided to individual customers,
because network description contains proprietary information.
IMIC

## Slide 8
3. Non-IC EMC/EMI Models
3.2 Connectors : Current Modeling Method
Modeling by Simulation
Make Model using filed solver and circuit simulators
from structure data.
Checking models by measurement
Checking by Measurement
Providing SPICE Model to individual customers
Small pin model and full pin model. (model size)

## Slide 9
3. Non-IC EMC/EMI Models
3.2 Connectors : Problems
Shielded Connectors
How to make a connector model with shield enclosure
Ground/Shield model depends on mounted on PCB
Accuracy
Modeling time and cost depend on required accuracy.
Model depends on other factors such as PCB ground.

## Slide 10
3. Non-IC EMC/EMI Models
3.3 Discrete Power Semiconductors :Current
Power diode models on Web.
Providing SPICE model to individual customers
Accurate models for power diodes and MOS needs
more complex network description for device and parasitic.
Providing Models
Current Status
Simple Power Transistor/Diode may be modeled in IBIS
by killing most of the elements.

## Slide 11
3.Non-IC EMC/EMI Models
3.3 Discrete Power Semiconductors :Future Model
IBIS
IMIC
(Table_SPICE)
AHDL
Candidates of
Power Semiconductor Model

## Slide 12
1. Most important issue for users is to get new device models timely.
Time to market is most important for set makers.
2. Simulation becomes important to reduce prototyping and cost.
Selection of components will be done by simulation with models.
3. Models of new devices to be used in the end products may be
obtained only through co-development between users and providers.
4. Users should tell model provides the required level of accuracy.
The time to get models depends on it.
Result of
Discussions between Model Providers and Users (1)

## Slide 13
5. Required level of simulation model accuracy or information are
different from engineers or applications.
6. Effect of parasitic on discrete component models is important.
Isolated component models may not show the real.
7. Socket models are also needed for set makers.
8. Crystal and passive oscillator models are required for
system design.
Result of
Discussions between Model Providers and Users (2)

## Slide 14
9. Set makers should detail the conditions of use to components.
10. Models should have the effect of temperature and aging.
11. Models should protect proprietary information.
12. Network description may be only way to improve accuracy.
Result of
Discussions between Model Providers and Users (3)

## Slide 15
1. Interviews IC makers.
2. Interviews more components such as crystal
oscillators.
3. Write reports.
Future activity Plan

## Slide 16
1. Most important issue for users is to get new device models timely.
Any data format (IBIS,IMIC,SPICE,etc) is acceptable.
Just in time in design process
Create distribution channel
2. Efforts must be made to expedite format standardization,
as well as to expand the range of application
from semiconductor devices to non- semiconductor devices.
3. To be supported by EDA tools
CAD and Checking tool of model quality
Easy to use
4. Standardization is required.
Relationship or migration with
IBIS and IMIC, IEC TC93/wg6 Positively.
Conclusion
ーTo Take a Step Forward ー

## Slide 17
Copy from Nikkei BP June14 1999(No745)
Thank you for your attention
We should know well more detail about
IBIS and IMIC and also EMI problems.