## Slide 1: SpiTran: A GUI for S2IBIS2 Mike LaBonte IBIS Summit 21 June 1999

## Slide 2: SpiTran: A GUI for S2IBIS2
Written as a Java application - platform portable
Audits SPICE files
Prepares top level test circuit
Prepares S2IBIS control file
Runs NCSU s2ibis2

## Slide 3: SpiTran Main Window
Click the “New Document” icon.

## Slide 4: Creating a New Project Directory
Enter the name of a new directory and click “Create”.

## Slide 5: Import a SPICE File To the Project
The selected SPICE file is copied into the project directory. Required process library files may be added here. Click “OK”.

## Slide 6: SPICE File Audit
The SPICE file is audited for elements that look like a built-in test fixture. Click “Edit Spice” to remove them, and then “Reparse”.

## Slide 7: Contents of iobuff.sp
...
.SUBCKT IO_IN OUT IN VDD VSSD1 IN VDD DD2 VSS IN DR1 IN 1 10
M1 OUT 1 VDD VDD pm L = 5U W = 120.00U
M2 OUT 1 VSS VSS nm L = 5U W = 50.00U .ENDS IO_IN
.SUBCKT IO_TEST_LOAD LOAD
R1 LOAD 1 50
V1 1 0 1.8
C1 LOAD 0 10p
.ENDS
XOUT 1 2 3 4 5 IO_OUT
XIN 6 1 4 5 IO_IN
XLOAD 1 IO_TEST_LOAD
VDD 4 0 5
VSS 5 0 0
VDATA 2 0 PULSE(0 5 0 10n 10n 50n)
VENA 3 0 5
RDUM 6 0 1e6
*simulator lang = spectre
model pm mos0 type=p
model nm mos0 type=n
model d diode
simulator lang = spice
The main circuit is a test fixture and must be commented out.

## Slide 8: Passes Audit without Warnings
The fixed-up file now passes the audit cleanly. Click “Continue”.

## Slide 9: Main Window Shows Available Subckts
Three subckt definitions are found in the SPICE file. Select “IO_OUT” and “IO_IN”, and click “Instantiate”.

## Slide 10: Instantiated Subckts
The instantiated subckts appear in the lower section. Change the node names to establish the test circuit netlist.

## Slide 11: Node names set
Click “Configure Nets”.

## Slide 12: Telling S2IBIS How Each Node is Used
Establish how each external node is to be used by s2ibis. The pin type of each node is set.

## Slide 13: Nodes Configured
The “rcvrout” node is unused by s2ibis, so it must be “floated” with a terminating resistor. Click “OK”.

## Slide 14: Prepare the S2IBIS Control File
Choose the “Options” item from the “Translate” menu.

## Slide 15: Node Options
Set the nodes to be used for power, ground, enable, etc.

## Slide 16: Mode Options
Choose the simulator to be used, and other s2ibis options.

## Slide 17: Voltage Options
Set voltages.

## Slide 18: Temperature Options
Set temperatures.

## Slide 19: Stimulus Options
Set simulation duration and input stimulus times and voltages.

## Slide 20: Model Options
Set logic thresholds and C_COMP.

## Slide 21: Buffer Delay Options
Set Vmeas and test fixture values.

## Slide 22: VT Options
Set test fixture values for 1st waveform set.

## Slide 23: VT Options for 2nd Waveform Set
Set test fixture values for 2nd waveform set.

## Slide 24: Ramp Load Options
Set load resistance for ramp time simulation.

## Slide 25: Post-Processing Options
Set derating values for optional curve post-processing.

## Slide 26: Running S2IBIS
Choose the “Execute” item from the “Translate” menu.

## Slide 27: S2IBIS Messages

## Slide 28: IBIS Model File in Project Directory