## Slide 1: Thoughts on equations in IBIS models
®
P
L
A
T
F
O
R
M
D
I
V
S
I
O
N
I
C
O
M
P
O
N
E
N
T
S
Arpad Muranyi
Intel Corporation
arpad.muranyi@intel.com
IBIS face to face summit
at DAC 1999
Hilton Hotel
New Orleans, Louisiana
June 21, 1999
Notes: 1

## Slide 2
Outline
Model types and their characteristics (background)
Pros and cons about the use of equations
IBIS accuracy needs
New ideas

## Slide 3
The essence of various model types
SPICE (transistor) model
  voltage/current/capacitance relationships of device nodes are calculated with detailed equations using device geometry, and properties of materials
  measured data is curve fitted to equations
Table driven transistor model
  voltage/current/capacitance relationships of device nodes are based on I/C/V lookup tables
  data tables are generated from full SPICE model simulations and/or die level measurements
  data may be curve fitted to equations for more efficiency and flexibility
IBIS (or behavioral) model
  current/voltage/time relationships of entire buffer are based on lookup tables (I/V and V/t curves)
  data tables are generated from full SPICE model simulations and/or external measurements
  data may be curve fitted to equations for more efficiency and flexibility

## Slide 4
Model characteristics
SPICE (transistor) model
  simulates very slowly, because voltage/current relationships are calculated from lower level data
  each device in the buffer modeled/simulated individually
  best for circuit designers
  too slow for system level interconnect design
  reveals process and circuit Intellectual Property
Table driven transistor model
  simulates faster, because voltage/current relationships are given directly
  each device in the buffer modeled individually
  more suitable for system level design
  hides process, but still reveals circuit Intellectual Property
IBIS (or behavioral) model
  simulates fastest, because voltage/current/time relationships are given only for the external nodes of the entire buffer
  no circuit detail involved
  useless for circuit designers
  ideal for system level interconnect design
  hides both process and circuit intellectual property

## Slide 5
The reason for speed differences
SPICE models are not slower because they are based on equations
  SPICE models are based on lower level information, such as physical dimensions, properties of material, etc.
Table driven models are not faster because they are table driven
  table driven models are usually faster, but only because they use a higher level device description
  lookup tables require a lot of conditional equation evaluation
  processing time depends on the length of the data tables
  multi-dimensional tables tend to get huge and difficult to handle
  expressions could make the information more efficient
  expressions could make behavioral modeling more general
  (no new syntax would be required for each new behavior)

## Slide 6
Behavioral vs. transistor model
Equations or data tables are not what makes one model transistor level and the other behavioral
  SPICE models could be re-written to be table driven from raw measurement data (don’t even think of it!)
  table driven models could be re-written to use curve fitted equations instead (may be a good thing to consider)
The real difference is in the level of abstraction
  molecular/atomic description of materials (crystal structure)
  electron behavior in crystal structure (mobility, etc.)
  geometric device description (width, length, thickness)
  properties of materials (doping, resistance, etc.)
  current/capacitance/voltage relationships on a device level
  current/capacitance/voltage/time relationships on a buffer level
All models are “behavioral”!

## Slide 7
Choosing the appropriate model type
Atomic level
  best for manufacturing process developers
  too much detail for everyone else
Transistor level (SPICE)
  best for circuit designers
  too much detail for system designers
Transistor level (table driven)
  may work for circuit designers, but
  better for system designers
IBIS model
  best for system designers
  not detailed enough for everyone else

## Slide 8
Benefits of using equations
Equations are more compact
  for example, y=ax2+bx+c describes a curve for x=- to x=
  but describing the same curve with a data table would require a large number of points
  defining a surface (2D), volume (3D) or multidimensional problems becomes impossible with data tables
Equations are more flexible and general
  keywords require certain assumptions
  a new buffer behavior requires new assumptions and keywords
  an expression evaluator could take any equation that describes any behavior
Equations may be faster than lookup tables
  if-then-else operations take longer time with larger data tables
Equations allow easy scalability
  typ., min., max. I-V curves could be scaled versions as a function of temperature and/or voltage
  Vinh, Vinl, C_comp, etc. could be expressed as a function of supply voltage, frequency, etc.

## Slide 9
Problems with equations
Extra burden on model developer
  generate data
  come up with an equation that works
  generate coefficients for the equations through curve fitting
With equation based models simulator tools would do less thinking at the expense of the model maker
Should simulator tools eventually pick up model making also?

## Slide 10
How could we start using EQs in IBIS?
Address immediate needs by developing equation equivalents / extensions for existing keywords
  Vinh, Vinl as a function of supply voltage
  C_comp as a function of I/O pad voltage (frequency?)
  scaled versions of various parameters and/or I-V and V-t curves for typ., min., max.
  curve fitted versions of data tables for I-V and V-t curves
  etc.
Develop new features and/or techniques for long-term improvement
  quick fixes must be well though out so that consistency could be maintained when developing long term solutions

## Slide 11
Accuracy problems - long term ideas
Proper accounting for currents is becoming an important issue
  a must for precise GND and Vcc bounce simulations
  a must for proper transmission line return current and discontinuity simulations
The connection of C_comp is too simplistic
  pad to GND, pad to Vcc, and pad to predriver(s) capacitance are currently lumped into one C_comp
GND
pull-
up
I-V
enable
I/O
pin
threshold
&
3-state
control
Vcc
input
Ramp
up
(or V-t)
package
C_comp
POWER
clamp
I-V
Ramp
down
(or V-t)
pull-down
I-V
GND
clamp
I-V

## Slide 12
The location of C_comp is important
C_comp influences the amount of GND and Vcc bounce
  the distribution of total die capacitance between Vcc and GND pins reduces the amount of current in the individual pins due to division
C_comp also acts as a decoupling capacitor
  the series combination of Cds of the poullup and pulldown transistors forms a decoupling capacitor between Vcc and GND

## Slide 13
Bleed through effect
The bump preceding the falling edge is a capacitive coupling of the gate voltage to the output pad
  if this V-t curve is used as a scaling coefficient to the pulldown I-V curve, the coefficient will go negative during for the duration of the bump (to push up)
  in reality, the current for the gate to pad capacitor comes from the supply rail (for the falling edge and for an inverting transistor)
  if the predriver is connected to a different supply rail, this current may bounce another power pin
Ibump
Iedge

## Slide 14
Disclaimer
The following foils discuss some of my ideas
I have no answers to many of the detail questions that the ideas may raise, and I have no definite methodologies worked out regarding their practical implementation
Please take them further with your own thinking or prove them useless

## Slide 15
Modeling with transfer functions
Describe pin-to-pin characteristics as a complex impedance or conductance (or transfer function)
  capacitive and inductive parasitics across driver transistor could also be described this way
  the expression needs to be time varying because of the transitions
  the expression must also be a function of voltage (Vcc to GND, I/O to GND) to account for the non linearities of I-V curves
  multiple expressions are needed for high-to-low, low-to-high (high-to-highZ, low-to-highZ, highZ-to-low, highZ-to-high) transitions and/or the receive (highZ) or terminator (not-so-highZ) mode
The simplest model for a pulldown or pullup stage should be a three-port
  the three ports are Vcc, GND, and the I/O node
  three-ports are necessary to account for the bump current correctly

## Slide 16
Power distribution on the die
The current to a buffer may be supplied by multiple power and GND pins
  power and GND interconnects (rails) on the die must be described more accurately to be able to account for on die supply bounce properly
  how do we know from which pin does the current really come from?
  the return path of the current may vary, but we need to know what it is to find out whether the chip/system works

## Slide 17
Model a component as a matrix
Analogy: transmission line matrix
  relationship between any input and any output node is characterized
Describe pin-to-pin relationships of a component similarly, in the form of a matrix
  inputs = power and GND pins (or pads)
  output(s) = I/O pins (or pads)
  define the (time varying, voltage dependent) transfer characteristics between an I/O pin (or pad) and all power and GND pins (or pads)
  power rail characteristics will become available this way
  this would show how current is delivered to an I/O pin (or pad) from multiple power and GND pins (or pads)
  return path of the current would be known more accurately